## Slide 1: The Ergonomics of Production Lines Measurement and Interventions from the Factory to the Office
Brian Peacock
SIM University
National University of Singapore

## Slide 2: Some Interesting Articles by Dr Chen
"A Fuzzy Sets Modeling Approach for Ergonomic Workload Stress Analysis", International Journal of Industrial Ergonomics (1994)
"A Computer Assisted System for Physical Ergonomics Analysis", Computers in Industrial Engineering (1991)
"An Observational Technique for Physical Work Stress Analysis", International Journal of Industrial Ergonomics, No.3 (1989)
"A Database Management System for Ergonomics Information Analysis,“ Trends in Ergonomics/Human Factors V, Elsevier (1988)
"Prototype Expert System for Physical Work Stress Analysis“ Trends in Ergonomics/Human Factors IV (1987)
"EVA Suit Glove Design." Space Tech '85 Conference, Anaheim, California (1985)
"An Interactive Biomechanical Lifting Model,“ Mid Central Human Factors/Ergonomics Conference, West Lafayette, Indiana (1985)

## Slide 3
Ergonomics = Human Factors
Most of the World
USA
HFE

## Slide 4: The History of Ergonomics
Tools

## Slide 5: Ergonomics = Human Factors
What – The analysis and design of……..
Why – For the purpose of…….
With – Due regard to ……….
Where – In the context of…….
How – With a bag of tools
When – Before, during and after
Who – People with Knowledge, Skills and Tools

## Slide 6: Ergonomics = Human Factors
What – The analysis and design of:
  Products, Systems, Processes, Workplaces, Tools, Interfaces etc
Why – For the purpose of:
  Effectiveness, Efficiency, Ease of use, Elegance, Safety, Security, Satisfaction, Sustainability
With – Due regard to:
  Human Characteristics, Capabilities, Limitations, Preferences
Where – In the context of:
  Physical, Social and Operational Environments
How – With a bag of tools
  For Analysis and Design
When – Before, during and after:
  Research, Analysis, Simulation, Design, Evaluation, Investigation
Who – People with Knowledge, Skills and Tools

## Slide 7: Human Factors Engineering / Ergonomics
Analysis
and
Design
with People in Mind

## Slide 8: Ergonomics Complexity
serves many PURPOSES
surrounded by VARIABILITY
swamped by CONTEXT
complicated by INTERACTIONS
contends with SPACE, FORCE and TIME
driven by INFORMATION and AFFECT
deals with BENEFITS, RISKS and TRADEOFFS

## Slide 9: An adaptation of the Edwards “SHEL” model
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E
Complexity

## Slide 10: Human Factors in Technology Integration Perspective Complexity
Interactions
People
Rules and Regulations
Context
Technology
Adapted from Edwards’ SHEL Model

## Slide 11: Product Life Cycle
Requirements
Concept
Development
Concept
Selection
Specifications
Tooling
Production
Marketing
Use and
Misuse
Maintenance
Disposal
Feedback, Technical Memory
Many Customers
(including the shareholders)
Design Team
Many Requirements
Feedforward (Anticipation)

## Slide 12: Big Picture Ergonomics
Force
Space
Time
Connections
Gravity
Posture
Reach
Access
Duration
Frequency
Sequence
Fit
E
P
B

## Slide 13: Many Responsibilities
Force
Space
Time
Product Engineer
Packaging Engineer
Manufacturing Engineer
Industrial Engineer
E
P
B

## Slide 14: Ergonomics also deals with Information and Affect
Force
Space
Time
Information
E
P
B
Affect
Satisfaction

## Slide 15: Human Centered Design
People
Equipment
Workplace
Environment
Time
Variability

## Slide 16: Big Picture Ergonomics Purposes
Effectiveness Quality
Efficiency Productivity
Ease of Use Comfort and Convenience
Emotional Appeal Pleasant job and context
Safety/Health Acute Injuries and Chronic Illnesses
Security Malicious Third Parties
Satisfaction Of ALL concerned
Sustainability Reliability AND Resilience
If you can’t / don’t measure it you can’t manage it
There will be tradeoffs
E4S4
E
P
B

## Slide 17: Multiple Purposes of Design
Effectiveness
  Meets functional requirements
  “quality”
Efficiency
  Optimal use of resources
  “productivity”
Ease of Use
  Intended users
  Comfort and Convenience
  Prevention of misuse
Elegance
  Esthetic / emotional appeal
  Affective Design
Safety and Health
  Prevention or mitigation of system failures
  For participants and third parties
Security
  Inadvertent or malicious misuse
Satisfaction
  Of ALL customers and stakeholders
There WILL be tradeoffs
Sustainability
  Reliability
    Under intended contexts over the life cycle
  Resilience
    Under unintended, unexpected and harsh conditions
E4S4

## Slide 18: The Purposes of Ergonomics
Contributing to the Multiple Purposes of Design
Helping with the tradeoffs
E4S4
Productivity
Safety

## Slide 19: The 6Us and 2Ms of Usability
Utility
  Is the system useful?
Usage and Misusage
  How and in what context will the system be used?
  What possible extreme contexts may be predicted
Usability
  Is the system easy to use or misuse?
Utilization
  How often and by how many people is the system used?
Users and Misusers
  Who are the users and possible misusers?
User Error
  What kinds of error can be made, when and how will they be made, how frequently and what are the possible consequences?
6U
2M

## Slide 20: Complications of Ergonomics
Integration
Interfaces
Interactions
Intraactions Interferences
Interdependencies
Operations
Technology
People
Contexts
Processes
“ ing”
Regulations
Energy
Information
Operational
Physical
Affective
Social
Cognitive
Physical
History
Variability
Sustainability
Satisfaction
Security
Safety
Effectiveness
Elegance
Ease of use
Efficiency
Purposes
Time

## Slide 21: Structures, Processes and Outcomes
People
Can be Selected, Trained and Assigned
Technology
(Hardware and Software)
Can be designed or changed by
“Engineering Controls”
Rules and Regulations
Can be managed or changed by
“Administrative Controls”
Outcomes
E4S4
Must be
monitored
Contexts / Environments
Usually cannot be changed so we must mitigate their effects by engineering or administrative controls
Effectiveness
Efficiency
Ease of Use
Emotional Appeal
Safety
Security
Satisfaction
Sustainability
Processes
Operations
Activities
Tasks
Jobs
Take Time
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E

## Slide 22: When Ergonomics Works RASDEI
Research
Analysis
Design
Evaluation
Outcome Investigation
Simulation
Ergonomics Projects need some or all these Skills
Success
Failure

## Slide 23: Activities of Ergonomists rasdei
Analysis
Design
Usability Testing
Outcome Investigation
Objective Feedback
(Fuzzy) Prediction
Research
External
Forces
Simulation

## Slide 24: Human Factors Applications Need
Domain Knowledge
Measurement and analysis tools
Knowledge of human characteristics, capabilities and limitations

## Slide 25: The Practice of Ergonomics
Breadth– Domain Knowledge
Agriculture, Gas and Oil, Manufacturing, Textiles, Transportation, Consumer Products, Service Industry, Sport and Recreation, Rehabilitation, Aviation, Space Exploration
Process
Depth
Investigation
Evaluation
Design
Simulation
Analysis
Research
Domain
Depth
Get help where it is needed
The
Shaped Profession

## Slide 26: The Ergo Cop Problem
Design
Specifications
Ergonomics
Evaluation
The Ergocop
Design
Performance
Review
(waivers by management)
Performance
Requirements
Performance
Review
Precise
Design
Specifications
Ergonomics
Support
Design
Clear
Performance
Requirements
Time to
Market
Calling the designer’s baby ugly!

## Slide 27: Big Picture Ergonomics
Force
Space
Time
Information
E
P
B
E4S4
Affect
Satisfaction
6U
2M
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E
Requirements
Concept
Development
Concept
Selection
Specifications
Tooling
Production
Marketing
Use and
Misuse
Maintenance
Disposal
Feedback, Technical Memory
Many Customers
(including the shareholders)
Design Team
Many Requirements
Feedforward (Anticipation)
Users
Purposes
Life Cycles
Complexity
Context

## Slide 28: The Broad Scope of Ergonomics
Physical
Sensory
Cognitive
Social
Affective
Environmental
Temporal

## Slide 29: The Broad Scope of Ergonomics
Shape
Size
Strength
Speed
Stamina
Skill
Sensing
Deciding
Learning
Planning
Perceiving
Attending
Communicating
Controlling
Calculating
Understanding
Remembering
Forgetting
Thermal
Heat
Humidity
Cold
Air movement
Acoustic
Communication
Hearing loss
Vibration
Hand / Arm
Whole body
Light and Dark
Vision
Contrast
Color
Customers
Groups
and
Teams
Hierarchies
Cooperation
Communication
Competition
Language
and
Jargon
Roles
Jobs
Supervision
Businesses and Companies
Emotion
Esthetics
Elegance
Attitude
Mood
Motivation
Excitement
Physical
Temporal
Environmental
Social
Cognitive
Affective
Sensory
Vision
Touch
Taste
Proprioception
Smell
Hearing

## Slide 30: Variability
Ergonomics Purpose and Achilles' Heel
Physical
Cognitive
Social
Affective
Context
Temporal
Sensory

## Slide 31: Physical Ergonomics
Shape
Size
Strength
Speed
Stamina
Skill

## Slide 32: People vary in Shape and Size

## Slide 33: People vary in their Strength

## Slide 34: People Vary in their Skills

## Slide 35: People vary in their Speed

## Slide 36: People vary in their Stamina

## Slide 37: Sensory Factors
Vision
Touch
Taste
Proprioception
Smell
Hearing

## Slide 38: What happens when you grow old?

## Slide 39: Are you Colorblind?
1. Normal Color Vision: A: 29, B: 45, C: --, D: 26
2. Red-Green Color-Blind: A: 70, B: --, C: 5, D: --
3. Red Color-blind: A: 70, B: --, C: 5, D: 6
4. Green Color-Blind: A: 70, B: --, C: 5, D: 2

## Slide 40: Cognitive Factors
Sensing
Deciding
Learning
Planning
Perceiving
Attending
Communicating
Controlling
Calculating
Understanding
Remembering
Forgetting

## Slide 41: Cognition is complex
Evaluating
Diagnosing
Judging
Deciding
Planning
Investigating
Predicting
Analyzing
Problem Solving
Cognition
Learning
Interpolating and Extrapolating
Goals
Understanding
Synthesizing

## Slide 42: Cognition
Attending
Perceiving
Understanding
Predicting
Deciding
Remembering
cON
Learning

## Slide 43: People vary in their Cognitive abilities

## Slide 44: Cognition is Complex

## Slide 45: Affective Factors
Emotion
Esthetics
Elegance
Attitude
Mood
Motivation
Excitement

## Slide 46: Environmental Factors
Acoustic
Communication
Hearing loss
Thermal
Heat
Humidity
Cold
Air movement
Vibration
Hand / Arm
Whole body
Light and Dark
Vision
Contrast
Color
Chemical and Biological
Gravitational
Space
Pressure
Under Water
Altitude

## Slide 47: Environmental Design - Lighting
Provide natural lighting
Provide sufficient lighting
Avoid glare
Provide special purpose lighting to emphasize task features

## Slide 48: Environmental Design - Noise
Reduce damaging / distracting / interfering noise
  At source
  By barriers
  By PPE
  By exposure reduction (rotation)
Enable task information, communications and alarms distinct from ambient noise
Allow / provide music if it doesn’t interfere with task or colleagues

## Slide 49: Environmental Design - Heat
Maintain air temperature between 220 C – 260 C
  For sedentary work (cooler for physical work)
  Allow some fluctuation
Maintain relative humidity necessary for process
  generally between 30% – 50%
Enable air movement
  Avoid drafts
Address / control radiant heat / cold sources

## Slide 50: Social Context
Customers
Groups
and
Teams
Hierarchies
Cooperation
Communication
Competition
Language
and
Jargon
Roles
Jobs
Supervision
Businesses and Companies

## Slide 51: Time Factors
Job Cycle Time
History
Task Pacing
Remembering
Acceleration
Velocity
Decision Time
Movement Time
Reaction Time
Psychological Refractoriness
Age
Fatigue
Vigilance
Circadian Rhythms
Mental Workload
Duty Cycle
Shift Length
Timing

## Slide 52: The Broad Scope of Ergonomics
Shape
Size
Strength
Speed
Stamina
Skill
Sensing
Deciding
Learning
Planning
Perceiving
Attending
Communicating
Controlling
Calculating
Understanding
Remembering
Forgetting
Customers
Groups
and
Teams
Hierarchies
Cooperation
Communication
Competition
Language
and
Jargon
Roles
Jobs
Supervision
Businesses and Companies
Emotion
Esthetics
Elegance
Attitude
Mood
Motivation
Excitement
Physical
Temporal
Environmental
Social
Cognitive
Affective
Sensory
Vision
Touch
Taste
Proprioception
Smell
Hearing
Job Cycle Time
History
Task Pacing
Remembering
Acceleration
Velocity
Decision Time
Movement Time
Reaction Time
Psychological Refractoriness
Age
Fatigue
Vigilance
Circadian Rhythms
Mental Workload
Duty Cycle
Shift Length
Timing
Acoustic
Communication
Hearing loss
Thermal
Heat
Humidity
Cold
Air movement
Vibration
Hand / Arm
Whole body
Light and Dark
Vision
Contrast
Color
Chemical and Biological
Gravitational
Space
Pressure
Under Water
Altitude

## Slide 53: The Process of Ergonomics
$
Decisions
Outcomes
Design
What can be changed
Measurement and Analysis
Contexts
(Difficult or Impossible to Change)
The Job

## Slide 54: The Process of Ergonomics
$
Decisions
Benefits, Costs,
Risks, Tradeoffs
Measurement and Analysis
Screening
In depth Research
Contexts
Spatial, Physical, Mechanical, Chemical, Biological, Geographical, Social, Political, Economic
Design
Tools, Equipment, Workplaces, Tasks, Procedures, Assignments.
The Job
Outcomes
Quality
Productivity
Health, Safety
Ease of Use
Security
Satisfaction
Sustainability

## Slide 55: How Ergonomics Works with a box of tools
General Tools
  E4S4
  6U2M
  SHEL
  HFACS
  CRM
  ICF, etc.
Workplace tools
  Checklists
  RULA / REBA
  HAL
  PWSI
  NLE, etc.

## Slide 56: Workplace Ergonomics

## Slide 57: Workplace Ergonomics
Space - layout, furniture, postures
Force - materials handling, strength, postures
Time – productivity, fatigue, shiftwork
Information – training, quality
Affect – motivation, behaviors
Context – physical and organizational

## Slide 58: Workplaces

## Slide 59: Postures and Environments

## Slide 60: Physical Workloads

## Slide 61: Awkward Postures

## Slide 62: Bicycle Assembly

## Slide 63: Workplaces and Postures

## Slide 64: Assembly Work

## Slide 65: The Office

## Slide 66: The Typing Pool

## Slide 67: Call Centers in the Phillipines

## Slide 68: Assembly Operations

## Slide 69: Mobile

## Slide 70: The History of Assembly Lines

## Slide 71: I love Lucy, Chocolate wrapping line.
http://www.google.com/url?sa=t&rct=j&q=lucy%20chocolate%20factory&source=web&cd=2&cad=rja&ved=0CCkQtwIwAQ&url=http%3A%2F%2Fwww.youtube.com%2Fwatch%3Fv%3DFGfplQ1FUFs&ei=_eJWULi3IYHNrQf28oCYBw&usg=AFQjCNHkkfIbZobjKqrGwXuspX-A1XPfVQ
http://lloyddeleon.multiply.com/video/item/4/I_Love_Lucy_--_at_chocolate_factory
https://www.youtube.com/watch?v=8NPzLBSBzPI

## Slide 72: Henry Ford – Work Simplification

## Slide 73: Bring the Work to the Worker

## Slide 74: Frederick Winslow Taylor - “Taylorism”
Scientific Management
Managers Manage, Workers Work
Prescriptive work methods

## Slide 75: Lillian and Frank Gilbreth
Time, Motion and Fatigue Studies
Micro motion – “Therbligs”

## Slide 76: Therbligs
Reach
Grasp
Move
Hold
Release
Use
Pre-position
Position
Assemble
Disassemble
Search
Select
Plan
Inspect
Unavoidable Delay
Avoidable delay
Rest

## Slide 77: Hawthorne Studies
Employees motivated by the attention given to them rather than impersonal change in working conditions (lighting)

## Slide 78: Tavistock Institute
Coal Mining
Human Centered Design

## Slide 79: MTM
Methods-Time Measurement is a procedure for improving methods and establishing time standards by recognizing, classifying, and describing the motions used or required to perform a given operation and assigning pre-determined time standards to these motions.
The foundation of modern Work Measurement and Industrial Engineering

## Slide 80: Standard Times (measured in seconds)

## Slide 81: Lots of Components
Lots of savings by removing none value added activities

## Slide 82: Sewing

## Slide 83: Meat Packing

## Slide 84: Boeing Assembly Line

## Slide 85: Electronics

## Slide 86: Foxconn

## Slide 87: Production lines brought enormous improvement in Productivity by the removal of Non Value added work and the improvement of Process consistency / Quality But at what cost?

## Slide 88: Measurement Industrial Engineering

## Slide 89: Work Measurement
Puropses
  Productivity
  Quality
Micro motion analysis
Remove non value added activities
  Searches, decisions, movements, (checks)
Work simplification
  Reduce the job cycle
  Shortens learning time
  Improves Productivity and Quality?

## Slide 90: Industrial Engineering The Job Cycle
Transport
Grasp
Attach
Inspect
Return
Time

## Slide 91: Overhead Work

## Slide 92: Postures

## Slide 93: Vehicle Height

## Slide 94: Sewing Factory Hand and Finger postures

## Slide 95: Assembly Lines

## Slide 96: The Job Cycle (varies between a few seconds, a few minutes and even a few hours)
Check
Position
Cycle Time
Force
*
Posture
Transport
Grasp
Reach
Attach
Return / Rest

## Slide 97: The Industrial Engineering Solution Cut off the peaks of Force and Posture, Reduce Non value Added work and Fill up the Job Cycle
Check
Position
Cycle Time
Force
*
Posture
Transport
Grasp
Reach
Attach
Return / Rest

## Slide 98: Tool balancers

## Slide 99: Doors Off

## Slide 100: Skillets

## Slide 101: Skillets – Work height adjustment

## Slide 102: Tilt the Task

## Slide 103: The Results Improved Productivity But increased Static Work
Cycle Time
Force
*
Posture
Transport
Grasp
Attach
Grasp
Attach
Transport
Transport
Grasp
Attach
Line Balance

## Slide 104: The $64,000 Question?
Does (pseudo) Ergonomics cause Illness and Injury?
“Ergonomic / Iatrogenic Disease”
Long durations, low forces, near neutral postures, high repetitions

## Slide 105: The CTD Epidemic Repetitive motion strain Occupational overuse syndrome
Meatpacking
Nursing homes
Automobile manufacturing
Parcel handling
Electronics manufacturing
Textiles
Food processing
Textiles
Checkout counters
etc
Years of Contentious / Combative dialog among Government (NIOSH / OSHA)
Business (NAM, COT), and Unions (UAW)
providing many opportunities for Ergonomics Researchers, Professionals, Practitioners and Product developers

## Slide 106: Upper Limbs and Backs

## Slide 107: Sedentary Work leads to metabolic disorders – obestity, circulatory disease, diabetes
Ergonomic
X

## Slide 108: Production with Protection Optimization among the multiple purposes and responsibilities of organizations
Suggested Policies Regarding Ergonomics
“Production with Protection”
Brian Peacock
GM Manufacturing Ergonomics Laboratory
December 8, 1995
E4S4

## Slide 109: Sedentary, Static and Repetitive Work lead to:
Repetitive Strain Injury
  Musculo skeletal disorders
Metabolic disorders
  Obesity, circulatory disorders, diabetes
Cognitive dullness
  Lack of flexibility
Job dissatisfaction
  Absenteeism
  Industrial unrest
Operational deterioration
  Productivity, quality

## Slide 110: Intervention Opportunities
Engineering Interventions
  Robotics
  Mechanical assists to reduce
    Force
    Extreme Postures
Administrative Interventions
  Time
    Job Enlargement
    Job Rotation
    Decoupled assembly lines
    Work Cells
    Vertical Job Enlargement
    Work Teams
    Participation
Time

## Slide 111: Task Aids

## Slide 112: Robots

## Slide 113: Robots

## Slide 114: Administrative Interventions
Time

## Slide 115: The Rest Pause Question
Are frequent short breaks “better than” less frequent long breaks?
The “Psycho-Social” Answer - No
  People invariably “work ahead” to increase “discretionary time”
The Physiological Answer – Maybe
Rest pauses need managing

## Slide 116: Administrative Interventions Job Design
Job Enlargement
Job Rotation
Decoupled assembly lines
Work Cells
Vertical job enlargement
Team structures
Participation
“Andon Chords”

## Slide 117: Decoupling
Separate cells by buffers so that teams are self rather than line paced
Allows for flexible response to variable conditions
Allows work to continue if there is a problem up or down the line

## Slide 118: The Job Cycle
Check
Position
Cycle Time
Force
*
Posture
Transport
Reach
Attach
Return / Rest
Grasp

## Slide 119: Horizontal Enlargement Increase the cycle time, put more (different) functions into the job cycle
Increased Cycle Time
(Load up to 90%)
Varied Force and Posture

## Slide 120: Horizontal Job Enlargement
Increase the duration of the work cycle and the number of job cycle elements
  Is of minimal (physical) value if all the elements are physically similar
    May increase static workload
  Will need greater training effort to achieve acceptable productivity and quality standards
    Will cause staffing problems with large labor turnover
May create greater understanding of the product, subassembly and quality, allows productivity shortcuts by parallel manual / cognitive work element overlap
Will be of significant physical value if the job elements are (physically) dissimilar
  May lead to excessive dynamic work load

## Slide 121: Horizontal Job Enlargement Examples
NUMMI
  Joint Venture between GM – Toyota
  Selected work force
  Team structure
  Participation
  5 minute job cycle
Lansing Craft Center
  Very long cycles
  Non valued added components handling

## Slide 122: Job Rotation
Task
1
Task
2
Task
3
Rotate every ½ , 1, 2 hours or on different days or even weeks

## Slide 123: Job Rotation
Work on one set of task elements then rotate onto another set
  Is of minimal (physical) value if all the elements are physically similar
    May increase static workload
  Will need greater training effort to achieve acceptable productivity and quality standards
    Will cause staffing problems with large labor turnover
May create greater understanding of the product or subassembly
Will be of significant physical value if the job elements are (physically) dissimilar

## Slide 124: The Hidden Advantages of Horizontal Job Enlargement and Rotation
Adds more knowledge and skills to the individual worker
Creates greater flexibility in job assignment
Resolves line balance problems due to absenteeism
Creates greater understanding of manufacturing quality issues

## Slide 125: Pay for Knowledge CAMI – Joint GM – Suzuki venture
Add incremental rewards to operators who learn more skills
When a operator learns all the operations in his / her work group he / she can be promoted to the role of utility worker – can fill in for absent operator without line disruption

## Slide 126: “Line Unbalance” Strategy in Mexican components plants due to high employee turnover
With large turnover training problems increase
Assign fewer work elements to new workers
Increase gradually to full “experienced worker standard”
Time
Fixed Job Cycle length
Experienced Worker Standard
New Employee
Operations

## Slide 127: Work Cells
The traditional assembly line can be inefficient, inflexible and uncomfortable
Group tasks in work cells
  5 to 8 operators
Allow personalization of work area
  Team identity, spirit
Reduce between operation transfers by equipment layout
  Non value added time
Use batch transfer between cells
Provide (controlled)buffers
  Allows flexibility

## Slide 128: Work Cell Schematic

## Slide 129: Kitting
Typically components are presented in separate batches
“Kitting” groups sets of components to support a particular assembly sequence
Reduces non value added part selection and transfer time
Supports work cell and task enlargement arrangements
Requires up front kitting function perhaps at the component plant

## Slide 130: Vertical Job Enlargement
Vertical job enlargement adds managerial responsibilities to an individual’s operational responsibilities
  Quality, Productivity, Health and Safety responsibilities
Both operational and motivational improvements
Removes one layer of supervision
Utility workers fill in
Team members manage different support responsibilities

## Slide 131: Self Directed Work Teams
A natural progression of Administrative Controls such as rotation and enlargement is the creation of self directed work teams.
Self directed work teams can arrange assignments, rotations enlergements etc
They are also collectively responsible for quality, productivity, health, safety and satisfaction
Create “ownership” of total product
They also remove the need for first line supervisors
They will prevent the formation of bottom up informal “complaints” groups

## Slide 132: Saturn
Green field plant
Substantial but not complete autonomy
New product
Collaborative union – management arrangement
Self Directed Team structure
Job rotation
Ownership
Poor (one week rotation) shift system

## Slide 133: The Saturn Plant
Created in the 1980s with a greenfield plant, a brand new different product and a collaborative, participating union
Adopted self directed work teams
Used job rotation
Vertical enlargement – all the way up to the shared plant managers office
The process failed in the late 1990s due to poor product performance (design and engineering causes) and infiltration by the national Union with its traditional combative approach.

## Slide 134: The Politics of Self Directed Work Teams
In the Toyota Production System “Self Directed Work Teams” are created by management
The team members are motivated to improve quality and productivity, with the constraint of health, safety and satisfaction
Without the teams, disgruntled groups form (hierarchical) unions, whose motivations may not gel with those of management

## Slide 135: The “Job Enrichment” Myth
It is possible to intervene with engineering and administrative devices but “enrichment” is an emotional characteristic of the individual employee – some may prefer simple repetitive jobs others may be more ambitious, but if there are incentives associated with the change then administrative interventions may be “enriching”

## Slide 136: Participation
Participation – “Vertical Job Enlargement” works
The people doing the job have the best knowledge of the causes of poor quality, productivity and health and safety.
Install ANDON Chord procedure
  Anyone can stop the line any time
This knowledge should be captured by the company and used to make improvements.

## Slide 137: Quality Management

## Slide 138: The Quality “Control” Myth
Measuring quality is like shutting the barn door after the horse has bolted
Quality is determined by PROCESS
If the PROCESS is managed then Quality will follow.
But it is still important to measure quality to observe trends
Quality charts should be used as described by Deming
  Do not interfere with “Common Causes”
  Only react to “Special Causes”
The Production Team usually has the knowledge to manage the PROCESS
PRODUCT QUALITY = COMPONENT QUALITY + PROCESS QUALITY

## Slide 139: The Toyota Production System W Edwards Deming Outcome measurement Statistical Quality Control The honest worker Prescriptive operations Simple TOOLs

## Slide 140: 5S, 5Why etc.

## Slide 141: Visual Controls Plot Quality, Productivity, Health and Safety measurements over appropriate time scales Post the charts in the work area
Use Statistical Quality Control Methods

## Slide 142: Special and Common Causes
Do not TAMPER with common causes

## Slide 143: Use “Loss Functions” rather than “Tolerances”
Tolerances
Target Specification
Loss Function
The principle of Continuous Improvement:
Kaizen Engineering
Target Dimension
“Good Enough”

## Slide 144: Socio Technical Systems Macro Ergonomics Big Picture Ergonomics
E
P
B

## Slide 145: Maslow Hierarchy of Human needs
People are motivated first by the need to survive, then by peer esteem and finally by personal fulfillment
Money isn’t everything
Maslow, A.H. (1943). "A Theory of Human Motivation," Psychological Review 50(4): 370-96

## Slide 147: Frederick Herzberg Intrinsic motivation and Hygiene (dissatisfiers) factors Job Enrichment
Herzberg, F. 1968, "One more time: how do you motivate employees?", Harvard Business Review, vol. 46, iss. 1, pp. 53–62

## Slide 148: MacroErgonomics Hendrick 1990s Socio Technical Systems revisited Big Picture Ergonomics with micro ergonomics details
E
P
B

## Slide 149: Toyota Production System
Principles
Eliminate waste
Visual controls
Standard processes
Quality circles(participation)
Kaizen - Continuous improvement
Simple Tools
5S – Tidy workplaces
Ishikawa Charts (6M)
5 Whys
Statistical process control
Lean
Agile
Participation
Quality Circles
Quality
Productivity

## Slide 150: Case Study: Job Redesign in the Bindery
Hong Kong university library
Hard covers on journals and books
10 people
Continuous work flow
  Batches within stages
The problems
  Access to library material, work in progress
  Equipment bottlenecks
  Physical environment
  Social context
  Productivity and job satisfaction

## Slide 151: The Binding Process
Receiving and planning
  Full binding – new cover
  Original cover - laminated, flush (no rounding) and perfect binding (no sewing)
Sewing
  Removing old covers, sewing sets of pages
Forwarding
  Cutting cards and cloth, making covers
Lettering
  Highly skilled, top job
Casing in
  Final assembly
Checking and documentation

## Slide 152: Materials Management
2 weeks after delivery journals sent to bindery
Documentation by accessions department
Stored on trolleys (60 volumes) – congestion
6 months work in progress
Access to work in process and binding priority based on level of influence

## Slide 153: The Bindery and the Binders
The bindery
  Congested, raw materials and journals / books
  Bottlenecks, equipment shortages (presses)
  Layout not functional
  Noise and radiant heat
The binders
  1 senior, 4 binders, 5 assistants all at least 5 years
  Blue collar job in white collar environment
  Job security, no turnover, low status
  Narrow job assignments based on seniority
Many complaints

## Slide 154: The Objectives
Make readable material accessible
Reduce work in progress
Improve productivity
  Reduce backlog
Improve morale and job satisfaction of the book binders

## Slide 155: The Changes
Redesign storage of periodicals waiting to be bound
Introduce cardex system for production control
Introduce small batch system with semi autonomous teams
Introduce job rotation and enlargement
Purchase new equipment, window blinds, task lighting, sound isolation
Rearrange the layout for functional flow
Review salary structure
Use some subcontracting for less skillful work
Protect the boss from the customers

## Slide 156: The Results (2 year follow up)
Better production control and accounting
Increased productivity
Removal of the backlog
Improved physical environment
Much happier customers
  Interface between the team and the customers
Improved job satisfaction
  Hawthorne effect?

## Slide 157: Case Study Organization and Job Design in Medicare Data Processing
200, mostly female clerical workers
High specialization
Open plan, functional zones, cubicles, noisy, untidy
Inefficiencies, backlogs, errors
New computer system
Low morale, threatened with takeover by subcontractor

## Slide 158: The Separate Functions
Receiving claims
Checking with suppliers and patients
Data input (classroom style)
Checking data
Special investigations
Disbursements

## Slide 159: The Organizational Problems
Repetitive specialized work, electronic performance monitoring
System breakdowns
Noise, housekeeping – piles of paper
Low productivity, high costs
Low morale, conflict

## Slide 160: Solutions
Discussions of job enlargement with management
Introduction of pilot team”
  Selection of 6 volunteers, with broad background
  Team to take full batch through the whole process, except disbursements
Team responsible for layout of own department and allocation of duties
Carpeted the whole floor and isolated noisy printers
Talked to all the groups

## Slide 161: Results
Acceleration phase
  Physical layout and equipment installation
  Some learning and cross training
Productivity way up, errors down
High team morale
  Envy from the rest of the organization
Everybody liked the new carpet
Organization taken over by subcontractor

## Slide 162: Micro Ergonomics and Design
Workplace Design
  Access, Fit, Reach, Postures
Manual Materials Handling
  Lifting, Holding, Carrying, Pulling, Pushing
Manipulation
  Assembly work
Information Design
  Controls, Displays, Tools
Environment Design
  Light, Heat, Noise
Operations Design
  Tasks, Variety
Job Design
  Control, Breaks, Shifts, Supervision, Teams
Macro
+
Micro

## Slide 163: Workplace Design What can be Changed?
Space
  Reach, fit, postures, support
Force
  Moments and levers
  Pressure points
  Interfaces
  Mechanical assists
Time
  Static – dynamic balance
  Work rest schedules
  Shift work

## Slide 164: Workplace Design
Measurement
Design
Anthropometry
Postural analysis
  The Box and the Ball
Movement analysis
  Ranges
  Macro motion analysis
  Micro motion analysis
Adjustability and flexibility
  Seat and task heights
    Lower limb, trunk and neck, arm posture
  Orientations
    Neck, arm and hand postures
  Allow variable postures
    Stand, sit , lean
  Provide support for stability
    Body weight, back, arms, feet

## Slide 165: You can only change posture by changing the workPlace Layout but even then behaviors will differ

## Slide 166: Sitting Posture by Google

## Slide 167: The Box
Shoulder height of the 5th percentile female
Knuckle height of the 95th percentile male
Forward functional reach of the 5th percentile female
Elbow width

## Slide 168: The box can be very simple to remember
30/75(20/50 for sitting)
50/125
(40/100 for sitting)
25/65
25/65
It is very useful for many practical purposes

## Slide 169: More on “the box”
It deals with back, leg and arm posture
It is in the design domain - it does not measure posture
It’s zones are
  Hand(s) inside the box
  At the edge of the box
  Outside the box
  Outside the box in two dimensions
You can add time to the discussion
  5 secs, 10 secs, 50% of job cycle etc
The corners may be an issue - so round them! – The Ball
The box moves to the sitting base posture

## Slide 170: Storage Rack Guidelines (North America)

## Slide 171: Racks
10
20
30
40
50
60
70

## Slide 172: The Box or the Ball Work (hand) placement for most of the time
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
Sitting
High Sitting
Leaning
Standing

## Slide 173: Visual, Light and Heavy Work
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
+ / - 20 cm

## Slide 174: Adjustability and Flexibility
Where possible make workplaces adjustable to individual preference and allow / encourage change

## Slide 175: How to find (approximate) percentile values
Stand group (10) in a row, tallest at one end shortest at the other
Measure dimensions from 2nd, 5th and 8th person
  or 1st, (5th + 6th) /2 and 9th
  Round the numbers
More people more accuracy
Or use anthropometric tables or Drillis and Contini proportional approach

## Slide 176: Manual Materials Handling

## Slide 177: Manual Materials Handling
Major cause of back injuries
Measurement
  RULA
  NIOSH Lift Equation – Lifting
  Snook Tables – Pushing, Pulling
Change the task?
  Automation
  Mechanical assists
  Change the elements
    Load, Location, Frequency, Duration
Change the method?
  Lifting training

## Slide 178: Low Back Strain
The most common disorder worldwide
  80% population have LBDs at some time
Multiple sites
  Complex anatomy
    Facet joints, intervertebral discs
    Muscles, tendons, ligaments, fascia
      Irritation, inflammation
      Exacerbation of acute strain
    Nerve involvement
      Root compression
      Referred pain
Difficult precise diagnosis

## Slide 179: Low Back Disorders
Common causes
  Repeated bending and twisting in outer range of joint movement (flexion, side flexion, rotation)
  Heavy loads
  Large moments
  Rapid / jerky movements
  Long duration sitting
  Note that individual spinal joint motions are controlled by facet joint orientation

## Slide 180: Sciatica
pain radiating down one or both buttocks/legs along the path of innervation of the sciatic nerve
compression at nerve root in spinal canal or in intervertebral canal

## Slide 181: Diagnosis
Difficult
Range of motion
  Passive, active, resisted
    Localized pain
    Referred pain
      Parasthesia
      Sciatica
Postural abnormalities
  Scoliosis
  Unequal weight bearing
Tenderness, spasm
Muscle atrophy
Gait abnormalities
Bilateral tendon reflexes (achilles, patellar)
Muscle strength

## Slide 182: Treatment of Back Disorders
Bed rest if severe
Ice in acute phase then heat
Gentle ROM exercises
  Passive, active, minimal resistance
Anti inflammatory medication, analgesics, muscle relaxants
Surgery????

## Slide 183: Lifting
Don’t put things on the floor!!
  Put them in the “Box” or “Ball”
Face the object
Move as close as possible to the object CG
Bend hips and knees
Keep back straight
Get a good grip
Don’t twist or jerk, lift smoothly

## Slide 184: MMH Measurement
NIOSH Lift Equation
Liberty Mutual (Snook) Tables

## Slide 185: NIOSH Lift Equation

## Slide 186: Should not be used for:
One handed lifts
More than 8 hours
Seated or kneeling
Restricted work space
Unstable Objects
Carrying, pushing or pulling while lifting
Wheelbarrows or shovels
High speed motion
Unreasonable foot/floor coupling
Unfavorable environment

## Slide 187
1991 Version
RWL = LC x HM x VM x DM x AM x FM x CM
A Discounting Equation
Lift Index = LOAD / RWL

## Slide 188
Definition of Terms
RWL = Recommended weight limit
LC = Load constant
HM = Horizontal multiplier
VM = Vertical multiplier
DM = Distance multiplier
AM = Asymmetric multiplier
FM = Frequency multiplier
CM = Coupling multiplier

## Slide 189: 1991 Multipliers
LC = 51 Pounds Load Constant
HM = 10/H Horizontal Distance
VM = 1-.0075 x / V-30/ I Vertical Distance – 30”I
DM = .82 + (1.8/D) Vertical Distance moved
AM = 1 – (.0032 x A) Asymmetry

## Slide 190: Frequency Multiplier

## Slide 191: Coupling Multiplier

## Slide 192: Asymmetry Multiplier

## Slide 193
NIOSH Worksheet

## Slide 194: Snook Tables

## Slide 195: Sources on the Internet
http://www.cdc.gov/niosh/docs/94-110/
http://www.emcins.com/losscontrol/quick_links/employee_safety_health/ergonomicsNIOSH.aspx
http://www.ergoweb.com/news/detail.cfm?id=566
http://www.ccohs.ca/oshanswers/ergonomics/niosh/calculating_rwl.html

## Slide 196: Manipulation

## Slide 197: Manipulation / Assembly Tasks
Task requirements
  Visual, cognitive and motor
  Repetition
Outcomes
  Product quality and productivity issues due to
  Hand and arm pathology
  Postural strain – shoulder, neck
  Motion strain – shoulder, elbow, wrist, hand, thumb and fingers
Causes (and opportunities for intervention)
  Force, posture, movement, frequency, duration
Measurement
  Hand Activity Level
  Postural analysis
  Micro motion analysis
Interventions
  Remove, reduce or replace non value added work
  Task / Target Design
  Enlarge or rotate to reduce frequency

## Slide 198: Grasping and Manipulating
Fingers have postures too
How big are your hands?
How big should handles be?
How bent should handles be?
Length, Width, Circumference, Shape
Avoid pressure points

## Slide 199: Tight Targets Take Time
Tight Targets Take Time

## Slide 200: Two Automobile Plants
Part Insertion Time
  6.3 secs
  3.9 secs
Target size, orientation ?

## Slide 201: Standard Times for Targets (hundredths of a minute)
Normal Place .03
Small Target .05
Blind Target .07
Enter Vehicle .08
Exit Vehicle .05
Lean into + Arise .05

## Slide 202: If You Don’t Resolve Ergonomics Problems During Product Design
Added Operators
  $75,000 / year x 2 shifts x 6 years product cycle
  $900,000 per added operator
Added Tools
  0.07 min / tool x $0.75 / min x 2 shifts x 75 jph
  x 8 hours per day x 243 days per year x 6 years
  $92,466 per tool

## Slide 203
Four Stages of Movement Exercise
(Place a coin then move the next one on top)
1
Primary, Ballistic
Aiming Movement
Finesse
(Tactile)
Final Adjustment
Move hand to
Task Vicinity
Place one coin squarely on the top of another
2
Pick up Coin

## Slide 204: Four Stages of Movement
1
Move to task vicinity
2
Primary ballistic aiming movement
3
Final adjustment
4
Finesse (Tactile)

## Slide 205: Targets and Triangles
A
B
Design for Assembly!
Which Targets are Easier?

## Slide 206: Fitts Law(1954)
MT = a + b log2 (2A/W)
where:
MT = Movement Time
a, b = Individual and Situational Constants
A = Amplitude of Movement
W = Width of Target
2A/W = Index of Difficulty (ID)

## Slide 207: Fitts Law Demonstration
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
o
A
W

## Slide 208: Fitts Law Exercise
Draw three small circles and three large circles on a sheet of paper with centers about 5 cm and 10cm apart
With a pencil make “dots” between pairs of circles
Record the time for 10 “dots”
5 cm
10 cm
2 cm
1 cm
MT = a + b log2 (2A/W)

## Slide 209: Case Study Barbie Dolls
How long does it take to assemble and pack a set of clothes for a Barbie Doll?
How many assemblies per day?
How many workers are needed?
TARGETS!!!

## Slide 210: Target Rules
Increase Target Size Percentage
  Access, Adjustment, Finesse
Consider Effect of Part Weight
Consider Effect of Part Size
Large time and postural stress savings by targeting the targets

## Slide 211: Simplify Choices Choices Take Time and may be Wrong

## Slide 212: Choices Exercise
Hold a pack of playing cards face down
Sort them into 2 piles
Sort them into 4 piles
Sort them into RED and BLACK
Sort them into H, C, D, S
  Hick’s Law MT = a + b log2n
  where: n = number of choices
Measure the Times, Observe the Errors and Hesitations

## Slide 213: Design for Manufacturing Target the Targets Reduce the choices

## Slide 214: Product Mix
It is sometimes effective to allow a product mix on the same line when many of the components are the same
Problems occur with workplace / stock layout and non value added search / walking time
Also wrong components may be installed
  Error may not be caught or passed on for rework

## Slide 215: Information Design
Make Targets Large and Choices Few
Facilitators - Provide unequivocal task instructions, procedures, labels, task aids and warnings
  Including responses to out of control situations
Displays - Provide clear task related information
  Use visual and acoustic information, cues
Controls -Enable precise task control
  Provide stops, detents where appropriate
Layout
  Address importance, frequency and sequence
  Address compatibility between displays and controls
Provide FEEDBACK regarding operation completion
Provide Andon Chord to stop the line for any reason

## Slide 216: The customer Required a lower Cowl / forward view

## Slide 217: The assembler had to deal with poorer ACCess and many more components

## Slide 218: A compromise between user styling requirements and design for manufacturability, even robots have a hard time with TIGHT Targets
“Thin is in” for the customer, but what about the assembler?

## Slide 219: Arms, Wrists and Fingers have Postures too
Orient the part
Bend the tool not the wrist
Increase the size of the handle to reduce pressure and force requirements and increase leverage

## Slide 220: Wrists have Postures too

## Slide 221: Beyond Fit and Reach Location and Orientation
The body works by first moving to the point of interest, adjusting the base posture and then using the arms, wrists and fingers to fine tune.
Under
In Front
Behind
On Top
Arms and Hands have Postures too!

## Slide 222: Orientation Problems cause Posture Problems that Interact with Force and Time
Under
In Front
Behind
On Top

## Slide 223: Sewing Lines

## Slide 224: Small Components Assembly

## Slide 225: Orient the job

## Slide 226: Bend the Tool not the Wrist

## Slide 227: Use the right Handle

## Slide 228: Biomechanical Risk factors for CTDs
Force
Posture
Movement
Repetition
Vibration
Temperature
Inadequate recovery time

## Slide 232: Job and Operations Design The Time factor

## Slide 233: Operations Design
The key to productivity is the removal of non value added work
  Long or frequent transfers
  Search for components or target
  Reorienting the component / product
Use belts / gravity for transfers, components
Place tools / components in the operations sequence
Use belt / gravity for finished goods

## Slide 234: Job Design
Taylorism
  Job simplification
  Managers manage workers work
But workers are able to master many tasks
Workers do have insight into quality, productivity and health and safety issues
Workers do not like to be bored
  Vigilance decrement may be a problem
  Local and general fatigue will be a problem
Therefore design job variety

## Slide 235: Operations Design – Grocery Store Checkout
Discuss the layout, operations and throughput
Discuss the repetitive strain illnesses

## Slide 236: Shift Work
Avoid one week rotations
Implement permanent shifts
Implement short cycle shift schedules
  2 – 3 days
  Use forward rotation: Day – Evening – Night – Off
Limit shift durations
  8 is better than 10 and 12 is the limit
  4 crew 3 shift or 3 crew 2 shift arrangements
Provide one long and many short relief breaks for assembly work
  Walking for at least 5 minutes every hour

## Slide 237: Singapore MOM ergo@work app
Postures, stretches, breaks

## Slide 238: Physical Work Stress Index (PWSI) Addressing the TIME Dimension

## Slide 239: PWSI
The Physical Work Stress Index (PWSI) is a simple, robust physical activity measurement system that indicates an optimal level of workload between high static and high dynamic demands.
It uses an activity sampling approach which can be applied to regular (cyclic) work and irregular work over short or long time periods.
The PWSI may be developed as a manual assessment tool or through the use of a spreadsheet

## Slide 240: Physical Stress and Strain People respond well to optimal levels of physical (and cognitive) variety
Strain
Stress

## Slide 241: History
The PWSI was first developed as a student project at the University of Hong Kong in 1976 (Brian Peacock, Janet Liu)
It was further developed at the University of Oklahoma through undergraduate and graduate projects during the early 1980s (Susan Cheatwood, Jacob Chen)
A description of the process was published by Chen, Peacock, and Schlegel in 1989 in the International Journal of Industrial Ergonomics

## Slide 242: Validation
The tool has been validated by application to a wide variety of jobs in comparison with physiological measures (heart rate) and by comparison with other physical work assessment tools.
The tool requires that statistically based activity sampling is applied and that a sufficient number of observations is made.
The tool is not aimed at predicting the occurrence of cumulative trauma, rather it aspires to indicate a level of physical activity conducive to good health

## Slide 243: The Elements
Location
Base Posture
Orientation
Posture (R/L Hand Position)
External Load
Thermal Load
These elements were chosen to reflect the major anthropometric, biomechanical and physiological loads on the worker.

## Slide 244: Activity Sampling
A random or regular sampling scheme is developed depending on the periodicity of the work activity.
  For regular, machine paced work, a random sample is recommended.
  For irregular work, a regular sampling process is both convenient and valid.
The ordinal mappings from values of each of these major elements are recorded at each sampling instant
Generally it is appropriate to gather data from about 10 samples but greater precision can be achieved by increasing the number of observations

## Slide 245: Ordinal Values
0 1 2 3
Location Distance from Primary Workplace
< 5 m 5 - 10 m 10 - 50m > 50 m
Postural Base Lying Sitting Leaning Standing
Orientation Forward R/L Side Backward Under
L Hand Position In Box Edge Outside Outside Box of Box Box in Two Planes
R Hand Position In Box Edge Outside Outside Box of Box Box in Two Planes
External Load Light Medium Heavy Very Heavy
0 - 1 lb 1 - 10 lb 10 - 25 lb > 25 lb
Thermal Load Comfortable Warm Hot Very Hot
65 - 75 75 - 85 85 - 95 >95

## Slide 246: Location
No changes in location, as would be observed in many computer, electronics assembly and machine minding tasks, indicate an undesirable level of static stress.
Large changes in location would be observed if the operator had to walk long distances - this would indicate an undesirable level of dynamic workload

## Slide 247: Base Posture
The range of base postures considered include lying, sitting, leaning (sit-stand) and standing
Maintaining anyone of these postures all day is undesirable - a high static load.
Constantly changing base posture as in changing from sitting to standing too frequently would indicate a high dynamic workload.

## Slide 248: Orientation
It is common for operators in some jobs to change their orientation frequently, often including trunk twisting or moving their feet to collect stock from a container placed adjacent to their workplace.
One example of such work is seen among supermarket checkout clerks.
Some degree of trunk twisting is desirable , but too much (or too little) is not.

## Slide 249: Hand Location
If the hands are within a small volume of “the box” all day long this may indicate a lack of shoulder, trunk and lower limb activity
In contrast, repeated movements outside the box as in working overhead or at floor level reflects a highly dynamic use of the arms, legs and trunk.
This simple concept of “the box” is therefore a good reflection of the physical demands of a task that is sufficiently accurate for most practical purposes.

## Slide 250: The Box
For the standing operator, the box is a region between 30 and 50 inches from the floor (between knuckle height and shoulder height), 25 inches out in front (functional reach)and 15 inches laterally from the midline of the body (minimal twist comfort region).
These numbers are rounded / approximated to account for a wide range of population anthropometric values; greater precision using reach curves may be used if desired.
For the seated operator the vertical dimensions of the box are between 20 and 40 inches
Operations within the box, at the edge of the box, outside the box and outside the box in two dimensions reflect increasing (ordinal) levels of postural deviation from the base postures.

## Slide 251: The Box or the Ball Work (hand) placement for most of the time
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
Sitting
High Sitting
Leaning
Standing

## Slide 252: External Loads
If the operator handles heavy (or light) objects repeatedly then this would reflect a high dynamic workload.
Conversely if an object is held or pushed continuously then this would constitute a highly static load

## Slide 253: Thermal Stress
Continuous exposures to high, low or even moderate temperatures may produce a high level of “static” stress on the body.
Conversely, constantly changing temperatures could over stimulate the body’s thermal regulatory processes.

## Slide 254: Data Processing
The “absolute” physical workload is calculated simply by averaging the scores from the sampled observations for each element of the index.
The “successive differences” sheet calculates the average of the absolute values of the differences between successive observations.
Averages are obtained by dividing the element totals by three times number of observations and the grand total by 7 (the number of elements) This produces a relative value between 0 and 3.

## Slide 255: Physical Workload
The absolute physical workload of a task may be estimated by averaging the within element scores and then producing a profile of the task.

## Slide 258: Static and Dynamic Workload Balance
Large differences in the ordinal values of the selected variables between sampling instants reflect a highly dynamic physical workload.
No change between successive time observations reflects a high static physical workload.
Summing (and then averaging) the changes over successive sampling intervals gives an indication of the overall static / dynamic workload balance for each of the elements.

## Slide 261: Interpretation
High scores >2 on the absolute workload profile represent undesirable levels of physical stress
Low scores (<1) on the static / dynamic balance profile are associated with static workloads
High scores (> 2) are associated with highly dynamic workloads
Optimal “balance” values range from 1 to 2

## Slide 262: The Best Posture is the Next Posture

## Slide 263: Walkie-Talkies
Require all employees to walk and talk every hour for 5 minutes
  Walking provides physical relief
  Talking provides social relief
  Walking and talking provide attention relief
  Productivity will not suffer

## Slide 264: Stretching
Systematically and slowly move every joint through its full range
  Move, hold for 3 seconds, relax
Standing (hold on to the back of the chair)
  Move knee up then push leg back
  Move leg across the body, away from the body and in big circles
Sitting
  Bend forward, back, side to side, and twist
  Move shoulders and shoulder girdles in big circles
  Move wrist and hands through full range
  https://itunes.apple.com/sg/app/ergo-work/id556877197?mt=8

## Slide 265: The Usain Bolt fitness test 10 – 100 – 1000 - 10000
Distance (m) | World Record (sec) | Your Time (secs) | Your %
10 | 1 | 5 | 20
100 | 10 | 40 | 25
1000 | 130 | 400 | 43
10000 | 1600 | 4000 | 40
Participants should walk or run 10, 100, 1000, 10000 meters, measure their times and calculate their percentage score against the world record.

## Slide 266: Workability Index

## Slide 267: Workability Index
Date |  |  |  |  |  |  |  |  |  |  | Job Description | 
Analyst |  |  |  |  |  |  |  |  |  |  |  | 
Survey Reference / Times |  |  |  |  |  |  |  |  |  |  |  | 
Job Survey Ratings |  |  |  |  |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
 | Place a small "x" in the appropriate rating cell | N/A | Green |  | Yellow |  | Orange |  | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria

## Slide 268
Policy Decisions
Engineering Variable or Composite Index
Common Currency
Outcome Scale
7
6
5
4
3
2
1
Unacceptable
Range
Ideal Range
Region of Interactions and Continuous Improvement
Policy Statements
1
2
3
4
6
5
7

## Slide 269
Design Rules - Consensus
Policy
Science
History
Experience
Evaluation
  Verification
  Validation
  Sensitivity
Predictions
Design
Rule
Rule
Implementation
Data
Consensus:
  HF Experts
  Engineers
  Managers
  Customers
Technical
Memory

## Slide 270: Workability Index
Addresses
  Spatial factors
  Manual materials handling
  Manipulation
  Environmental factors
  Information factors
  Operational factors

## Slide 271: Spatial Factors
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Access |  |  |  |  |  |  |  | Clearances, obstructions, doors, barriers
Fit |  |  |  |  |  |  |  | Head room, Knee / Foot room, Width
Reach |  |  |  |  |  |  |  | Box, 50 cm reach curves
Postures |  |  |  |  |  |  |  | Sitting, Standing, Squatting, Middle, Outer, Inner ranges
Movements |  |  |  |  |  |  |  | Range, speed
Task surface orientation |  |  |  |  |  |  |  | Front, above, below, behind
Ramps |  |  |  |  |  |  |  | Slope, length
Stairs |  |  |  |  |  |  |  | Number, height
Counts |  |  |  |  |  |  |  | Refer to HF Specialist, manufacturing engineer for interventions

## Slide 272: Manual Materials Handling
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Lifting |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Carrying |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Holding |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Pulling |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Pushing |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Twisting, bending |  |  |  |  |  |  |  | Vertical and horizontal task locations
Interfaces, coupling |  |  |  |  |  |  |  | Good, sharp
Counts |  |  |  |  |  |  |  | Refer to NIOSH Lifting Equation and Snook Tables

## Slide 273: Manipulation
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Shoulder, Elbow |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces
Hand, Wrist, Fingers |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces, coupling, interfaces
Targets |  |  |  |  |  |  |  | Target sizes and tolerances
Precision |  |  |  |  |  |  |  | Fine, coarse
Counts |  |  |  |  |  |  |  | Use Hand activity level TLVs

## Slide 274: Environmental Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Heat, Cold |  |  |  |  |  |  |  | Air Temperature, Humidity, Radiant heat, Air movement
Glare |  |  |  |  |  |  |  | Location, intensity, contrast, window and local lighting
Dark |  |  |  |  |  |  |  | Interference with visual demands
Noise Intensity |  |  |  |  |  |  |  | Task, Ambient, Sound Level, Frequency, Variability
Vibration |  |  |  |  |  |  |  | Whole body, hand arm
Accelerations |  |  |  |  |  |  |  | Pounding, jerks
Slip, trip, fall |  |  |  |  |  |  |  | Work context hazards, visibility, barriers
Chemical |  |  |  |  |  |  |  | Refer to OH
Radiation |  |  |  |  |  |  |  | Refer to OH
Counts |  |  |  |  |  |  |  | Refer to OH, Safety or Engineering for intervention

## Slide 275: Information Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Visual |  |  |  |  |  |  |  | Visual acuity, discrimination demands, importance
Acoustic |  |  |  |  |  |  |  | Hearing acuity, discrimination demands, importance
Attentional |  |  |  |  |  |  |  | Sustained and divided attention demands
Memory |  |  |  |  |  |  |  | Operational memory span, interferences
Cognitive |  |  |  |  |  |  |  | Calculations, planning, analyses
Decisions |  |  |  |  |  |  |  | Number of choices, ambiguity, risk
Communication |  |  |  |  |  |  |  | Frequency, variability, importance
Control |  |  |  |  |  |  |  | Precision, feedback, prediction
Situation awareness |  |  |  |  |  |  |  | Importance, distractions
Mental workload |  |  |  |  |  |  |  | Information and time demands, training, stress
Outcomes |  |  |  |  |  |  |  | Consequences of human error
Counts |  |  |  |  |  |  |  | Refer to HF specialist for intervention

## Slide 276: Operational Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
 |  |  |  |  |  |  | Operational factors will usually interact with some or all of the other factors | Intervention through administrative and / or operational controls
Job cycle duration |  |  |  |  |  | Engineering issues |  | Operations per hour, job cycle time
Static posture duration |  |  |  |  |  |  |  | % job cycle, % day
Repetitions, frequencies |  |  |  |  |  |  |  | Frequency per hour of same or similar task
Job pacing |  |  |  |  |  |  |  | Self paced, Piece Rate, Machine paced, Supervisor
Span of responsibility |  |  |  |  |  | Operational Issues |  | Product quality, other colleagues, autonomy
Team structures |  |  |  |  |  |  |  | Job rotations
Participatory processes |  |  |  |  |  |  |  | Do employees participate in work design decisions
Technical support |  |  |  |  |  |  |  | Availability, supervision
Training, Acclimatization |  |  |  |  |  |  |  | Level of experience, adaptation to task
Special Populations |  |  |  |  |  |  |  | Are eldely or disabled persons employed with accommodations?
Counts |  |  |  |  |  |  |  | Refer to HF Specialist / Management for intervention

## Slide 277: Overall Counts
 |  |  | Job Survey Ratings |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
 | Place a small "x" in the appropriate rating cell |  | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Overall Counts 1 |  |  |  |  |  |  |  |  | Notes | Engineering Controls
 |  | 2 |  |  |  |  |  |  | Jobs should be analysed before and after interventions | 
 |  | 3 |  |  |  |  |  |  | The worksheet may also be used repeatedly over a day to analyse the variability of work demands | Administrative Controls
 |  | 4 |  |  |  |  |  |  | Consensus quantitative anchors may be added to the rating scales to improve their consitency | 
 |  | 5 |  |  |  |  |  |  | Basic training (1 day) in the use of this worksheet should be required of all ergonomics monitors (CEM Level 1) | 

## Slide 278
 |  |  |  |  |  |  |  | Singapore Workplace Ergonomics | 
 |  |  |  |  |  |  |  | Workability Index | 
Date |  |  |  |  |  |  |  | Job Description | 
Analyst |  |  |  |  |  |  |  |  | 
Survey Reference / Times |  |  |  |  |  |  |  |  | 
 |  |  |  | Job Survey Ratings |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
 | Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Spatial Factors |  |  |  |  |  |  |  |  | 
 | Access |  |  |  |  |  |  |  | Clearances, obstructions, doors, barriers
 | Fit |  |  |  |  |  |  |  | Head room, Knee / Foot room, Width
 | Reach |  |  |  |  |  |  |  | Box, 50 cm reach curves
 | Postures |  |  |  |  |  |  |  | Sitting, Standing, Squatting, Middle, Outer, Inner ranges
 | Movements |  |  |  |  |  |  |  | Range, speed
 | Task surface orientation |  |  |  |  |  |  |  | Front, above, below, behind
 | Ramps |  |  |  |  |  |  |  | Slope, length
 | Stairs |  |  |  |  |  |  |  | Number, height
 | Counts |  |  |  |  |  |  |  | Refer to HF Specialist, manufacturing engineer for interventions
Manual Materials Handling |  |  |  |  |  |  |  |  | 
 | Lifting |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
 | Carrying |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
 | Holding |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
 | Pulling |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
 | Pushing |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
 | Twisting, bending |  |  |  |  |  |  |  | Vertical and horizontal task locations
 | Interfaces, coupling |  |  |  |  |  |  |  | Good, sharp
 | Counts |  |  |  |  |  |  |  | Refer to NIOSH Lifting Equation and Snook Tables
Manipulation |  |  |  |  |  |  |  |  | 
 | Shoulder, Elbow |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces
 | Hand, Wrist, Fingers |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces, coupling, interfaces
 | Targets |  |  |  |  |  |  |  | Target sizes and tolerances
 | Precision |  |  |  |  |  |  |  | Fine, coarse
 | Counts |  |  |  |  |  |  |  | Use Hand activity level TLVs
Environmental Factors |  |  |  |  |  |  |  |  | 
 | Heat, Cold |  |  |  |  |  |  |  | Air Temperature, Humidity, Radiant heat, Air movement
 | Glare |  |  |  |  |  |  |  | Location, intensity, contrast, window and local lighting
 | Dark |  |  |  |  |  |  |  | Interference with visual demands
 | Noise Intensity |  |  |  |  |  |  |  | Task, Ambient, Sound Level, Frequency, Variability
 | Vibration |  |  |  |  |  |  |  | Whole body, hand arm
 | Accelerations |  |  |  |  |  |  |  | Pounding, jerks
 | Slip, trip, fall |  |  |  |  |  |  |  | Work context hazards, visibility, barriers
 | Chemical |  |  |  |  |  |  |  | Refer to OH
 | Radiation |  |  |  |  |  |  |  | Refer to OH
 | Counts |  |  |  |  |  |  |  | Refer to OH, Safety or Engineering for intervention
Information Factors |  |  |  |  |  |  |  |  | 
 | Visual |  |  |  |  |  |  |  | Visual acuity, discrimination demands, importance
 | Acoustic |  |  |  |  |  |  |  | Hearing acuity, discrimination demands, importance
 | Attentional |  |  |  |  |  |  |  | Sustained and divided attention demands
 | Memory |  |  |  |  |  |  |  | Operational memory span, interferences
 | Cognitive |  |  |  |  |  |  |  | Calculations, planning, analyses
 | Decisions |  |  |  |  |  |  |  | Number of choices, ambiguity, risk
 | Communication |  |  |  |  |  |  |  | Frequency, variability, importance
 | Control |  |  |  |  |  |  |  | Precision, feedback, prediction
 | Situation awareness |  |  |  |  |  |  |  | Importance, distractions
 | Mental workload |  |  |  |  |  |  |  | Information and time demands, training, stress
 | Outcomes |  |  |  |  |  |  |  | Consequences of human error
 | Counts |  |  |  |  |  |  |  | Refer to HF specialist for intervention
Operational Factors |  |  |  |  |  |  |  | Operational factors will usually interact with some or all of the other factors | Intervention through administrative and / or operational controls
 | Job cycle duration |  |  |  |  |  | Engineering issues |  | Operations per hour, job cycle time
 | Static posture duration |  |  |  |  |  |  |  | % job cycle, % day
 | Repetitions, frequencies |  |  |  |  |  |  |  | Frequency per hour of same or similar task
 | Job pacing |  |  |  |  |  |  |  | Self paced, Piece Rate, Machine paced, Supervisor
 | Span of responsibility |  |  |  |  |  | Operational Issues |  | Product quality, other colleagues, autonomy
 | Team structures |  |  |  |  |  |  |  | Job rotations
 | Participatory processes |  |  |  |  |  |  |  | Do employees participate in work design decisions
 | Technical support |  |  |  |  |  |  |  | Availability, supervision
 | Training, Acclimatization |  |  |  |  |  |  |  | Level of experience, adaptation to task
 | Special Populations |  |  |  |  |  |  |  | Are eldely or disabled persons employed with accommodations?
 | Counts |  |  |  |  |  |  |  | Refer to HF Specialist / Management for intervention
Overall Counts 1 |  |  |  |  |  |  |  | Notes | Engineering Controls
 | 2 |  |  |  |  |  |  | Jobs should be analysed before and after interventions | 
 | 3 |  |  |  |  |  |  | The worksheet may also be used repeatedly over a day to analyse the variability of work demands | Administrative Controls
 | 4 |  |  |  |  |  |  | Consensus quantitative anchors may be added to the rating scales to improve their consitency | 
 | 5 |  |  |  |  |  |  | Basic training (1 day) in the use of this worksheet should be required of all ergonomics monitors (CEM Level 1) | 
 | ÓBrian Peacock Ergonomics (BPE) Pte Ltd |  |  |  |  |  |  |  | 

## Slide 280: Conclusions – How Ergonomics Works

## Slide 281: Ergonomics Addresses
human, technological, contextual and operational complexity and variability
tradeoffs among many job outcomes
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E
Physical
Cognitive
Social
Affective
Context
Temporal
Sensory
E
P
B
E4S4
Macro
+
Micro

## Slide 282: The Design Cycle
The Process,
Job, Task,
Transaction
or Simulation
Uncontrollable
Conditions / Context
Specifications
Design
Equipment
Context
Humans
Operations
Guidelines
and
Constraints
Decisions
Policy
Money
Analysis
Requirements
Outcomes
Analysis
Analysis
Tools
Analyses
6U
2M
E4S4
Prediction
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E

## Slide 283: Cumulative Trauma Disorders

## Slide 284: The CTD Epidemic Repetitive motion strain Occupational overuse syndrome
Meatpacking
Nursing homes
Automobile manufacturing
Parcel handling
Electronics manufacturing
Textiles
Food processing
Textiles
Years of Contentious / Combative dialog among Government (NIOSH / OSHA)
Business (NAM, COT), and Unions (UAW)
providing many opportunities for Ergonomics Researchers, Professionals, Practitioners and Product developers

## Slide 285
Occupational Musculoskeletal Disorders
Acute –slips, trips, falls
  strains, sprains, fractures
Chronic – cumulative trauma disorders, repetitive strain injuries, etc.
Work Related Musculoskeletal Disorders (WRMSDs)
Injury
  biomechanical basis
  mechanical disruption of tissues
  results in pain, inflammation and other biological responses
  acute or chronic (overuse, abuse)
    “illness”

## Slide 286: Risk Factors for MSDs
Genetic / morphological
  carpal tunnel diameter
  gender
Psychosocial
  pain threshold
  job and work environment factors
    job content
    work organization/supervision
    financial aspects of work
  non-occupational factors
    socioeconomic status
    non-occupational activities
    family status and relations
    personality and psychological factors
  iatrogenesis (cause by the health care system)
    health care system
    work safety analysis
    insurance requires labels

## Slide 287: Upper Limbs and Backs

## Slide 288: Lot’s of MSDs!

## Slide 289: Anatomical Location of MSDs
tendon
muscle
nerve
vascular
bursa
bone/cartilage

## Slide 290: Tendon Disorders
Tenosynovitis
  inflammation of tendon and tendon sheath
  may result in either micro- or macrotrauma
  localized swelling (resulting in narrowing or stenosing) of the sheath
  may form nodule on tendon – resulting in tendon entrapment
Tendinitis
  inflammation of tendon alone

## Slide 292: Localized Fatigue
Normal
  Reduced circulation
  Tiredness, discomfort
  Loss of control
  Increased effort
  Decreased strength
Recovers with removal of stress
With insufficient recovery and / or mechanical damage – may lead to cumulative trauma disorder
Sustained and repeated forceful exertions in awkward postures

## Slide 294: The Neck
Localized pain, redness and swelling
Muscle spasm / tenderness
Active ROM
  Flex 45
  Extend 55
  Rotate L/R 70
  Side flex 40
Check for radiated pain/ parasthesia down arm
  Cervical nerve root / brachial plexus involvement
Check for arthritis
Sustained posture
  Looking at work / computer screen
Drooping shoulders
Rest, ice / heat, massage
Mobilization exercises
Work place / posture intervention
Frequent rest breaks
Job enlargement and / or rotation

## Slide 295
Compression between two other types of tissue (muscle, bone, ligament, etc.)
Direct compression of nerve by contact with an external object
Impedes the transmission of nerve impulse
Nerve Disorders

## Slide 296: Peripheral nerve Conditions

## Slide 297: Carpal Tunnel Syndrome

## Slide 298: Carpal Tunnel Syndrome
Tingling, numbness, weakness
Nocturnal parasthesia
Clumsiness
  Thumb muscles
  Thenar eminence atrophy
Tinel’s Sign
  Tapping
Phalen’s test
  Flex wrist for 1 minute
  Parasthesia
Pin prick around distribution of median nerve
Nerve conduction tests with electromyography

## Slide 299
hold position for 1 minute
pain/tingling radiating distally through innervated areas may be a positive test for CTS
Carpal Tunnel Syndrome
Phalen’s test

## Slide 300
Tapping median nerve
Tingling/pain is positive for CTS
Carpal Tunnel Syndrome: Tinel’s test
Quality of Phalen’s and Tinel’s tests:
sensitivity – 32% to 89%
specificity – 72% to 84%
not an unequivocal diagnosis
Therefore Nerve Conduction Test
  Not definitive

## Slide 301: Carpal Tunnel Syndrome
Ice / Heat
ROM exercises
Job redesign
  No sustained, forceful, repeated, flexion / extension / ulnar deviation of the wrist
Anti inflammatory medication
Night splints
  (Work splints not advised)
Surgery -transverse carpal ligament release

## Slide 302
Entrapment of the ulnar nerve
  Guyon canal on the medial side of the hand
  hand hammering, flexion/extension at wrist
  cubital tunnel at the elbow (formed by the two heads of the flexor carpi ulnaris)
  results from resting elbows on hard surface or twisting at the elbow
Guyon Canal and Cubital Tunnel Syndrome

## Slide 304: Hypothenar Hammer Syndrome
Repeated forceful pounding with the palm
  Push fasteners
Occlusion of ulnar artery
Nerves of 4th and 5th digits
Tenderness and parasthesia
Hypothenar atrophy
Heat and ice
Gentle exercise
Stop pounding!
“Flat muscle”

## Slide 305: Ulnar Nerve Compression
Ulnar nerve
Guyon’s canal
  Pisiform and hook of hamate bones
  Palmaris muscle
Hammering / Pounding
Wrist hyper extension
Prolonged and repetitive full range wrist flexion and extension
Pain, tenderness
Tinel’s sign
Stop hammering
Stop offending wrist movements

## Slide 306
Prepatellar bursitis is experienced by carpet layers
Subacromial or subdeltoid bursitis
Bursitis

## Slide 307: Trigger Finger
Swelling and nodule formation of flexor tendons of the digits
  Clicking
  Locking
Pistol type tools
  High force / range trigger
Surgery
Tool design
  Broader / lighter trigger
  Push to start

## Slide 308: Ganglions
Tenosynovitis
Digit extensors
Repetitive forceful extension

## Slide 309: De Quervain’s Disease
Abductor pollicis longus / extensor pollicis brevis
  Friction
  Tenosynovitis
Repeated thumb activity
  Inter phalangeal joint flexion with proximal joint extension
  Video game thumb
  Repeated hard gripping of oversize handle
Pain
Swelling
Tenderness
Clicking
Finkelstein’s test
  Thumb in palm
  Forced ulnar deviation
  Pain over radial styloid
Stop doing the movement that causes the problem
Heat / ice / massage / gentle ROM activities

## Slide 310
Finkelstein’s test
positive if position causes pain at the radial styloid and along the thumb extensor tendon
Testing for de Quervain’s disease

## Slide 311: Raynaud’s Syndrome
“White Finger”
  Multiple levels
Circulatory disorder
  Vibration
  Cold
  Occupational / hereditary
Progressive
  Months, years
Chain saws (forestry)
Chipping hammers (foundry)
Gloves
Lighter grip
Padded handles
Vibration absorbing tools
Supported tools
Automation
Job rotation

## Slide 313: The Shoulder
Very complex, comprises shoulder girdle and shoulder joint
  Large range of motion
  Rotator cuff muscles
  Bursae
  Long head of biceps
    Tendinitis, tenosynovitis
Frozen shoulder
  Multiple inflammatory sites
  Joint capsule
Check for passive ROM
Check for active ROM with and without gravity / resistance
Crepitus
Painful arc
Check for referred pain from neck, cardiac ischemia, diaphragm area etc.

## Slide 314
Entrapment of the brachial plexus (nerve roots at C5 through C8)
May occur at several locations, for instance between clavicle and first rib, scalenus muscles in the back of the neck
Overhead work
Thoracic Outlet Syndrome
Also blood vessel compression