## Slide 1: Time The Ultimate Ergonomics Challenge
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: Ergonomics Opportunities What can we change?
Why the activity is being performed – purpose and constraints
Where things are – space
When things happen – TIME
How difficult things are - force, information
Who is involved – selection, training, assignment
How the activity is performed - behavior
What is the context – environment

## Slide 3: Things that Happen over Time
Aging (everything)
Growth (size, strength)
Learning (motor, information)
Fatigue (local, general)
Adaptation (light, perception)
Acclimatization (temperature, noise)
Forgetting (information)
Cumulative trauma (musculoskeletal)
Boredom (motivation)
Vigilance decrement (attention)
Etc.
Time is “filled” with something such as Work, Information, and Environmental and Social stresses
“Exposure”
=
Stress x Time

## Slide 4: Aspects of Time
Frequency
  Repetition (Hertz)
Duration
  Continuous exposure to a physical, informational or social source of stress
    Static postures, noise, crowding, artificial habitat
  Intermittent exposure to a physical, informational or social source of stress
    Climate, schedule, job, training

## Slide 5: Too Much or Too Little Time Exposure = Stress x Time
To much time exposure causes such things as forgetting, fatigue.
To little time means we have to hurry our tasks and may not be able to make the most of available information, which leads to errors of omission, inaccuracy etc.

## Slide 6: Time Interacts With Context (e.g. Physical Work Load, Environment)
Time
Effect
Context

## Slide 7: Time Effects Are Non Linear (e.g. Adaptation)
Cause (including Time)
Effect
}
Human
Variability
Region
of
Interest

## Slide 8: Asymptotes and Diminishing Returns
Time – Duration, Repetition, Age
Effects of exposure over time
Time works both ways
Fatigue
Skill

## Slide 9: Catastrophic Failure (e.g. Local Muscle Fatigue, Aging)
Time
Failure
Capability
Limitation

## Slide 10
People Vary
In their Response to Stress over Time
Time – Duration, Repetition, Age
Effects of exposure over time
As much as 10:1 on many dimensions

## Slide 11: Industrial Engineering
The industrial engineering profession has been committed to time analysis and time management for almost a century.
  Production lines are efficient.
  Line balance is a simple concept with some merit.
  Line unbalance may be more appropriate for people with different capabilities or training.
  Autonomous teams may address these issues.
This major aspect of the industrial engineering profession (time management), though generally appealing to management and sometimes to labor, objectifies human labor, ignores human variability and has to face the inevitable consequence – “human nature” (ergonomics).

## Slide 12: Line Balance
Same
Different
Different

## Slide 13
Work Cells, Work Teams
Flexibility

## Slide 14: Time, Stress and Context (Interactions)
Time
Primary
Stress
Context

## Slide 15: An example: The NIOSH Lift Equation
Space
  Horizontal distance, vertical distance, distance moved, angle, interface(s)
  Posture
Time
  Frequency (lifts per minute)
  Duration (length of shift, rotation)
Force
  Weight
Assumptions :
Who does the job and how long they have been doing it –
Selection training assignment age
Protection

## Slide 16
The NIOSH Lift Equation (Another way of looking at it)
Force (Weight)
Spatial Factors (context)
Relatively easy to change
Sometimes easy to change
Staffing Levels
Line Rate
1
5
10
10
50
Time (repetitions per minute)
100
1

## Slide 17: The Box (Functional Reach Curves, Cut off the corners?)
25
30
50
30
If work is kept within this volume, most people will be comfortable, most of the time.

## Slide 18
52.7
49.5
40.5
27.0
13.5
40
35
30
25
20
15
10
.33
1
3
6
9
12
The 1981 NIOSH Lift Equation (All Spatial Multipliers {context} = 1, 8 Hours)
Lifts per minute
Weight
Action Limit
Maximum Permissible Limit
149
122
81
158
41

## Slide 19: The 1991 NIOSH Lift Index (All Spatial Multipliers {context} = 1, 8 Hours) (Cutoffs assumed to be 1 and 2)
.94
1.05
1.43
2.90
5.23
.82
.92
1.25
2.54
4.58
.7
.78
1.07
2.18
3.92
.58
.65
.89
1.82
3.27
.47
.52
.71
1.45
2.61
.35
.39
.53
1.09
1.96
..23
.26
.36
.73
.1.31
40
35
30
25
20
15
10
.33
1
3
6
9
12
Lifts per minute
Weight
Lift Index is more sensitive to frequency than the 1981 NIOSH Lift AL

## Slide 20
13.2
40
120
240
360
480
11.55
35
105
210
315
420
9.9
30
90
180
270
360
8.25
25
75
150
225
300
6.6
20
60
120
180
240
4.95
15
45
90
135
180
3.3
10
30
60
90
120
40
35
30
25
20
15
10
.33
1
3
6
9
12
Pounds per Minute
(Energy: 50, 100)
Lifts per minute
Weight
More sensitive to frequency than the 1991 NIOSH Lift Equation

## Slide 21: ‘81, ‘91 and Pounds per Minute (All Contextual Factors = 1, 8 Hours)
9.9
30
90
180
270
300
3.3
10
30
60
90
120
30
10
.70
.78
1.07
2.18
3.92
.23
.26
.36
.73
1.31
30
10
10
52.7
49.5
40.5
27.0
13.5
52.7
49.5
40.5
27.0
13.5
30
.33
1
3
6
9
12
Lifts per minute
Weight
lb/min (50, 100)
’91 LI (RWL 1,2)
’81 AL

## Slide 22: Solve the Contextual Problems by Design
Spatial problems and their solutions are usually obvious
  Raise the line, rack
  Bring the load close to the operator
  Design good handles
Environmental problems are usually obvious
  Raise / lower the temperature, noise, light
Focus on the main issues (e.g. Weight) and TIME

## Slide 23: But how do we come up with the numbers? Consensus Rule Making
Because of human variability there will never be a totally “scientific” / “data driven” basis of rule making
Epidemiology is probabilistic
Job assignment /matching is an imperfect process
The NIOSH equations, RULA and the Repetition Index are based on conservative expert interpretation of the evidence.
Risk is a management, government or negotiated responsibility
But ENGINEERS, DESIGNERS, Managers and Legislators need a NUMBER! Or a “Loss Function”

## Slide 24: Understand Loss Functions
Simple or Complex Stress
Strain
Intolerable
Ideal
Continuous Improvement

## Slide 25
Consensus
Consensus
  HFExperts
  Engineers
  Managers
  Customers
Policy
Science
History
Experience
Data
Predictions
Rule
Rule
Application
Rule Evaluation:
  Verification
  Validation
  Sensitivity

## Slide 26: Rules and Tools A pragmatic approach to ergonomics
Why not?
  Multiple dimensions – complex interactions
  Human variability - 10:1 on many dimensions
  Nonlinearities between causes and effects
But why?
  Limited change opportunities
  Insufficient detailed information
Keep the rules and tools simple (but not too simple)
  Face complexity with intelligence
  Make reasonable assumptions
  Use the Voice of the Customer for fine tuning

## Slide 27
Where Do the Experts Fit in?
Simple Rules
70%
Analysis Tools
20%
The Expert
10%
Problems
Design
Design
Design

## Slide 28
Rating Response
Not Applicable
Adequate Accept
Marginal Investigate
Intolerable Reject / Modify
Unthinkable Unacceptable
Common Currency for Individual Stressors (a 10 point scale)
5
8 - 10
4
3
2
1
0
7
6
This scale provides a sufficient level of resolution.
It facilitates comparisons and prioritization
In general only 7 points are necessary

## Slide 29
7
14
21
28
35
42
49
6
12
18
24
30
36
42
5
10
15
20
25
30
35
4
8
12
16
20
24
28
3
6
9
12
15
18
21
2
4
6
8
10
12
14
7
6
5
4
3
2
1
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Time
Stress
A Common Currency
for interactions with TIME
A simple design tool

## Slide 30
7
14
21
28
35
42
49
6
12
18
24
30
36
42
5
10
15
20
25
30
35
4
8
12
16
20
24
28
3
6
9
12
15
18
21
2
4
6
8
10
12
14
7
6
5
4
3
2
1
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Time
Stress
Dealing with Major Context
As contextual factor values increase, move up or across the chart
Rating
Value
7
6
5
4
3
2
1

## Slide 31
7
14
21
28
35
42
49
6
12
18
24
30
36
42
5
10
15
20
25
30
35
4
8
12
16
20
24
28
3
6
9
12
15
18
21
2
4
6
8
10
12
14
1
2
3
4
5
6
7
7
6
5
4
3
2
1
1
2
3
4
5
6
7
Duration (minutes)
% Joint Range
Example: Static Posture
60
50
40
30
20
10
0
1
5
10
15
20
25
30
Neutral
<
>
7
30
6
25
5
20
4
15
3
10
2
5
1
1
Force

## Slide 32
7
14
21
6
12
18
5
10
15
20
4
8
12
16
20
3
6
9
12
15
18
21
2
4
6
8
10
12
14
1
2
3
4
5
6
7
7
6
5
4
3
2
1
1
2
3
4
5
6
7
Percent Job Cycle
% MVC
Example: Force Exertion
90
80
70
60
50
40
30
1
5
10
15
20
25
30
<
>
7
60
6
50
5
40
4
30
3
20
2
10
1
0
Posture

## Slide 33
7
14
21
6
12
18
5
10
15
20
4
8
12
16
20
3
6
9
12
15
18
21
2
4
6
8
10
12
14
1
2
3
4
5
6
7
7
6
5
4
3
2
1
1
2
3
4
5
6
7
Duration (minutes)
Temperature
0F
Example: Thermal Environment
110
105
100
95
90
85
80
1
5
10
15
20
25
30
<
>
7
9
6
8
5
7
4
6
3
5
2
4
1
3
kcal / min

## Slide 34: Time Management
Traditional Industrial Engineering
  Henry Ford
  Gilbreths (Therbligs)
Predetermined Time Systems
  MTM
  Work-factor
  Standard data
Job Design
  Rotation, enlargement
  Semi autonomous teams
  Selection, assignment
Ergonomics
  Anthropometry, Biomechanics, Work physiology
  Cognition
  Checklists and worksheets
Incentives
Line pacing
Quotas
Cars
Chickens
Computers
Textiles
Toys
Telemarketers

## Slide 35: Time Management
Manage time with simple charts that involve major stressors and major context.
Use a Common Currency
Use consensus to establish cut off points.
  Use data if it is available.
  Use established tools eg NLE to establish cut offs.
Don’t try to micro manage time.
Use work cells to increase flexibility.
Use teams to deal with individual differences and choices.