## Slide 1: A Discounting Model for Task Design
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: Some People and Many Jobs are Less Than Perfect

## Slide 3: The Discounting Philosophy
If we take the maximum possible capability of the most capable person in the world at a particular task under ideal conditions and call that 100% performance, then all people of lesser capability and faced with less than ideal conditions will perform at some level between 0% and 99%

## Slide 4: Production with Protection
Production
Protection
Labor
Task
Difficulty
Constraints

## Slide 5: Discounting Factors
Individual differences
  Age, sex, aptitude, training, disability
Task
  Workplace, equipment, materials, tools
    Physical, informational
  Protective equipment and clothing
Context
  Environment
    Thermal. lighting, gravitational, vibration, noise, atmosphere
    Psychosocial
Time
  Duration
    Within task
    Mission, shift
  Sleep loss
INTERACTIONS
Specific Training
Relative Importance

## Slide 6: Interactions
Interaction effects are real, but they are for the analysts and statisticians to worry about
Engineers can only change main effects (independent variables) one at a time.
A1(Slow) A2(Fast)
B1(Hot)
B2(Cool)
Response
e.g. Work rate and thermal environment

## Slide 7: Importance Weighting
All variables that affect human performance have a similar general relationship (using a common currency), providing the scale (and shape) are adjusted in the model
Response
Region of interest
Ideal
Cool Hot
Light Heavy
y = a + bxc

## Slide 8: The Purposes of Discounting
Work standards
  Experienced worker standard
  Predetermined times
  Traditional industrial engineering
Task planning
Manpower planning

## Slide 9: Be Careful with the Arithmetic!
There are 365 days in a year
We work 8 hours a day – that makes 365 / 3 = 121
Two day weekends 121 – 104 = 17
17 public holidays 17 – 17 = 0
20 days vacation 0 – 20 = -20 days
Not bad if we get paid for 365 – 104 – 17 – 20 = 224, 8 hour days a year for 8 * 224 = 1792 hours

## Slide 10: Also
.9 x .9 x .9 x .9 = .65
.9 x .9 x .9 x .9 x .9 = .59
.9 x .9 x .9 x .9 x .9 x .9 = .53
.9 x .9 x .9 x .9 x .9 x .9 x .1 = .05
And so on

## Slide 11: Work Standards and Task Planning
Work standards developers and task designers are not interested in Percentiles
  but they are interested in Productivity and how many people it takes to deliver a product or service, with the always present quality, health and safety constraints.
  Ergonomists are obsessed by percentiles
Work standards development and task planning can benefit from the a discounting approach that uses Percentages to describe those factors that detract from ideal performance

## Slide 12: The Speed Accuracy Tradeoff
Speed
Accuracy
Labor
Task
Difficulty
Constraints

## Slide 13: Percentages and Percentiles
In the context of Ergonomics
  Percentiles are about People
  Percentages are about Work
Percentages
  If I work half as fast as the person next door then I will take twice as long to finish the job
  My productivity is 50% of the “standard”
Percentiles
  If 95% of the people in a group (sample, population) are taller, stronger or faster than me then I am classed as a 5th Percentile

## Slide 14: The Normal Distribution
68% of a Normal Population is between +/- 1 Standard Deviation
95% of a Normal Population is between +/- 2 Standard Deviations
99% of a Normal Population is between +/- 3 Standard Deviations
Percentiles
Performance

## Slide 15: Problems with Percentiles
The sacred cow of the ergonomics profession is the 5th (95th) percentile.
This is only of value where there is data on the particular variable of interest, such as height, for the target population of interest
  We have a lot of population data on population characteristics
  There is usually very poor correlation between “percentiles” on different human characteristic or performance dimensions
  But we have very little data on specific task performance
Similarly “universal design” is misleading – we should not attempt to design everything so that everybody can use it
Percentile values are policy statements which may sometimes be of use in design standards

## Slide 16: Some Discounting Data
Manual materials handling
Age and gender
Clothing
Thermal environment
Endurance
Training

## Slide 17: The NIOSH Lift Equation
RWL = LC x HM x VM x DM x AM x FM x CM
The Recommended Weight Limit (RWL) for a particular task is obtained by multiplying the Load Constant (LC) by a series of multipliers (HM, VM, DM, AM, FM, CM) related to the characteristics of the task, that are all >0 and <=1
In other words, given the maximum load in ideal conditions, the recommended load is “discounted” as the conditions deviate from the ideal.

## Slide 18: Productivity
If you don’t design the task right the only solution is more labor

## Slide 19: Spatial “Multipliers”
METRIC US
Load Constant 23 kg 51 LB
Horizontal (25/H) (10/H)
Vertical 1-(.003 [V-75]) 1-(.0075 [V-30])
Distance .82 + (4.5/D) .82 + (1.8/D)
Asymmetry 1-(.0032A) 1-(.0032A)

## Slide 20: Typical Jobs
Load Constant | 51lbs |  |  | 
 | ins |  | ins | 
Horizontal (ins) | 20 | .50 | 30 | .33
Vertical (ins) | 20 | .93 | 0 | .78
Distance (ins) | 20 | .91 | 40 | .87
Asymmetry | 300 | .90 | 900 | .71
A poor grip interface drops you to 0.9

## Slide 21: Frequency and Duration
 | <1 Hour | 2 - 8 Hours
1 / 5 minutes | 1.00 | .85
1 / minute | .94 | .75
6 / minute | .75 | .27
You can’t walk all day as fast as you can for 5 minutes

## Slide 22: Strength Limitations
 | Occasional lbs | Repeated lbs | 
Sedentary work | 10 | (<2)? | .10
Light work | 20 | 10 | .20
Medium work | 50 | 25 | .50
Heavy work | 100 | 50 | 1.00
From Chaffin and Anderson, 1991

## Slide 23: Repetition Index
Armstrong, UMich

## Slide 24: Non Linearity
The NIOSH Lift Equation comprises a set of linear functions with cutoffs in the extreme ranges
The relationship between human responses and design (independent) variables are usually NON linear.
Relationships are usually MONOTONIC
Where they appear not to be monotonic (e.g. temperature) it may be convenient to divide the relationship into two effects

## Slide 25: Age and Performance
The best a 90 year old can expect is to perform at 40% of his capability at age 40

## Slide 26: Performance in 16 Olympic Events

## Slide 27: Percentile Performance based on Age and Athletic Records
        Age Max
        40 1.00
        50 .95
        60 .85
        70 .75
        80 .60
        90 .40
        100 .20
Note that this is the best that can be expected, individuals will be less capable than this, based on DNA, disease, disuse, disinterest etc.

## Slide 28: Sex Differences
Strength 66% (Roebuck et al, 1975)
Energy 66% (Ayoub and Mital, 1989)
In athletics female record holders perform at between 80% and 90% of their male counterparts
  The problem with comparing averages is that they are based on a multitude of sampling and societal / environmental factors.

## Slide 29: Grip Strength
The “Kodak Book” has a table that shows the average percent reduction in Maximum Isometric Grip Strength to vary between 19% and 38%, depending on the type of gloves being worn.
.81 – .62
Try wearing a multilayered space suit glove, with a 4 psi differential pressure
Suzanne Rodgers (1986) “Ergonomic Design for People at Work” Van Nostrand Reinhold, New York
This leads to quicker fatigue or longer durations if the task can’t be changed

## Slide 30: Context Factors
Temperature
Lighting
Noise
Vibration
Altitude
(Gravity)
People adapt / acclimatize to moderate ranges of these factors, but at extreme levels performance declines rapidly
Physical and Cognitive

## Slide 31: Thermal Environment
Ideal temperature for sedentary activity 720 (22.50)
800 – Physical work output .50 – .60
550 - Hand dexterity .50 - .75
Woodson, Tillman and Tillman,1992

## Slide 32: Thermal Environment
Precise manipulation work lasting 3 hours
Temperature Performance
290 1.00
330 .75
35.50 .50
370 .25
(Astrand and Rodahl, 1977)

## Slide 33: Lighting and Task Time
Illumination (lux) 5000 10
Note taking (secs) 200 260 .77
Needle probing (secs) 54 70 .77
Micrometer reading (secs) 40 52 .77
Bennett et all (1977) in Sanders and McCormick, 1993

## Slide 34: Fitts Law
Tight targets take time
MT = a + blog2 (2D/W) (non linear)
  M = Movement time
  D = Distance Moved
  W = Target Width
  a, b are task related constants
    Object size, mass etc
Task difficulty
  Precise, Medium, Easy
  Object / Target Ratio, modulated by object size, mass
    0.1 to 1

## Slide 35: Training
Training (practice) has a very large effect on physical, motor skill and mental performance
  De Jong’s Law
Hence the experienced worker standard
But it may be expedient to expect less from untrained people while they ride their learning curve - LINE UNBALANCE
Values in the literature (Astrand and Rohdal,1977) range from .1 - . 5 – 1.00

## Slide 36: A Discounting Model

## Slide 37: Model Assumptions and Limitations
All variables are reduced to a common currency - discount
Relationships are linear, over the ranges of interest
Non linear loss functions will improve tool accuracy
Interactions are ignored; address the main variables
Other human, task, context or time variables may be substituted or added
This task analysis / design model focuses on physical tasks

## Slide 38: Conclusions
Engineers need work standards
  Small companies don’t have / use predetermined time standards
Ergonomists focus on constraints
  Human, Task, Context, Time
There is data in the literature to estimate the effects of constraints on performance
A discounting model is intuitive
It results in the engineer being able to design and improve task throughput by removing the feasible constraints
The model needs more development and field validation