## Slide 1: A Checklist on Checklists
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: What Are Checklists for?
Information
Diagnosis
Action
Which way do the arrows go?
We would hope that they go clockwise, but some people, with a limited set of actions, choose a diagnosis to suit their favorite action and then seek information to justify their diagnosis.
Doctors
Engineers
Scientists
Others

## Slide 3: A Plethora of Checklists
  There are probably more ergonomics checklists than ergonomists, some are related to outcomes, some to analysis, some to decisions and others directly linked to design. They vary widely in scope and format, and questions come in varying levels of quantification.

## Slide 4: The Context of Checklists
Outcomes
The
Operators
Analysis
The Job, Task
or Simulation
Design or
Intervention
Decisions
Protection
Performance
Preference

## Slide 5: The Focus of Checklists
Checklists can address any area of human activity and outcomes of that activity. The present discussion will focus on those factors that affect performance and protection in physical work.

## Slide 6: Outcomes
Health and safety
  Injury – acute incidents
  Illness – cumulative deterioration
    Incidents / # people / time
    Incidents / 100 workers / 2000 hours
    Incidents / 200,000 hours
  Severity
    Lost work days
Performance
  Effectiveness – accuracy – quality
    Defects / # products
    Pareto analysis of defect type
  Efficiency – speed – productivity
    Products / # people / time
    Products / 100 operators / year
Outcome assessment checklists should have clear units and accurate measurement protocols

## Slide 7: Job Satisfaction and Symptoms Surveys
Job satisfaction and symptoms survey checklists are volatile – they may be influenced by prevailing economic, social and political conditions. They may be useful but must be used in context and should be supported by more objective evidence before changes are made.
“Error” in such checklists may be addressed by careful question wording, broad sampling frames, large sample sizes and multiple replications over time.

## Slide 8: Symptoms Surveys
Where does it hurt?
How much does it hurt?
When did it start?
What caused it to hurt?
What have you done about it?
Responses are not part of the medical record until confirmed by a health care professional.
Symptoms surveys are a useful way of gaining information about the individual and larger groups of people.
Users of symptoms surveys must be cognizant of the possible biases in reported discomfort.

## Slide 9: The Purpose of Checklists
Compliance and enforcement
  Investigation and action thresholds
Intervention
  Finding – the easy part
  Fixing – useful for designers and engineers
Analytic
  The collection of data in order to investigate cause and effect relationships

## Slide 10: Levels of Checklist Questions
Qualitative
  Is the work beyond the capability of the operator?
Yes / no
  Is the weight greater than 10 lbs.?
  Have injuries been associated with this job?
Screening / intervention
  Is the weight greater than 10 lbs
    If so investigate contextual factors and outcomes
  Is the weight greater than 40 lbs
    If so provide some assistance
Complex
  Are the energy requirements of the job greater than 5 kcal/min?
  Are the operators conditioned? Is fatigue an issue?
  Can mechanization or additional manpower resolve the problem?

## Slide 11: Sliding Scales Alternative
Weight Response
  > 40 lbs Get a mechanical assist
  20 – 40 lbs Assign a selected operator
  Get a mechanical assist
  10 – 20 lbs Investigate the other factors
  Moments, frequency
  5 – 10 lbs Investigate the method of lifting
  1 – 5 lbs Investigate the frequency of lifting
  < 1 lbs Unlikely to be a problem
Questions on a sliding scale such as this imply that lighter is better but different investigation / resolution responses may be appropriate given differing contexts

## Slide 12: Usability of Checklists
What is the context of checklist application?
  User knowledge level
  Operational context
  Observation or instrumentation
Is the checklist
  Too short or too long?
    Is it useful? Will it get used?
  Comprehensive or focused?
    General physical work, MMH, work environment
  Intuitive – easy to use?
    Read, comprehend, complete

## Slide 13: More on Usability
Visual and motor factors
  Is the font clear and are the boxes big enough?
Do the questions flow in a logical manner?
Do the questions require supplementary instruments or calculations?
Are the questions unequivocal or are the instructions convenient and easy to use?
Is the checklist complete – does it require or refer to other data collection / communication media?
Are the responses collected in a way that is easy to translate into some decision or action?

## Slide 14: Reliability of Checklists
Checklists may be subjective or objective
In either case the results may be inaccurate or unreliable
If the checklist is applied by other observers to similar tasks with similar operators, will the results be consistent?
  These problems can be helped by user training, instructions and replication
Measurement error is a fact of life – checklist designers and users should comprehend error and plan for error avoidance or recovery.

## Slide 15: Replication
The methods of statistics exist to prevent you from jumping to conclusions based on insufficient evidence – such as small samples
To err is human and when humans measure humans human error is rampant!!
  To forgive is not helpful; To replicate is divine
Checklists should always use the power of replication
  Multiple job cycles
  Multiple occasions
  Multiple vantage points
  Multiple operators
  Multiple observers
  Repeated measures

## Slide 16: Validation of Checklists
Has the checklist been evaluated for:
  Scope and comprehensiveness?
  Relevance – pertinent questions?
  Ease of use?
  Reliability when used by different observers under the same and different conditions?
  Linkage to decisions and / or interventions?

## Slide 17: The Checklist Development Cycle
Theory
Data
Development
Team
Consensus
Managers
Developers
Customers
Users
The
Checklist
Experience
Usability
Evaluation
Verification
Validation
Implementation
Policy
Logic
Efficiency
Effectiveness

## Slide 18: Checklist Format – Manual or Electronic?
If the checklist is to be used at a worksite then the use of instrumentation and calculation should be minimized.
Generally univariate, round numbers or categories are the easiest to collect reliably.
Tables and charts are a quick way of embedding the calculation ( amalgamation of multivariate information) into the checklist / worksheet.
  RULA, NIOSH lift equation, thermal environment.
Electronic devices (e.g. PDAs) add a wide variety of opportunities to use complex calculations with simple inputs.

## Slide 19: Do’s and Don'ts in Checklist Design
Is the weight greater than 10 lbs?
How many Newton – meters does the operator apply per hour?
Is the distance between the edge of the table and the center of gravity of the object less than 25”?
Is the lifting moment greater than 250 in.lb?
What is the weight, horizontal distance, vertical height, distance lifted, type of coupling, asymmetry and frequency of lift?
What is the calculated NIOSH lift index?
Ask simple questions, do the calculations later, or better still incorporate the calculations in a look-up table

## Slide 20: Interactions
WRMSDs rarely occur because of one environmental stressor such as posture, force, repetition and individual susceptibility.
It is the interaction between these factors that is usually the problem.
But it is easier to measure the individual factors separately.
Simple charts embedded in checklists can be used to do the arithmetic of interactions.

## Slide 21: Interactions
1 1 2 5 10 20 40
2 2 4 10 20 40 80
5 5 10 25 50 100 200
10 10 20 50 100 200 400
20 20 40 100 200 400 800
40 40 80 200 400 800 1600
It is easy to create simple charts to do arithmetic
Pounds
Inches
Seconds
Repetitions

## Slide 22: Complex Questions Simplified E.G. Lift Moment
Horizontal (ins) 5 10 15 20 25
Weight (lbs)
5 25 50 75 100 125
10 50 100 150 200 250
15 75 150 225 300 375
20 100 200 300 400 500
25 125 250 375 500 625
Circle the Weight and Horizontal Distance and read off the Lifting Moment -

## Slide 23: Workload (lbs / hour)
Operations per Hour 5 10 20 40 60 120
Average
Load / Force
  1 5 10 20 40 60 120
  2 10 20 40 60 120 240
  5 25 50 100 200 300 600
  10 50 100 200 400 600 1200
  20 100 200 400 800 1200 2400
  40 200 400 800 1600 2400 4800
Estimate the average object load / force, count the operations per minute and use the table to calculate workload

## Slide 24: The Analysis of Work
The elements of work
  Equipment
  Tools
  Materials
  Environments
  Workspaces
  People
  Time
What can be changed?
  Equipment
  Tools
  Materials
  Environments
  Workspaces
  People
  Time
What should be measured?

## Slide 25: Reactive and Proactive Checklists
In most circumstances ergonomists are faced with situations where the change options are severely constrained.
  Equipment, materials, facilities and environments may be unchangeable for reasons of function or cost.
  The worker population may not be changed.
  Often the only feasible changes may be to the smaller tools, work place arrangements and the (temporal) assignment of duties.
Reactive checklists should focus on those factors that can be changed, other measures may only be of academic or long term value.
Where the ergonomist has the opportunity to change the more basic elements of work – the materials and major equipment – then the proactive checklist should focus on those factors.

## Slide 26: The Purpose of Checklists Revisited
If the checklist is about change then it should measure what can be changed.
If the checklist is about compliance or enforcement then it should comprehend the opportunities for change.
  It is conceivable that ceilings could be painted before they are erected but an acceptable solution may be to add an extension to the paint brush; The same goes for agriculture!
  The traveling public wish to take with them large suitcases, the options for the airlines are to introduce baggage handling processes that eliminate manual lifting.
  The supermarkets make great use of the bar codes on the variable sized products and also need to be competitive in customer throughput – automation worked in the banking industry!

## Slide 27: The Scope and Content of Work Analysis Checklists
Job, product or service classification
Spatial factors
Force factors
People factors
Exposure factors
Linkage to outcomes and interventions
Communication and prioritization

## Slide 28: Job, Product or Service Classification
Essential elements:
  Date, job code, product code, location, observer, reference number.
Optional elements.
  Similar jobs, operator / team characteristics, associated data / records, supporting material etc.

## Slide 29: Spatial Factors (Those Factors in the Work Environment That Can Be Changed)
Reference point (must be repeatable)
  Point on the floor between the ankles
Three dimensional space
  Height, horizontal distance, lateral offset
Orientation
  In front, on top, R/L side, under, behind
Interface
  Grip type as quantified by surface area of contact

## Slide 30: Spatial Factors (Record Those Dimensions That the Engineer Can Change)
H
RS
F
U
B
T
V
L
R

## Slide 31: Interfaces
Full grasp, pinch grip, pulp grip etc.
Use square inches.
  Length x breadth of total contact area.
  Length x circumference of a handle.
1 2 5 10 20 40 60
Bad
Square Inches
Good
1 2 3 4 5
1 2 3 4 5
2 4 6 8 10
3 6 9 12 15
4 8 12 16 20
5 10 15 20 25

## Slide 32: The Posture Problem
It is very difficult to measure posture accurately
The engineer cannot change the operators posture, he/she can only change those workplace factors that affect posture
Measuring posture is probably a waste of time

## Slide 33: Try Estimating These Postures (These Jobs Are All Associated With WRMSDs)
Try measuring posture!

## Slide 34: If You Must Measure Posture Try Using Stick Figure Comparisons

## Slide 35: But!
Can you really tell the difference between hip angle and lumbar spine angle?
Can you measure shoulder girdle elevation and scapular rotation?
Can you measure the combined wrist flexion / ulnar deviation angle?
Can you measure the effect of anthropometric variation on joint angle?
Remember, ergonomists should measure what they can change

## Slide 36
Spatial Factors (Record Those Dimensions That the Engineer Can Change)
H
RS
F
U
B
T
V
L
R

## Slide 37: Movement
Movement (rather than posture) is what causes harm.
But movement is much more difficult to measure than posture.
  It has elements of multiple joints, directions, speeds, accelerations and jerks.
Ballet choreographers use the Laban notation.
Physical therapists describe “functional patterns.”
The UofMichigan HUMOSIM project measures and models empirical motions.
How can engineers affect human movement except by changing the spatial arrangements of objects?

## Slide 38: How Should We Describe Movement? (Use the Richness of Language)
Bending
Slight Extreme
Stooping
Bending
Squatting
Reaching
Twisting
Pulling
Pushing
Holding
Carrying
Lifting
Walking
Climbing
Etc.
Quantify these movements with verbal descriptors
Superimpose verbal limits
Use diagrams / scales / physical units to quantify the movement
Ankle + Knee + Hip Angle
0
300
Pushing 40 lbs at 100 ft / min

## Slide 39: Force Factors
Damage to the musculo-skeletal systems usually involves the application of force or an attempt to change the effect of an external force, such as gravity or a moving or vibrating object.
Interactions with force.
  Pressure – force x surface area.
  Moment – force x distance from joint center.
  Work – force x distance moved.
  Direction of force.
    Human strength varies considerable with the direction of force application.
  Time.
    Local and general fatigue.
      Human strength varies considerably over time.
  People vary greatly in their strength capabilities.

## Slide 40: Simple Force Factors
Weight action and maximum permissible limits.
  10, 25, 40, 70….?
  It all depends…
  But the designers of weights do not always know the conditions of handling!
  So it may be appropriate to set simple weight limits.
Force.
  Pushing, pulling, pinching, manipulating.
  The designer of the required force often does know the conditions of force actuation.
  It may therefore be appropriate to set force limits based on the context.

## Slide 41: Interactions With Force
Force (Weight)
1 2 5 10 25 50 100
Interface (sq ins)
Moment arm (inches)
Distance moved (feet)
1 1 2 5 10 25 50 100
2 2 4 10 20 50 100 200
5 5 10 25 50 125 250 500
10 10 20 50 100 250 500 1000
25 25 50 125 250 625 1250 2500
50 50 100 250 500 1150 2500 5000
100 100 200 500 1000 2500 5000 10000
This interaction table helps with the calculations, the matter of limits will be discussed later

## Slide 42: Force (Weight) x Time
Force / Weight (lbs)
1 5 10 25 50 100
Repetitions (per hour)
Static Durations (secs)
% Job Cycle
1 1 5 10 25 50 100
2 2 10 20 50 100 200
5 5 25 50 25 250 500
10 10 50 100 250 500 1000
25 25 125 250 625 1250 2500
50 50 250 500 1250 2500 5000
100 100 500 1000 2500 5000 10000
This interaction table helps with the calculations, the matter of limits will be discussed later

## Slide 43: The Exposure Problem Interactions with Time
Repetitions, frequencies
Durations, work – rest schedules
  Static postures and exertions
  Percent of job cycle
  Length of the shift or work day
  Length of a “rotation”
  Days, weeks, months, years on the job
The same or similar activity in and out of work
  Home computers, hobbies
The complicating competition between the training effect and the cumulative deterioration effect

## Slide 44: The Time Dimension
Activity Forces and Postures
Maximum values
Cycles Minutes Hours Days Weeks Months Years
Fluctuating Demands

## Slide 45: Exposure Based Checklists
Postural and/or Force Demands
Exposure (Time): 1 5 10 25 50 100
1 1 5 10 25 50 100
2 2 10 20 50 100 200
5 5 25 50 25 250 500
10 10 50 100 250 500 1000
25 25 125 250 625 1250 2500
50 50 250 500 1250 2500 5000
100 100 500 1000 2500 5000 10000

## Slide 46: Force (etc.) and the Individual
People vary enormously in strength capability due to inheritance, sex, age, ethnicity, handicap, training, fatigue etc.
  There may be a 10 fold difference on any force dimension to individuals.
It is feasible to select individuals or groups to do different jobs based on their capabilities.
  Self selection, seniority.
  Fitness for duty testing.
    Formal.
    Casual.
The setting of standards for force limits must comprehend the target population or individual characteristics.
Where assumptions can be made about the population characteristics then it will be necessary to superimpose percentile accommodation levels – a policy matter – in the process of standards setting.

## Slide 47: Individual and Population Factors
People vary - the normal distribution is a very powerful staring point.
Data exists on population characteristics on a variety of dimensions.
Percentile accommodation is a matter of policy, not ergonomics.
Policy may be set by managers and politicians with the help of experts or it may be negotiated.
Ergonomics, job standards, percentile accommodation are inextricably mixed.

## Slide 48: Another “Percentile” Problem
People vary differently on all dimensions.
A 50th percentile stature will not necessarily have 50th percentile segment lengths, girths, strength or stamina.
The “percentile” is dimension specific!

## Slide 49: The Policy Problem
- +
Highly selected (and paid) populations
High level of “protection”
Any simple or complex design dimension
The realistic decision region

## Slide 50: Different “Policy” for Different Dimensions? (Percent Accommodation)
Protection Selection
Safety critical 99.99 99.9
Fit 99 50
Reach 95 50
Strength 90 10
Stamina 80 5
Skills 70 10
Sight 50 10
Etc. ? ?
These numbers are meant to generate discussion, not initiate policy!!

## Slide 51: The Liberty Mutual (Snook) Tables
Psychophysically derived and statistically smoothed tables indicating percent of adult population capable of performing various manual handling and manipulative tasks.
Very useful.
But what percent level should I choose?

## Slide 52: Setting Standards (Decision Thresholds)
Standards are useful – they resolve ambiguity.
Round numbers are easy to deal with and, because of the pervading people, situational and temporal variability, round numbers are sufficiently accurate.
Compliance, investigation, action and maximum permissible limits.
  It’s important to know why a standard is being set!

## Slide 53
Rule Based Ergonomics Common Currency
Black Intolerable
Purple Unacceptable
Red Undesirable
Orange Marginal
Yellow Tolerable
Green Acceptable
White Ideal
All Human Factors Communications use the same “currency”

## Slide 54: The Decision Graph
Measure of something that can be changed
Probability of Failure
Region of Uncertainty and Interactions
Region of no concern
Region of no dispute
Lines in the sand
Black
White

## Slide 55: The Consensus Approach to Standards Setting
Science
History
Experience
Data
Predictions
Risk
Statement
Standard
Implementation
Customer “buy in”
Government / Management Policy
(e.g safety has absolute priority, accommodate 95%
Standard
Management
Endorsement
Evaluation Validation Verification Sensitivity
Consensus Ergonomists Engineers Customers

## Slide 56: The Usefulness of Common Currency
The “gold standard” is a traditional (but not universally accepted) financial comparison.
Ergonomist develop scales of “goodness” and “badness.”
Verbal scales are useful:
  Ideal, acceptable, tolerable, unacceptable, intolerable.

## Slide 57
Colors
Width
Height
B
P
R
R
P
B
R
P
B
R
P
B
R
R
R
R
P
P
P
P
B
B
B
B
>80
75-80
70-75
60-70
B
P
P
P
B
B
B
B
B
55-60
50-55
50
O
Y
G
W
G
G
Y
O
Y
Y
O
O
O
O
O
R
25
20
<20
50
45
40
30
>

## Slide 58
Graphical Analysis
For Interacting Variables
Frequency / hour
Other Workplace Factors
Weight
120
40
10
20
Awkward Posture
Good Posture

## Slide 59
Example of Interactions with Time (Exposure)
Weight
Frequency (Movements / Hour)
<10
B
P
R
R
P
B
10-15
R
P
B
15-20
R
P
B
20-30
R
R
R
R
P
P
P
P
B
B
B
B
<1
1-5
5-10
10-20
30-40
B
P
P
P
B
B
40-50
B
B
B
>50
20-30
30-40
>40
O
Y
G
W
G
G
Y
O
Y
Y
O
O
O
O
O
R

## Slide 60
Counting
For Independent Variables
Number of Variables
1 2 3 4 5
Black B B
Purple P P B
Red R R P B
Orange O O R R P
Yellow Y Y O O O
Green G G G Y Y
White W W W W W
E.G Load, Target Size, Temperature ….

## Slide 61: Usability Revisited - TLVs
TLVs (threshold limit values) are convenient for.
  Design, compliance, enforcement.
TLVs have stood the test of time in the equally variable areas of the physical and chemical environment.
Because of the underlying variability TLVs will never be absolutely (deterministically) predictive of outcomes.
TLVs in ergonomics, if set by an appropriate consensus with due regard to the available evidence, will greatly improve the “usability” of our science.

## Slide 62: Weightings and Decisions
In reality, some factors are more important than others and some interventions are more feasible than others so we must address the “weighting” of evidence issue and the decision processes that lead to alternative interventions.
Weighting can be achieved in two practical ways:
  Setting questions in various zones of a common currency spectrum.
  Adding a multiplier to certain questions depending on the context.
There is the counter argument that attempts to introduce weightings into checklists unnecessarily complicate the process.

## Slide 63: Linkage to Outcomes
Ergonomics analysis checklists should link some designed variable to some prediction of outcome. – The more direct the link the better.
  Indexes are OK but do not help the individual analyst or designer (investor).
The linkage to outcomes directly will always be probabilistic.

## Slide 64
The Context of Checklists
Outcomes
The
Operators
Analysis
The Job, Task
or Simulation
Design or
Intervention
Decisions
Protection
Performance
Preference

## Slide 65
Checklist Content
Purpose Compliance Intervention
Scope Physical Information Environment Organization
Classification Job Date Analyst Reference
Spatial Vertical Horizontal Orientation Interface Access
Posture Back Neck Shoulder Wrist
Movement Range Direction Speed Acceleration / Jerk
Force Weight Normal Force Friction Inertia
Exposure Repetitions Static Duration Shift Length Weeks/Months/Years
Interactions
Spatial x Force Moments Torque Pressure Work
Spatial x Exposure Static Posture x Duration
Force x Exposure Weight / Hour
Complex Index NLI RULA Strain Index Repetition Index
Other Factors
Environmental Thermal Light Noise Vibration
Information Sensory Attention Memory Decision
Organizational Autonomy Pacing Teams Training
Circle all that apply to your checklist
Consider omissions and additions
Add notes where necessary

## Slide 66: Checklist Format and Context
Measurement Subjective Objective Nominal Ordinal Interval Complex Indices
Conditions Shop floor Video Instruments Replications
Accommodation Policy % ADA Seniority Job Assignment
Observer Training Experience Qualification
Outcome linkage Injuries Quality Cost Productivity
Communications Counts Sums Index Profile Risk
Evaluation Content Users Time Errors Acceptance
Consensus Ergonomists Engineers Managers Customers
Circle all that apply to your checklist
Consider omissions and additions
Add notes where necessary

## Slide 67: Conclusions
Ergonomics checklists are useful for both compliance and design.
Checklists should be simple.
Charts can help with the analysis of interactions.
Checklists should measure those things about the job that can be changed.
Checklists need reliable measurement and consensus policy.