## Slide 1: Train The Trainer OH Master Class For Ergonomics: Introduction to Mechanics Professor Brian Peacock

## Slide 2: Introduction
Work in pairs or small groups
Have plenty of paper and colored pencils available
A protractor and compass would be useful
Have access to some coins, a tape measure and a stop watch
Have access to the Internet
This module will address:
  Movement
  Force
  Moments
  Pressure

## Slide 3: Location
The location of an object may be described by Cartesian or Polar coordinates
Cartesian coordinates describe an object’s location by reference to its distance in one two or three dimensions (x, y, z) from a reference point (the origin)
Place a coin on a sheet of paper and describe (sketch) its location (in two dimensions) with reference to the bottom left hand corner of the paper
Place your hand on the table in front of you and describe (sketch) its location by reference to a point on the floor between your ankles (hint: use multiple two dimensional sketches)
Polar coordinates describe the location of an object using trigonometry concepts such as sines, cosines and tangents and distances
Search the Internet for trigonometric tables
Repeat the Cartesian coordinate exercises using Polar coordinates

## Slide 4: Movement
Movement is the change in location of an object
Velocity is the movement distance divided by time
Acceleration is the rate of change of velocity
Draw pairs of targets at different distances apart on your paper
Move a coin between a pair of targets
Draw a velocity – time diagram; discuss and describe the acceleration / deceleration phases
Repeat the movement ten times; calculate the average velocity
Repeat the exercise with different size and spacing of the targets; how do these variables affect the times?
Measure the width (length) of the room; walk from wall to wall ten times; calculate your average velocity
A car assembly line is moving at 3kph, the components are placed in baskets placed one meter from the line and the fastening (attachment) operation takes 30 seconds; develop an annotated sketch to describe the movements (distances, directions and times) of the operator

## Slide 5: Angular Movement
Angular velocity is described by the number of degrees (or radians) per second.
What is the difference between a radian and a degree?
Estimate the changes in the angle of your knee during a gait cycle
Sketch (sagittal plane) angle-time diagrams for walking and running
Sketch sagittal, frontal and horizontal plane angle time diagrams for throwing
Sketch angle time and angular velocity – time diagrams for the arm (shoulder) of a supermarket checkout clerk.
Repeat the exercise for the clerk’s wrist joint

## Slide 6: Shape and mass
The human body is comprised of multiple segments; consider the head as a sphere, the trunk as a cylinder, and the arms and legs as two truncated cones (forget the hands and feet)
Measure (approximately) and sketch the segments on your partner
Create sketches of the segments and calculate the volume, mass (kg) and center of mass of each segment and the overall center of mass of the body

## Slide 7: Force
Force is mass times acceleration
Weight is the mass of an object times the acceleration due to gravity
Force changes the motion of an object
A vector diagram can be used to resolve a force into its orthogonal (e.g. horizontal and vertical) components with the length of the vector representing the component of force in a direction calculated by taking the sine (cosine) of the original direction.
Develop a (simple) vector diagram for riding a bicycle up a hill
Static equilibrium exists when all the (orthogonal) forces acting on an object “cancel each other out”
Have a three person tug of war; describe the (2 dimensional) horizontal forces if no one moves.

## Slide 8: Moment (of force)
A moment is force times distance from a fulcrum
A moment is measures in Newton meters
Why is it easier to lift an object close to your body than with outstretched arms?
Discuss and develop an annotated sketch to describe the shoulder muscle (deltoid) force needed to hold an object at arms length
In this example what happens to the body’s center of mass? (Why? How?)
Develop a sketch of the distances and forces involved in bending over and lifting a box from the floor
Discuss how the moment is changed by changing the force or the distance with reference to common ball games using racquets, clubs or bats

## Slide 9: Levers
In a class one lever the fulcrum is between the load and the effort
In a class two lever the load is between the fulcrum and the effort
In a class three lever the effort is between the load and the fulcrum
Discuss and sketch these three different types of lever by sketching various anatomical / biomechanical functions
Discuss and sketch the principles of moments and levers with regard to manual materials handling, tools, tool handles and triggers

## Slide 10: Pressure
Pressure is force times area; it is measure in Newtons / m2
Use sketches and numerical estimates to analyze the following situations:
Compare pressing the pointed end of your pencil and the top end
How does a knife work?
Why do back packs have wide straps?
Why do suitcases have wide handles?
How much pressure is there on a lumbar spine disc when you are standing or sitting upright?
How do ballet dancers go “en pointe?”
Describe the biomechanical pressure challenges of hand tool handles and triggers
What is the body’s response to pressure?

## Slide 11: Reflections
An understanding of mechanical principles is essential for an understanding on occupational biomechanics
Mechanical principles are usefully described by sketches and functional anatomical exercises.
People vary considerably in their size, strength, stamina and skill and this variation affects their ability to perform physical tasks and their vulnerability to mechanical injury