## Slide 1: Posture and Motion Analysis
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: Posture
Holding a fixed position against gravity with or without other external support
The relative position of adjacent limb segments in a defined plane
Base Posture - Standing, Sitting, Lying, Leaning, Kneeling, Squatting etc..

## Slide 3: Posture Exercise
Get in groups of 3, two sit back to back, the other observes
Describe your present posture in sufficient detail so that your partner can repeat it
Third person judges accuracy of communication and records the use of language and quantification in posture description

## Slide 4: Posture and Gravity
Balance
Line of Gravity
Dynamic Stability
Muscles and Tendons
Base - External Interfaces

## Slide 5: Posture and Gravity Exercise
Sit on chair
Replicate posture without chair
Stand on toes
Stand on one foot
Hold weights with outstretched arms

## Slide 6: Movement
Joint Movement - The angular displacement of one segment relative to an adjacent segment in a defined plane
Functional Movement - The (curvi)linear movement of a body part (e.g.. the hand) resulting from the combined angular movements of multiple joints

## Slide 7: Movement Exercise
Move single joints in defined planes, estimate range of motion
Vary adjacent joint position and repeat previous exercise
Perform functional movement, describe multiple joint motions
Most muscles pass over two joints

## Slide 8: Postural and Motion Planes
Saggital Plane - The plane parallel to the one which cuts the body into right and left halves
Frontal Plane - The plane which divides the body into front and back portions
Horizontal Plane - The plane which separates the body into upper and lower (proximal and distal for limbs) portions

## Slide 9: Movement Plane Exercise
Stand facing partner
Observe bony references for movement planes
Move different joints / segments through full range of motion in defined planes
Discuss anatomical and functional movements

## Slide 10: The “Anatomical” Position
Stand upright, feet together, palms facing forward
Exercise
  Adopt “anatomical” position
  Describe individual joint postures

## Slide 11: Classical Joint Movements
Flexion and Extension
Abduction and Adduction
Medial and Lateral Rotation
Circumduction
Supination and Pronation
Radial and Ulnar Deviation
Opposition
Inversion and Eversion
Sliding
Measure Range of motion in each plane
  Saggital
  Frontal
  Horizontal

## Slide 12: Joint Movement Exercise
Perform and list all possible movement and ranges for the following joints:
  Fingers and Thumb (I/P, M/P)
  Wrist, Forearm, Elbow
  Shoulder and Shoulder Girdle
  Head, Neck, Thoracic Spine and Lumbar Spine
  Hip, Knee and Ankle

## Slide 13: Factors Affecting Movement Direction and Range of Motion
Joint Surface Shape
Ligaments
Muscles and Tendons
Soft Tissue Contact
The Position of Adjacent Joints
Clothing

## Slide 14: Range of Motion Exercise
Compare ROMs for
  Wrist, Elbow, Shoulder, Knee, Hip, Spine
Examine joint surface shapes on skeleton
Examine muscle, tendon and ligament relationships with joints
Describe soft tissue contact effects
Investigate adjacent joint position effects

## Slide 15: Pattern Movements Oblique with Rotation
Flexion, adduction, external rotation
Extension, abduction, internal rotation
Flexion, abduction, external rotation
Extension, adduction, internal rotation

## Slide 16: Pattern Movement Exercise
Perform each oblique pattern with arms and legs
Repeat and include head, neck and trunk movements

## Slide 17: “Good” and “Bad” Posture
Joints in mid range
Joints at right angles as in upright sitting
A comfortable position
An upright stretched posture
“The only good posture is the next posture” - people are dynamic organisms

## Slide 18: Good and Bad Posture Exercise
Adopt comfortable standing, TV viewing, computer operation, squatting and kneeling postures
Hold each posture for one minute
Describe sensations of comfort / discomfort
What is a good posture?

## Slide 19: The Measurement of Joint Angles
Goniometry
  Mechanical
  Electrical
  Optical / video
Define plane of interest
Identify two bony points on adjacent bones
Use mechanical goniometer (protractor)

## Slide 20: Joint Angle Measurement Exercise
Form groups of 3
Mark bony points on limbs, head and trunk (two for each segment) on one subject
Adopt snap shot of typical working posture
Describe planes of movement for joints of interest
Each observer should independently apply goniometer and measure and record joint angle
Compare results

## Slide 21: Pitfalls in Joint Angle Measurement
Individual differences in size and body build
Joint centers of rotation move
Inconsistent planes and reference points
Clothing
Precision, accuracy, repeatability
Repeat previous exercise using two subjects in “identical” postures
Each observer repeats his / her own measurements
Describe causes of discrepancies between observers and between subjects in “same” posture

## Slide 22: Multiple Joint Angle Measurement
Video methods - Peak, Selspot, Expert Vision, Vision 3000 etc.
Subjective judgment and categorization into approximate ranges - e.g.. Greater than 20 degrees
http://www.c-motion.com/products/visual3d/Visual3DOverview.htm

## Slide 23: Trunk Motion Measurement
Lumbar Motion Monitor
Electrogoniometer
Small, medium and large sizes
Fitting
Segment mass and load inputs
Kinematic and kinetic outputs
Predictive equation for risk of injury
http://www.askaphysio.com/services.htm

## Slide 24: Motion Analysis Parameters
(Curvi) linear motion
Rotations at individual joints
Displacement - position, angle, range
Velocity - change in position over time
Acceleration - change in velocity over time
Jerk - sudden changes in acceleration

## Slide 25: Angle - Time Diagrams
Time
Flexion
Extension
Joint
Angle
Variable
Maximum
Range

## Slide 26: Velocity-Time Diagrams
Time
Velocity (angular)
Acceleration
Deceleration

## Slide 27: Angle - Angle - Time Diagrams
Flexion
Extension
Flexion
Extension
Joint 1
Joint 2

## Slide 28: Angle - Angle - Time Diagrams
Joint 1
Joint 2
F
E
E
F

## Slide 29
Angle - Force - Time Diagrams
Joint 2
F
E
Angle
Force
Time

## Slide 30: Motion Analysis Exercise
Draw Angle - Time Diagrams for single and multiple joints during:
  Walking
  Lifting and Carrying
  Operating Hand Tool

## Slide 31: Advanced Motion Analysis Exercise
Use the above techniques to describe:
  De-palettizing
  Attaching heat shield under vehicle
  Tying your tie or shoe lace
  Performing a gymnastic, athletic or recreational activity

## Slide 32: Conclusions
How precise, accurate, repeatable and useful are posture and motion measurements?