## Slide 1: The Spatial Aspects of Work
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: Soyuz capsule
For launch and landing astronauts are strapped into their body molded reclining seats.
The controls are out of reach
They are given a little stick with which to press the buttons

## Slide 3: Rounded English – Metric Conversions
Inches | Centimeters |  | Centimeters | Inches |  | Pounds | kg |  | kg | Pounds
5 | 13 |  | 10 | 4 |  | 5 | 2 |  | 2 | 4
10 | 25 |  | 20 | 8 |  | 10 | 5 |  | 4 | 9
15 | 38 |  | 30 | 12 |  | 15 | 7 |  | 6 | 13
20 | 51 |  | 40 | 16 |  | 20 | 9 |  | 8 | 18
25 | 64 |  | 50 | 20 |  | 25 | 11 |  | 10 | 22
30 | 76 |  | 60 | 24 |  | 30 | 14 |  | 12 | 26
35 | 89 |  | 70 | 28 |  | 35 | 16 |  | 14 | 31
40 | 102 |  | 80 | 31 |  | 40 | 18 |  | 16 | 35
45 | 114 |  | 90 | 35 |  | 45 | 20 |  | 18 | 40
50 | 127 |  | 100 | 39 |  | 50 | 23 |  | 20 | 44
55 | 140 |  | 110 | 43 |  | 55 | 25 |  | 22 | 48
60 | 152 |  | 120 | 47 |  | 60 | 27 |  | 24 | 53
65 | 165 |  | 130 | 51 |  | 65 | 30 |  | 26 | 57
70 | 178 |  | 140 | 55 |  | 70 | 32 |  | 28 | 62
75 | 191 |  | 150 | 59 |  | 75 | 34 |  | 30 | 66
80 | 203 |  | 160 | 63 |  | 80 | 36 |  | 32 | 70
 |  |  | 170 | 67 |  | 85 | 39 |  | 34 | 75
 |  |  | 180 | 71 |  | 90 | 41 |  | 36 | 79
 |  |  | 190 | 75 |  | 95 | 43 |  | 38 | 84
 |  |  | 200 | 79 |  | 100 | 45 |  | 40 | 88
 |  |  |  |  |  |  |  |  | 42 | 92
 |  |  |  |  |  |  |  |  | 44 | 97

## Slide 4: Anthropometry

## Slide 5: Anthropometry Measures
Stature
Segment lengths
Widths
Girths
Weight
Body Mass Index
Somatotypes

## Slide 6: Body Mass Index and Health Risk for Singapore (MARCH 16, 2005)
BMI (kg/m2) for Adults | Health Risk
27.5 and above | High Risk
23 – 27.4 | Moderate Risk
18.5 – 22.9 | Low Risk (healthy range)
Below 18.5 | Risk of nutritional deficiency diseases and osteoporosis

## Slide 7: Somatotypes (William Sheldon (1898-1977)
Rate yourselves and your colleagues on 1-7 scales (1 low, 7 high) on each dimension – the “average person” would be a 4-4-4

## Slide 8: Drillis and Contini estimates of segment lengths based on stature

## Slide 10: Statistics

## Slide 11: Anthropometric Data based on Drillis and Contini Ratios From USA stature data (Sanders and McCormick)
 |  | 5th Percentile |  | 50th Percentile |  | 95th Percentile | 
 |  | Male | Female | Male | Female | Male | Female
 | Proportion | 163.6 | 151.1 | 175.3 | 161.8 | 187 | 172.2
Stature | 1 | 64.4 | 59.5 | 69.0 | 63.7 | 73.6 | 67.8
Ankle | 0.039 | 2.5 | 2.3 | 2.7 | 2.5 | 2.9 | 2.6
Foot Length | 0.152 | 9.8 | 9.0 | 10.5 | 9.7 | 11.2 | 10.3
Foot Breadth | 0.055 | 3.5 | 3.3 | 3.8 | 3.5 | 4.0 | 3.7
Knee | 0.285 | 18.4 | 17.0 | 19.7 | 18.2 | 21.0 | 19.3
Crotch | 0.485 | 31.2 | 28.9 | 33.5 | 30.9 | 35.7 | 32.9
Hip | 0.53 | 34.1 | 31.5 | 36.6 | 33.8 | 39.0 | 35.9
Navel | 0.63 | 40.6 | 37.5 | 43.5 | 40.1 | 46.4 | 42.7
Shoulder | 0.818 | 52.7 | 48.7 | 56.5 | 52.1 | 60.2 | 55.5
Eye | 0.936 | 60.3 | 55.7 | 64.6 | 59.6 | 68.9 | 63.5
Upper Arm | 0.186 | 12.0 | 11.1 | 12.8 | 11.8 | 13.7 | 12.6
Forarm | 0.146 | 9.4 | 8.7 | 10.1 | 9.3 | 10.7 | 9.9
Hand | 0.108 | 7.0 | 6.4 | 7.5 | 6.9 | 8.0 | 7.3
Arm | 0.44 | 28.3 | 26.2 | 30.4 | 28.0 | 32.4 | 29.8
Trunk Shoulder to Hip) | 0.288 | 18.5 | 17.1 | 19.9 | 18.3 | 21.2 | 19.5

## Slide 12: Typical Anthropometric Data
 | Percentile |  |  | 
 | Male |  | Female | 
Measurement | 95 | 5 | 95 | 5
1. Forward Reach | 26.9 | 24.0 | 25.1 | 22.2
2. Elbow Height | 44.6 | 39.5 | 41.5 | 36.1
3. Knuckle Height | 31.0 | 27.2 | 28.6 | 24.8
4. Shoulder Height | 60.1 | 53.2 | 55.8 | 48.8
5. Eye Height | 68.4 | 60.9 | 63.7 | 56.0
6. Stature | 73.2 | 64.4 | 67.7 | 59.5
7. Overhead Reach | 84.8 | 75.2 | 78.8 | 69.2

## Slide 13: Workplace Design

## Slide 14: You can change posture by changing the work environment

## Slide 15: In the 1970s I developed the “box”
Shoulder height of the 5th percentile female
Knuckle height of the 95th percentile male
Forward functional reach of the 5th percentile female
Elbow width

## Slide 16: The box can be very simple to remember
30/75(20/50 for sitting)
50/125
(40/100 for sitting)
25/65
25/65
It is very useful for many practical purposes

## Slide 17: More on “the box”
It deals with both back, leg and arm posture
It is in the design domain - it does not measure posture
It’s zones are
  Hand(s) inside the box
  At the edge of the box
  Outside the box
  Outside the box in two dimensions
You can add time to the discussion
  5 secs, 10 secs, 50% of job cycle etc
The corners may be an issue - so round them!
The box moves to the sitting base posture

## Slide 18: How high should a computer screen be?

## Slide 19: How high should a work bench be?
Close visual work
Elbow height - the rule of thumb
Heavy work

## Slide 20: Whose Elbow are we Talking About?
5%
10%
50%
95%
99%

## Slide 21
More Rules of Thumb
5%
10%
50%
95%
99%
Fit
Reach

## Slide 22: How much headroom should there be in the back seat of a sports car?

## Slide 23
To Reach, Raise or Tilt?
Cars and trucks need gas tanks, fuel lines, brake lines, exhaust pipes and heat shields etc. - they are generally located on the underbody.

## Slide 24: To Reach, Raise or Tilt?
  Overhead work can be a pain, but you can work overhead for short periods without any untoward effects. - what about 1/3 of the job cycle?
  On frame vehicles - trucks - much of this work is done with the frame rotated
  It may be better to build up a sub assembly and use automation to raise it up
  Another alternative is to tilt the vehicle - 30o, 450, 60o or 90o
  $$$$$$$$$$$$$$$$$$$$$$$$$$$$$$$$$$$$

## Slide 25: Beyond Fit and Reach Location to Orientation
The body works by first moving to the point of interest, adjusting the base posture and then using the arms, wrists and fingers to fine tune.
Under
In Front
Behind
On Top

## Slide 26: Orientation Problems cause Posture Problems that Interact with Force and Time
Under
In Front
Behind
On Top

## Slide 27: Posture, Force and Time
Get Carry Insert Walk Rest
Time
Force = f(Person, Posture, Time, Interactions etc.)
Fmax
varies
too
Posture = f(Location, Orientation)

## Slide 28: Grasping and Manipulating
Fingers have postures too
How big are your hands?
How big should handles be?
How big should keyboards be?
Length, Width, Circumference, Shape

## Slide 29: The Theater and Stadium Problem
X = ?
Y = ?

## Slide 30: Seat Width – measure the MRT seats
Hips, Shoulders, Elbows, Clothes, Bags and Personal Space
W = ?

## Slide 31: Rules of Bum
“It was normal to erect temporary viewing stands (bleachers) along the route in London of a royal procession. The official directive to the builders of stands was, for some centuries, to allow 18” for each aristocratic behind and 17” for commoners.” - the Toronto Transit Commission chose 17” for their subway.
The rules brought to the table for the Hong Kong Mass Transit design were 16” to the bum, 16 bums to the ton”

## Slide 32
The Storage Problem
Racks
Pallets
Containers
Space
$$$$$$$
Moments and Moments
How many bottles of beer in a pack?

## Slide 33: Question “it all depends……”
Should we set weight limits for packages or should we wait until we can analyze the conditions of manual materials handling?

## Slide 34: Storage Rack Guidelines

## Slide 35: Racks
10
20
30
40
50
60
70

## Slide 36: Questions
How close should you sit to the air bag?
How long are your arms?
How long are your legs?
Are these lengths correlated?
What seat back angle do you prefer?
How much do you tilt your wheel
Should we have adjustable pedals?

## Slide 37: Fitting Trials
First we use anthropometry to get to the ball park
Then we design an adjustable physical mockup
We bring in a representative sample of subjects to adjust the mockup to their liking as they go through a series of functional trials
We use an appropriate experimental design and psychophysical methods of adjustment
  method of limits, just noticeable differences
Sometimes the anthropometric evidence and the fitting trials evidence don’t match - why?

## Slide 38: Ergonomics Contributions to the Design of the Hong Kong Mass Transit Railway
Compare the Singapore MRT

## Slide 40: The Opportunities
Passenger Compartment
  Seats
  Grab Rails
  Entry / Egress
Operators Cab
  Seat
  Instrument Panel
Emergency Systems
Thermal Environment
Control Room Design
Turnstiles
Transport for the Handicapped

## Slide 41: The Passenger Compartment
Short Journeys, Most Passengers Stand
Maximize Pay Load, Stability and Mobility
Get 25 Passengers On and Off in 25 seconds

## Slide 42: The Seat Design
Aluminum, Scalloped Seats
Seat Centers - 500 mm (19.7”)
Seat Height - 400 mm (15.7”)
Seat Depth - 380 mm (15”)
3 degrees upward inclination of seat surface
Lumbar Curve - 230 mm (9”) 250 mm (9.8”) radius
Head contact with side wall and encroachment on standing area / capacity

## Slide 43: The Seats
96 “ (2438 mm)
How many passengers per seat?
  5 - Anthropometry - elbow width -19.9” (500mm)
  6 - Traditional Rules - 16” (406 mm)
  7 - Fitting Trials - 13.7” (348 mm)

## Slide 44: The Fire Department and the Transportation Department
Hot aluminum gives of noxious fumes
Helicopter pad material for floors
Stainless steel seats, no padding, no scallops
  Sometimes cold
  Sliding
  Easy to clean
  Durable
Stainless steel grab rails

## Slide 45: Grab Rails
Reach for short passengers (including children)
Fit (for tall passengers - head clearance)
Horizontal Bars (above the seats)
  3” set back
Vertical Poles
Straps

## Slide 46: The Grab Rails
Criteria:
  Accessibility
  Stability
  Mobility
  Safety
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Clusters
Pathways

## Slide 47: Entry / Egress
Headway
Dwell time
Passenger flow through doors
Physical mock ups (Bamboo)
Timed Trials
  Old, Young, Big, Small, Packages, etc.

## Slide 48: Operator’s Cab
Seat
Entry - Egress (Every 90 seconds)
Control Panel
  Brake, Speed Control
  Communications
  Doors
  Emergency Stop
  Lighting and Thermal Environment
Coffee Cups

## Slide 49: Operator’s Seat
Sitting
Flip Up - Standing - Emergency and Routine Exit
Padded Front Edge
  Most Common Posture
Monks, Sit Stand, Hip Angle and Pelvic Tilt

## Slide 50: Conclusions
Ergonomics starts with Anthropometry
Then it deals with all the other human characteristics
Sometimes there are conflicts and tradeoffs
Always we must deal with variability
If it isn’t design it isn’t ergonomics

## Slide 51: Design Exercise
Measure the seat heights and pole / rail / strap locations on the Singapore MRT
Discuss the workplace design

## Slide 52: Who fits in a Cessna? Who can reach the controls?

## Slide 53: Design Exercise
Horizontal Adjustment
Vertical
Adjustment
Range of
Movement
Range of
Movement
“H” Point
Eye Ellipse
Z = 0
Y = 0
X = 0
Heel Point

## Slide 54: Design Exercise
Measure the fixed interior dimensions of the vehicle cockpit
Measure the range of movement of the seat, pedals and yoke / steering wheel
Obtain population segment lengths (use spreadsheet data and Drillis and Contini proportions if you wish)
Assume that the seat angles (seat pan and back rest) are fixed
Use a reference point at floor level at the front of the airplane
Develop an Excel spreadsheet model for the anthropometric and workspace dimensions
Create reach and fit tables for Male and Female 5th, 50th and 95th percentiles
Assess the population fit and reach proportions with the seat in the full forward / full rearward / full up / full down positions.
Discuss the model assumptions and shortcomings.
Discuss how anthropometric dimensions, cabin dimensions and seat adjustment ranges can affect the driver / pilot’s ability to safely perform required tasks.
Discuss how you would create a Three Dimensional Model
Check the literature (and car / airplane manuals) for recommended seated workplace dimensions