## Slide 1: Occupational Biomechanics
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: Trigonometry
A
b c
C a B
Triangles
Pythagoras’ theorem (right angle)
Sine, cosine, tangent
c2 = a2 + b2
Triangles are useful in structures, biomechanics and soccer

## Slide 3: Mechanical Units
Scalars – Magnitude
- e.g. mass, time, energy, speed
Vectors – Magnitude and Direction
- e.g. force, velocity
Movement
- Displacement (s) - distance
- Velocity (v)– distance / time ds /dt
- Acceleration (a) velocity / time dv /dt
- Jerk da /dt d2v/dt2 d3s / dt3
What happens when the bus starts to leave the bus stop?

## Slide 4: Angular Movement
Velocity
 = (2 - 1) / (t2 – t1) =   / t
Degrees, radians or revolutions per second
1 Radian = 180 /  degrees
Acceleration
 =   / t
Radians per second squared
2
1
t2
t1

## Slide 5: Force
Force = mass X acceleration
mass = Force / acceleration
Acceleration due to gravity - g
- 9.8066 meters per second squared
Weight = mass X g (Force)
Pressure = Force / area

## Slide 6: Resultant Force Vectors
Fy
FR
Fx


Magnitude FR =( Fx2 + Fy2), Direction = Fx cos()

## Slide 8: Moments
Moment = Force x Distance
Load (Force, Weight, Mass x g
Distance

## Slide 9: Levers
DD
DD
DD

## Slide 10: Moments

## Slide 11: Momentum mass x velocity

## Slide 12: Moment of Inertia
Force = mass x acceleration
Torque – moment of inertia x angular acceleration

## Slide 13: Newton’s Laws
I – A particle stays at rest or moves in a straight lie at a constant velocity if there is no unbalanced force acting on it.
II – The acceleration of a particle is proportional to the resultant force acting on it and is the direction of the force
III – Action and reaction are equal and opposite.

## Slide 14: More Mechanical Concepts
Friction – Walking on ice
Elasticity – A golf ball
Compression – Joints
Tension – Tendons and ligaments
Shear – Intervertebral discs

## Slide 16: Statics
Free body diagram (Force vector diagram)
  Remove from surrounding structures
  Resolve forces into components
  Represent vectors by line length and direction
  Draw whole structure then separate diagrams
Static Equilibrium
  Sum of horizontal, vertical and rotational (moments) forces equals zero

## Slide 17: Free Body Diagram and Equilibrium

## Slide 18: Static Equilibrium

## Slide 19: Flying
Drag
Thrust
Weight
Lift
Constant speed

## Slide 24: Kinematics

## Slide 25: Standard Movements
Movement Type | Plane of Motion | Notes
Flexion | Saggital | Hip, Shoulder, Wrist, Knee, Ankle, Spine
Extension | Saggital | Hip, Shoulder, Wrist, Knee, nkle, Spine
Abduction | Frontal | Hip, Shoulder, Wrist, Carpo-metacarpal
Adduction | Frontal | Hip, Shoulder, Wrist, Carpo-metacarpal
Side Flexion | Frontal | Spine
Rotation | Spine | Horizontal
Medial Rotation | Horizontal | Hip, Shoulder, Knee
Lateral Rotation | Horizontal | Hip, Shoulder, Knee
Circumduction | All | Hip, Shoulder, Wrist, Ankle
Pronation | Horizontal | Forearm
Supination | Horizontal | Forearm
Inversion | Frontal | Ankle
Eversion | Frontal | Ankle
Opposition | All | Thumb
Sliding | All | Fingers, Toes, Spinal Facets

## Slide 26: Range of Motion
Movement Type | Plane of Motion | Range of Motion
Flexion | Saggital | 
Extension | Saggital | 
Abduction | Frontal | 
Adduction | Frontal | 
Side Flexion | Frontal | 
Rotation | Spine | 
Medial Rotation | Horizontal | 
Lateral Rotation | Horizontal | 
Circumduction | All | 
Pronation | Horizontal | 
Supination | Horizontal | 
Inversion | Frontal | 
Eversion | Frontal | 
Opposition | All | 
Sliding | All | 
Demonstrate these movements

## Slide 27: Angle - Time Diagrams
Time
Flexion
Extension
Joint
Angle

## Slide 28: Velocity-Time Diagrams
Time
Velocity (angular)
Acceleration
Deceleration

## Slide 29: Angle - Angle - Time Diagrams
Flexion
Extension
Flexion
Extension
Joint 1
Joint 2

## Slide 30: Angle - Angle - Time Diagrams
Joint 1
Joint 2
F
E
E
F

## Slide 31: Kinetics

## Slide 33
Compression
Tension
Shear

## Slide 34
Angle - Force - Time Diagrams
Joint 2
F
E
Angle
Force
Time

## Slide 35: Dynamics
Force (at a joint) = f(gravity, inertia)
- Inertia = mass x distance squared
Swing a heavy and light hammer
In cricket, big hitters use “the long handle”, why?
Figure skating
Stopping an articulating arm with a heavy load

## Slide 36: Checklists and Operational Models
Checklists
- Range of motion limits / ranges
- Weight and force limits / ranges
- Moment and torque limits / ranges
- Single and complex engineering measures
Discounting model NIOSH Lift Equation
- RWL = LC*HM*VM*DM*AM*CM*FM
- Various durations 1 – 8 hours
- Lift index – what should be the upper limit?

## Slide 37: Checklist Exercises
Create a consensus checklist for:
- manual materials handling
- assembling push fasteners (clips, hoses, electrical connectors)
- different types of screw / nut / bolt runners
Create a discounting equation for repetitive upper limb activity

## Slide 38: Motion Analysis - Goniometry
  Electrogoniometers
• Orthogonal potentiometers mounted close to joint
  Optical goniometers
• Reflective joint center markers
  • Video

## Slide 39: Video Analysis
Analyst, Date, Place, Job Description etc.
Subjects, Views, Durations and Replications
Lighting
Distances, Weights, Forces, Frequencies
Analysis – Motions, Forces, Indices
Reporting – Annotated Video

## Slide 40: Peak – Vicon Motion Analysis

## Slide 42: University of Michigan 3DSSPP

## Slide 43: Lumbar Motion Monitor

## Slide 44: Kistler Force Platforms

## Slide 45: NEXGEN Ergonomics

## Slide 46: Checklists and Operational Models
Checklists
- Range of motion limits / ranges
- Weight and force limits / ranges
- Moment and torque limits / ranges
- Single and complex engineering measures
Discounting model NIOSH Lift Equation
- RWL = LC*HM*VM*DM*AM*CM*FM
- Various durations 1 – 8 hours
- Lift index – what should be the upper limit?

## Slide 47: Mapping
Black
Purple
Red
Orange
Yellow
Green
White
Engineering Dimension
Probability of accident, process failure or user rejection

## Slide 48
Different User Populations and Conditions
Black
Purple
Red
Orange
Yellow
Green
White
Engineering Dimension
Probability of accident, process failure or user rejection

## Slide 49
Policy Decisions
Engineering Variable or Composite Index
Common Currency
Outcome Scale
7
6
5
4
3
2
1
Unacceptable
Range
Ideal Range
Region of Interactions and Continuous Improvement
Policy Statements
1
2
3
4
6
5
7