## Slide 1: Physical Work Stress Index (PWSI)
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: PWSI
The Physical Work Stress Index (PWSI) is a simple, robust physical activity measurement system that indicates an optimal level of workload between high static and high dynamic demands.
It uses an activity sampling approach which can be applied to regular (cyclic) work and irregular work over short or long time periods.
The PWSI may be developed as a manual assessment tool or through the use of a spreadsheet

## Slide 3: History
The PWSI was first developed as a student project at the University of Hong Kong in 1976 (Brian Peacock, Janet Liu)
It was further developed at the University of Oklahoma through undergraduate and graduate projects during the early 1980s (Susan Cheatwood, Jacob Chen)
A description of the process was published by Chen, Peacock, and Schlegel in 1989 in the International Journal of Industrial Ergonomics

## Slide 4: Validation
The tool has been validated by application to a wide variety of jobs in comparison with physiological measures (heart rate) and by comparison with other physical work assessment tools.
The confidence in the tool requires that statistically based activity sampling is applied and that a sufficient number of observations is made.
The tool is not aimed at predicting the occurrence of cumulative trauma, rather it aspires to indicate a level of physical activity conducive to good health

## Slide 5: The Elements
Location
Base Posture
Orientation
Posture (R/L Hand Position)
External Load
Thermal Load
These elements were chosen to reflect the major anthropometric, biomechanical and physiological loads on the worker.

## Slide 6: Activity Sampling
A random or regular sampling scheme is developed depending on the periodicity of the work activity.
  For regular, machine paced work, a random sample is recommended.
  For irregular work, a regular sampling process is both convenient and valid.
The ordinal mappings from values of each of these major elements are recorded at each sampling instant
Generally it is appropriate to gather data from about 10 sampling instants but greater precision can be achieved by increasing the number of sampling instants in a study.

## Slide 7: Ordinal Values
0 1 2 3
Location Distance from Primary Workplace
< 5 m 5 - 10 m 10 - 50m > 50 m
Postural Base Lying Sitting Leaning Standing
Orientation Forward R/L Side Backward Under
L Hand Position In Box Edge Outside Outside Box of Box Box in Two Planes
R Hand Position In Box Edge Outside Outside Box of Box Box in Two Planes
External Load Light Medium Heavy Very Heavy
0 - 1 lb 1 - 10 lb 10 - 25 lb > 25 lb
Thermal Load Comfortable Warm Hot Very Hot
65 - 75 75 - 85 85 - 95 >95

## Slide 8: Location
No changes in location, as would be observed in many computer and machine minding tasks, indicate an undesirable level of static stress.
Large changes in location would be observed if the operator had to walk long distances - this would indicate an undesirable level of dynamic workload

## Slide 9: Base Posture
The range of base postures considered include lying, sitting, leaning (sit-stand) and standing
Maintaining anyone of these postures all day is undesirable - a high static load.
Constantly changing base posture as in changing from sitting to standing too frequently would indicate a high dynamic workload.

## Slide 10: Orientation
It is common for operators in some jobs to change their orientation frequently, often including trunk twisting or moving their feet to collect stock from a container placed adjacent to their workplace.
One example of such work is seen among supermarket checkout clerks.
Some degree of trunk twisting is desirable , but too much (or too little) is not.

## Slide 11: Hand Location
If the hands are within “the box” all day long this may indicate a lack of shoulder, trunk and lower limb activity
In contrast, repeated movements outside the box as in working overhead or at floor level reflects a highly dynamic use of the arms, legs and trunk.
This simple concept of “the box” is therefore a good reflection of the physical demands of a task that is sufficiently accurate for most practical purposes.

## Slide 12: The Box
For the standing operator, the box is a region between 30 and 50 inches from the floor (between knuckle height and shoulder height), 25 inches out in front (functional reach)and 15 inches laterally from the midline of the body (minimal twist comfort region).
These numbers are rounded / approximated to account for a wide range of population anthropometric values; greater precision using reach curves may be used if desired.
For the seated operator the vertical dimensions of the box are between 20 and 40 inches
Operations within the box, at the edge of the box, outside the box and outside the box in two dimensions reflect increasing (ordinal) levels of postural deviation from the base postures.

## Slide 13: External Loads
If the operator handles heavy (or light) objects repeatedly then this would reflect a high dynamic workload.
Conversely if an object is held or pushed continuously then this would constitute a highly static load

## Slide 14: Thermal Stress
Continuous exposures to high, low or even moderate temperatures may produce a high level of “static” stress on the body.
Conversely, constantly changing temperatures could overstimulate the body’s thermal regulatory processes.

## Slide 15: Data Processing
The “absolute” physical workload is calculated simply by averaging the scores from the sampled observations for each element of the index.
The “successive differences” sheet calculates the average of the absolute values of the differences between successive observations.
Averages are obtained by dividing the element totals by three times number of observations and the grand total by 7 (the number of elements) This produces a relative value between 0 and 3.

## Slide 16: Physical Workload
The absolute physical workload of a task may be estimated by averaging the within element scores and then producing a profile of the the task.

## Slide 19: Static and Dynamic Workload Balance
Large differences in the ordinal values of the selected variables between sampling instants reflect a highly dynamic physical workload.
No change between successive time observations reflects a high static physical workload.
Summing (and then averaging) the changes over successive sampling intervals gives an indication of the overall static / dynamic workload balance for each of the elements.

## Slide 22: Interpretation
High scores >2 on the absolute workload profile represent undesirable levels of physical stress
Low scores (<1) on the static / dynamic balance profile are associated with static workloads
High scores (> 2) are associated with highly dynamic workloads
Optimal “balance” values range from 1 to 2

## Slide 23: Interactions
The choice of these variables was based on the premise that they were somewhat exclusive categories of activity, reflecting different types of stress.
However these independent variables may interact to produce additional (multiplicative) static or dynamic extremes.
Analysis of the interactions may be obtained by multiplying element scores such as the postural and external load scores

## Slide 24: Weightings
It may be argued that the different variable have differing levels of importance.
  In this case it is convenient to use regression or consensus based weightings prior to calculating the overall score.

## Slide 25: Conclusions
This activity sampling based tool produces a measure of both the absolute physical demand of the task and the degree of balance between static and dynamic workloads.
All measures are on a 0 to 3 scale with ideal balanced loads being between 1 and 2.