## Slide 1: Whole Body Vibration
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: What is Vibration?
The oscillatory motion of bodies which have mass and elasticity
Frequency - periodic, stochastic
Amplitude - acceleration, RMS
Frequency Spectrum
External forces
Internal forces
Resonance - when the frequency of external excitation coincides with the natural frequency of the system

## Slide 3: What is Vibration?
Shakings and Jerkings
Whole Body Vibration
  Vehicles
  Helicopters, Fork Trucks etc
Segmental or Hand Arm Vibration
  Powered Hand Tools
  Chipping Tools, Chain Saws, Grinders etc

## Slide 4: Shakings
Accelerometers - g
Planes - x, y, z
Spectral analysis - breakdown of the vibration, in each plane, into its constituent frequencies and accelerations
Low frequencies of greatest concern

## Slide 5: Jerkings
A change of acceleration
Driving over bumps
Transmission of an external force to the body
Damped oscillations - internally absorbed forces

## Slide 6: Mechanical System
Spring
Damper
Mass
Force = Mass x Acceleration
Proportional
to Velocity
Proportional
to Length
Vibration force f(t) = m d2x/dt2 + c dx/dt + kx
Constraint

## Slide 7: Active Suspensions

## Slide 8: Human System
Long Bones - Framework
Joints - Centers of Rotation
Ligaments - Constraints
Muscles - Springs, Active Damping
Spinal Column - Spring, Passive Damping
Organs - Mass, Passive Damping
Internal Systems Absorb the Energy from the External Environment

## Slide 9: Why Should We Worry?
Continuous exposure to jerkings and shakings can give rise to discomfort, pain and damage to various structures:
  Spinal Joints
  Limb Joints
  Organs
Injury or Temporary Discomfort and Fatigue?

## Slide 10: A Perennial Source of Concern
Reports of pain and discomfort
Complaints about the floor and dock plates
Relatively little hard evidence of vibration related illness
  NIOSH WRMSD report
Numerous investigations
  measurements
  symptoms, lost work day incidents
Back pain has high prevalence in the general population

## Slide 11: NIOSH Literature Review, 1997
There is strong evidence of a positive association between WBV, from Vehicle Operation, and back disorder
Subjective (Symptoms Surveys) and Objective (Medical Diagnosis) assessment methods
  Discs, Back Muscles, End Plates
Combined effects with Lifting, Prolonged Sitting and Awkward Postures
Positive Exposure Duration Effects

## Slide 12: SPO Denver Injury / Illness Reports
100 + symptoms and OSHA 200 reports over 5 years
Only 3 possibly related to vibration!
Most to do with contusions, trips, slips and falls while mounting / dismounting

## Slide 13: The Daily Dose
Hours per day
Hours per day riding the truck
Vibration sources
  Continuous vibration
  Bumps
Vibration exposure per day

## Slide 14: What is a Shrinkmeter? (Corlett, Pope and Bonney)
Spinal Length Measurement
Spinal Length Decreases:
  After living a long time
  After a long day fighting gravity
  After a long day fighting bumps or vibrations
Increased Spinal Curvature
Decreased Disk Thickness

## Slide 15: ANSI Standard S3.18-1979 ISO 2631- 1 - 1978, 1997

## Slide 16: Fatigue Decreased Proficiency Boundary Z

## Slide 17: Fatigue Decreased Proficiency Boundary X, Y

## Slide 18: ANSI Standard
Fatigue Decreased Proficiency Boundary
Exposure Limit for Health and Safety
  FDPB x 2
Reduced Comfort Boundary
  FDPB / 3

## Slide 19: Resonance (Rasmussen 1982)
The higher the mass the lower the resonant frequency
  Upper Torso - 5 Hz
  Abdomen - 4 - 8 Hz
  Spinal Column - 10 - 12 Hz
  Head - 20 - 30 Hz
  Eyeball - about 60 - 80 Hz

## Slide 20: Symptoms (Rasmussen 1982)
Frequency Discomfort
4 - 9 General Discomfort
5 - 7 Chest
4 - 10 Abdomen
13 – 20 Head, Speech
1 - 2 Drowsiness

## Slide 21: Industrial Trucks
Solid Wheels
Rigid Suspensions
Sit Down
Stand Up
High Seniority Jobs
Largely Self Paced - When you’re done, you’re done for the day
  High Skill, High Speed
Rough Floors
Warped Loading Dock Plates

## Slide 22: Case Studies
SPO Fork Trucks and Pick Vehicles
  Loading docks and in plant routes
  Vehicles instrumented
    Seat Pad
    Accelerometer mounted on floor
    Fixed trial routes and speeds
Exposure less than 16 hour limit
Investigations of alternative seats
  Grammar seat preferred

## Slide 23: Laboratory Seat Testing
Delphi Interior Ergonomics Seat Test Laboratory
Sears vs Grammar Seat
Frequency range 0.5 - 30 Hz
Natural Frequencies
  Sears 4Hz, Grammar < 4 Hz
Seat Effective Amplitude Transmissibility
  Output / Input acceleration over whole frequency range
  Grammar(70+/-) < Sears (90+/-)
  >100 implies amplification

## Slide 24: Interventions
Stand Up Fork Trucks
  Widely used at loading docks because of short turning circle (operator stands directly over rear wheels)
  Some local plant proposals involved spring mounted platform!
  “Shock absorbent” matting
  Spring-Damper system would require sufficient travel - retrofit would cause back bending
Drive more slowly over the bumps! - this would delay job completion time
Provide lean seat with damper
Provide suspended (spring - damper) seats
Active suspensions (active vibration cancellation )

## Slide 25: Conclusions
A perennial source of complaint
High amplitude and long duration exposures likely to have adverse effects
Occasional bumps are of marginal significance
Slow down over the bumps
Buy suspended seats
Isolate the standing operator
Reduce exposure durations through rotation