## Slide 1: Ergonomics Analysis of Sheet Metal Handling
Brian Peacock
for
Pitney Bowes Inc

## Slide 2: A Day in the Life of a Piece of Pressed Metal
Roll of Steel from Steel Mill
Stamping Press
Off loading into Wire Baskets
Transportation to Assembly Plant
Delivery to Body Shop
Loading into Welding Fixture
The basic choices are related to manual or automatic processes (Allocation of Function in ergonomics parlance)

## Slide 3: What can be changed? Factors Affecting Throughput
Panels per hour off the Press
Panels per Basket
Number of Operators offloading the Press
Hours worked per day
Vehicles per hour through the Body Shop
Transportation facilities
Handling devices
Number of Operators in the Body Shop
Capacity of the Welding Robots

## Slide 4: What can be changed? Factors Affecting Human Performance
Workplace design
  End of Press Line
  Basket Design and Presentation
  Welding Fixture Design
Thermal Environment
Workload
Job Design - Rotations etc

## Slide 5: What can be changed? Micro Factors Affecting Performance
Location and Orientation of Conveyors, Baskets and Fixtures
Targets in Baskets and Fixtures
Dunnage and Obstructions
Panel Size and Weight
Handling devices

## Slide 6: What process output factors can be measured? System Performance Criteria
Throughput - panels per hour
Quality - mutilations
Safety - cuts and abrasions
Health - musculoskeletal disorders
Motivation - job content, job environment, control and rewards, attendance

## Slide 7: Questions Why not Automate the whole thing?
Task variety and complexity
Cost
Throughput
Until a few years ago and under low throughput conditions manual welding was/is still preferred.

## Slide 8: Questions Why not use handling devices?
They are used for heavy parts
They slow down the operator
They are cumbersome
They require more floor space
They only deal with gravity, not inertia
Contemporary Intelligent Assists may have some application
  Recent experience still indicates that they slow down the operator

## Slide 9: Questions How can Work Spaces be Modified?
Heights
Reaches
Orientations
Obstructions / Interferences
Carry Distances

## Slide 10: Analysis must provide evidence for decisions and lead to interventions that are measurable
The Job
Outcomes
Analysis and
Simulation
Interventions
Decisions

## Slide 11: How can task factors be assessed? Ergonomics Analysis and Modeling Techniques
Checklist Analysis
Work Measurement - workload, manpower
Anthropometry and Workplace Design
Biomechanical Analysis
Manual Materials Handling Analysis
Target Analysis
Energy Analysis
Biomechanical Modeling
Anthropomorphic Modeling
Comprehensive computer based ergonomics analysis systems

## Slide 12: Checklist Analysis
There are checklists and checklists
Some are qualitative
Some are quantitative
Some measure people
Others measure what can be changed
Most checklists have their uses
Many checklists miss the point - they should be a tool that enhances the reliability of decisions and points the engineer or manager to an appropriate decision

## Slide 13: Work Measurement
Traditional work measurement methods - from stop watches through predetermined times to negotiated staffing levels - explicitly address time but pay insufficient attention to the detailed content of work or to human variability
This is why ergo nomos is an essential supplement to traditional work measurement methods

## Slide 14: Anthropometry and Workplace Design
We look up the anthropometric tables, find the averages and percentiles for the expected user population, combine these numbers to optimize the reach and fit requirements of the task and design or modify the equipment accordingly
This is Ergonomics 101
But we didn’t learn about the real world complexities and constraints in ERGO 101

## Slide 15: Biomechanics
Archimedes knew all about moments but he either forgot to tell our engineers or they forgot that moments apply to people as well as machines
We build big wire baskets to transport parts but not for the convenience of getting things in and out
Are backs and shoulders hurt by statics or dynamics?

## Slide 16: Biomechanical Models
The University of Michigan 3DSSPP and the University of Waterloo’s WATBACK are outstanding static models
Their ease of use has improved enormously
They produce enough reports to sink a ship or write a thesis
They are great analysis or simulation tools in the right hands
But are they a cumbersome way of getting to what can be changed?

## Slide 17: NIOSH Lift Equation
The ubiquitous “NIOSH”
The weighting factors and indices were based on good science, plus a lot of professional judgement
There were some gaps in logic in the development of the ‘91 version
It is a very easy to use tool, both in its manual and computerized forms
It is a great analysis and simulation tool in the right hands
But the interpretation of the LIFT INDEX has become a battle ground between science, epidemiology, business, government, the unions and the courts.

## Slide 18: Energy Analysis
Carrying heavy pieces of sheet metal around all day can be energy consuming
Gravity is the main challenge
Picking, orienting, carrying and placing add to the workload
The operator also has to move himself
Modern presses can spit out panels at very high rates
The key to energy analysis and, thence, job design is physiological variety, not simplistic maximum kcals per minute

## Slide 19: Target Analysis
Tight targets take time
Sometimes an operator may need to make three or four adjustments to hit the “target” in the container, often while he is in an exposed, overreaching posture
Easy targets reduce energy demands and reduce biomechanical stress

## Slide 20: Anthropomorphic Modeling
SAMMIE, JACK, DENEB, RAMSIS, SAFEWORK, ROBCADMAN and others promise to solve all our analysis and simulation problems and lead us to an ergonomic utopia
But they are just tools, some more accurate and some more easy to use than others
They all address anthropometry and range of motion and have a variety of biomechanical, work measurement and energy analysis add ons
They also offer decision aids in the form of “flags”
To date they do not offer an integrated human model
They are somewhat useful in looking at sheet metal handling

## Slide 21: Anthropomorphic Modeling in Sheet Metal Handling
Anthropomorphic models have been used in the analysis and simulation of sheet metal handling workstations
But there are only a few things that can be changed:
  Vertical height, Horizontal reach, Part and Fixture orientations, Motion pathways and obstructions, Targets, Handling aids
  It is debatable whether the more complex modeling tools add significantly to the judicious application of ERG 101.

## Slide 22: BUT
A comprehensive modeling tool, in trained hands, could greatly enhance design activities by simultaneously asking many ergonomics questions
Reach, fit, moments, forces, times, pathways, targets, energy, repetitions, fixtures, handling aids, containers, conveyors, tooling, staffing levels, automation decisions

## Slide 23: Comprehensive Analysis and Simulation
The development of comprehensive anthropomorphic modeling and simulation requires the simultaneous attention to organizational design, the design process, selection and training of ergonomists and technicians
But will the tasks that we are designing for these analysts and simulators create ergonomics problems of their own - I think so
Consequently we must design our modeling systems and processes so that routine, posture constraining tasks are minimized.

## Slide 24: Conclusion
To date, the jury is still out in the utility of anthropomorphic modeling tools, perhaps because the organizational, process and humanware design activities have not matched the progress of software development, which also has a long way to go