## Slide 1: Ergonomics Container Checklist
Brian Peacock
for
Pitney Bowes Inc

## Slide 2
Part Name:_____________________________
Program: _______________
Model Yr:_______
Date of Analysis: __________ Analyst:_______
Part Number:___________________________
Container Number:_______________________
Container Dimensions: L:___in. W:___in H:___in.
Part Wt (lb.)_____
Dunnage: removable
ÿ
contained
ÿ
moveable
ÿ
O = Original Condition; R = Revised Condition
DUNNAGE (D1-D3)
D1. Dunnage Weight/Force (include swing
arms).
O
R
·
< 1 lb.
0
0
·
1 to 10 lb.
1
1
·
>10 to 25 lb.
2
2
·
>25 lb.
3
3
Comments:
________________________________________
________________________________________
D2. Removable Dunnage size (length + width
+ height).
O
R
·
< 1 ft. (30 cm.)
0
0
·
1-5 ft. (30 - 150 cm.)
1
1
·
> 5 ft.-10 ft. (> 150 cm
to 300 cm.)
2
2
·
>10 ft. (>300 cm.)
3
3
Comments:
________________________________________
________________________________________
D3.
Dunnage Work Envelope Matrix.
(numbers in parentheses used if posture held <5 sec. or
performed <1 per minute)
H
or. Dist. (in) measured from belt buckle to hands
H
orizontal Distance
1-10
>10-15
>15-20
>20-25
>25-30
>30
>75
3
V
>70-75
3 (2)
3
e
>65-70
2 (1)
3 (2)
3
r
>60-65
1
2 (1)
3 (2)
3
t
>55-60
1
1
2 (1)
3 (2)
3
i
>50-55
1
1
1
2 (1)
3 (2)
3
c
>45-50
0
0
1
2 (1)
3 (2)
3
a
>40-45
0
0
1
2 (1)
3 (2)
3
l
>35-40
0
1
2 (1)
3 (2)
3
>30-35
1
2 (1)
3 (2)
3
H
>25-30
2 (1)
3 (2)
3
t
>20-25
3 (2)
3 (2)
<20
3 (2)
V
ertical Height (in) measured from floor to hands
Original Score: _____
Revised Score: _____
Comments:
________________________________________
________________________________________
PARTS (P1- P4)
P1. Hand clearance for loading/unloading
part (exclude stacked part
s).
O
R
·
>6 in.
0
0
·
>3 to 6 in.
1
1
·
1 to 3 in.
2
2
·
<1 in.
3
3
Comments:
________________________________________________________________________________
________________________________________
P2. Part Placement.
O
R
·
self align or non critical
0
0
·
guided/ rough locators
1
1
·
critical operator judgement
3
3
Comments:
________________________________________
________________________________________
P3. Part Rotation, Flipping or Obstructions
( 2-handed loading ).
O
R
·
no rotate/flip; smooth
0
0
continuous motion
·
no rotate/flip; minor
1
1
direction adjustment
·
rotate
<
90
°
or flip
<
120
°
2
2
·
rotate>90
°
; flip>120
°
; regrasp
3
3
Comments:
________________________________________
________________________________________
P4.
Part Load/Unload Work Envelope Matrix.
H
orizontal Distance
1-10
>10-15
>15-20
>20-25
>25-30
>30
V
>70-75
3
3
e
>65-70
3
3
3
r
>60-65
3
3
3
3
t
>55-60
3
3
3
3
3
i
>50-55
2
2
3
3
3
3
c
>45-50
1
1
2
3
3
3
a
>40-45
0
0
1
2
3
3
l
>35-40
1
1
2
3
3
>30-35
1
2
3
3
H
>25-30
2
3
3
t
>20-25
3
3
<20
3
Original Score: _____
Revised Score: _____
Ergonomics Container Checklist
Notes: 1

## Slide 3
LATCHES / LOCKS (L1-L5)
L1. Finger/Thumb forces - latches, locks
and/or pulls.
O
R
·
< 2 lb.
0
0
·
2 to 6 lb.
1
1
·
> 6 to 10 lb.
2
2
·
> 10 lb.
3
3
Comments:
________________________________________
________________________________________
L2. Hand forces for pull cable release.
O
R
·
< 20 lb.
0
0
·
20 lb. to 35 lb.
1
1
·
> 35 to 55 lb.
2
2
·
> 55 lb.
3
3
Comments:
________________________________________
________________________________________
L3. Pull/Push Surface Diameter.
O
R
·
> 0.5 in. to
<
1.5 in.
0
0
·
0.25 in. to 0.5 in.
1
1
·
< 0.25
in.; > 1.5 in.
3
3
Comments:
________________________________________
________________________________________
L4. Clearance for latches, locks and pull rings.
O
R
·
> 2 in.
0
0
·
1 to 2 in.
2
2
·
< 1 in.
3
3
Comments:
________________________________________
________________________________________
RACK ENTRY
R1. Rack Entry.
O
R
·
no entry into rack
0
0
·
enter onto even, unobstructed
1
1
rigid surface
·
enter onto uneven, obstructed,
3
3
non-rigid surface or walk path
< 24"
Comments:
________________________________________
________________________________________
LIFTING MOMENT
M1. Lifting moment for part, dunnage, or
swing bar.
Load Wt. __ lb.
x
Hor Reach __ in. = Lift Moment ___ in. lb.
If Lift Moment at initiation of lift is greater than 245 in. lb., a lift
analysis required.
O
R
·
<84 in. lb.
0
0
·
84-245 in. lb.
1
1
·
>245- 410 in. lb.
2
2
·
>410 in. lb.
3
3
Lift Analysis Recommended: YES
ÿ
NO
ÿ
Scoring the Worksheet
Total Scores:
Original
Revised
Þ
# of 3’s
_______
_______
Þ
# of 2’s
_______
_______
Þ
# of 1’s
_______
_______
Totals
1
2-5
>5
3 scores
3
3
3
2 scores
1
2
3
1 scores
1
1
1
Insert Picture or sketch of container and/or part below
Notes: 2