## Slide 1: Ergonomics and Quality
Brian Peacock

## Slide 2: The ABCs of Qs and Ps Ergonomics and Quality The Score Chart for the Quality Problems
A - The situation is fine customer satisfaction is Assured P(p)=0
B - Occasional / random problems may occur but are likely to be easily corrected P(p)= 0.0001
C - Occasional / random problems may occur and some may escape detection P(p)=0.001
D- Systematic(special cause) problems occur but solution is straightforward P(p)=0.01
E -Systematic(special cause) problems occur but detection or resolution may be difficult P(p)=0.01
F-Frequent random and systematic problems occur P(p)=0.1
Each situation described below should be ranked according to this scale, Ds, Es and Fs must be dealt with, Bs and Cs must have enhanced monitoring, As should be recorded as best practices

## Slide 3: The Ergonomics Angle
Quality problems are the result of some human error that occurs between the articulation of customer requirements, through design and production to delivery.
The propensity for human error pervades these processes, and quality statistics demonstrate the form and frequency of these errors.
Many, but not all errors can be avoided by the design of processes, systems and parts that address the required human involvement and foreseeable interactions
Errors do not become a problem if they are detected and resolved in an appropriate time frame
Error detection and resolution processes should be built into all stages of the process - design for error detection and recovery

## Slide 4: The Ps
Problems - An articulation of the nature and incidence of the problem
Product - A design characteristic of the part
Protection - The steps taken to protect the part from damage during transportation from the source to the vehicle and on to the customer
Packaging - the location of the part in the vehicle relative to other parts
Plant - the major storage, fixturing and moving facilities
Process - the equipment, tools, fixtures and workplace arrangements
Procedure - the sequence and form of actions required to manufacture / assemble the part, including facilitators such as instructions and other job aids
Planning - the steps taken to assure quality throughout the design and production process
Production - the productivity demands of the process in terms of efficiency, throughput, line speed, resources etc.
People - the characteristics, capabilities, limitations, selection, training, motivation and management of the people associated with the design and production processes
Note that quality problems may occur due to interactions between two or more of these elements of the quality assurance process

## Slide 5: Problems
Standard statistical methods may be used to collect, analyze and communicate the types, severity and incidence of quality problems.
There are many routine data sources from in-plant observations to warranty and customer reports - and ad hoc studies that report on particular quality issues.
Analysis of these data classifications is key to the description of context, cause and cure

## Slide 6: Product (A design characteristic of the part)
Is the part intrinsically reliable - does it perform the desired function?
Is the part designed to interact, interface (or interfere) with other parts?
Is the part clearly distinguishable from other parts or variations?
Are facilitators designed with the part to assure accurate manufacture, transportation, assembly and inspection
Is the part vulnerable to damage? Are the results of damage likely to be clear with or without formal testing?

## Slide 7: Protection
Is the life cycle of the part from design, through manufacture, transportation and assembly to use and disposal clearly articulated.
Are all human interactions and requirements during this cycle articulated.
Is protection provided for each