## Slide 1: The Ergonomics of Production Lines Measurement and Interventions from the Factory to the Office
Brian Peacock
SIM University
National University of Singapore

## Slide 2: Some Interesting Articles by Dr Chen
"A Fuzzy Sets Modeling Approach for Ergonomic Workload Stress Analysis", International Journal of Industrial Ergonomics (1994)
"A Computer Assisted System for Physical Ergonomics Analysis", Computers in Industrial Engineering (1991)
"An Observational Technique for Physical Work Stress Analysis", International Journal of Industrial Ergonomics, No.3 (1989)
"A Database Management System for Ergonomics Information Analysis,“ Trends in Ergonomics/Human Factors V, Elsevier (1988)
"Prototype Expert System for Physical Work Stress Analysis“ Trends in Ergonomics/Human Factors IV (1987)
"EVA Suit Glove Design." Space Tech '85 Conference, Anaheim, California (1985)
"An Interactive Biomechanical Lifting Model,“ Mid Central Human Factors/Ergonomics Conference, West Lafayette, Indiana (1985)

## Slide 3
Ergonomics = Human Factors
Most of the World
USA
HFE

## Slide 4: The History of Ergonomics
Tools

## Slide 5: Human Factors Engineering / Ergonomics
Analysis
and
Design
with People in Mind

## Slide 6: Human Factors in Technology Integration Perspective Complexity
Interactions
People
Rules and Regulations
Context
Technology
Adapted from Edwards’ SHEL Model

## Slide 7: The Design Cycle
The Process,
Job, Task,
Transaction
or Simulation
Uncontrollable
Conditions / Context
Specifications
Design
Equipment
Context
Humans
Operations
Guidelines
and
Constraints
Decisions
Policy
Money
Analysis
Requirements
Outcomes
Analysis
Analysis
Tools
Analyses
6U
2M
E4S4
Prediction
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E

## Slide 8: Many Responsibilities
Force
Space
Time
Product Engineer
Packaging Engineer
Manufacturing Engineer
Industrial Engineer
E
P
B
Information
Affect
Satisfaction

## Slide 9: Big Picture Ergonomics Purposes
Effectiveness Quality
Efficiency Productivity
Ease of Use Comfort and Convenience
Emotional Appeal Pleasant job and context
Safety/Health Acute Injuries and Chronic Illnesses
Security Malicious Third Parties
Satisfaction Of ALL concerned
Sustainability Reliability AND Resilience
If you can’t / don’t measure it you can’t manage it
There will be tradeoffs
E4S4
E
P
B

## Slide 10: The Purposes of Ergonomics
Contributing to the Multiple Purposes of Design
Helping with the tradeoffs
E4S4
Productivity
Safety

## Slide 11: The 6Us and 2Ms of Usability
Utility
  Is the system useful?
Usage and Misusage
  How and in what context will the system be used?
  What possible extreme contexts may be predicted
Usability
  Is the system easy to use or misuse?
Utilization
  How often and by how many people is the system used?
Users and Misusers
  Who are the users and possible misusers?
User Error
  What kinds of error can be made, when and how will they be made, how frequently and what are the possible consequences?
6U
2M

## Slide 12: When Ergonomics Works RASDEI
Research
Analysis
Design
Evaluation
Outcome Investigation
Simulation
Ergonomics Projects need some or all these Skills
Success
Failure

## Slide 13: Product Life Cycle
Requirements
Concept
Development
Concept
Selection
Specifications
Tooling
Production
Marketing
Use and
Misuse
Maintenance
Disposal
Feedback, Technical Memory
Many Customers
(including the shareholders)
Design Team
Many Requirements
Feedforward (Anticipation)

## Slide 14: The Process of Ergonomics
$
Decisions
Benefits, Costs,
Risks, Tradeoffs
Measurement and Analysis
Screening
In depth Research
Contexts
Spatial, Physical, Mechanical, Chemical, Biological, Geographical, Social, Political, Economic
Design
Tools, Equipment, Workplaces, Tasks, Procedures, Assignments.
The Job
Outcomes
Quality
Productivity
Health, Safety
Ease of Use
Security
Satisfaction
Sustainability

## Slide 15: Human Factors Applications Need
Domain Knowledge
Measurement and analysis tools
Knowledge of human characteristics, capabilities and limitations

## Slide 16: The Ergo Cop Problem
Design
Specifications
Ergonomics
Evaluation
The Ergocop
Design
Performance
Review
(waivers by management)
Performance
Requirements
Performance
Review
Precise
Design
Specifications
Ergonomics
Support
Design
Clear
Performance
Requirements
Time to
Market
Calling the designer’s baby ugly!

## Slide 17: The Broad Scope of Ergonomics
Physical
Sensory
Cognitive
Social
Affective
Environmental
Temporal

## Slide 18: Variability
Ergonomics Purpose and Achilles' Heel
Physical
Cognitive
Social
Affective
Context
Temporal
Sensory

## Slide 19: Physical Ergonomics
Shape
Size
Strength
Speed
Stamina
Skill

## Slide 20: People vary in Shape and Size

## Slide 21: People vary in their Strength

## Slide 22: People Vary in their Skills

## Slide 23: People vary in their Speed

## Slide 24: People vary in their Stamina

## Slide 25: Sensory Factors
Vision
Touch
Taste
Proprioception
Smell
Hearing

## Slide 26: What happens when you grow old?

## Slide 27: Are you Colorblind?
1. Normal Color Vision: A: 29, B: 45, C: --, D: 26
2. Red-Green Color-Blind: A: 70, B: --, C: 5, D: --
3. Red Color-blind: A: 70, B: --, C: 5, D: 6
4. Green Color-Blind: A: 70, B: --, C: 5, D: 2

## Slide 28: Cognition is complex
Evaluating
Diagnosing
Judging
Deciding
Planning
Investigating
Predicting
Analyzing
Problem Solving
Cognition
Learning
Interpolating and Extrapolating
Goals
Understanding
Synthesizing

## Slide 29: People vary in their Cognitive abilities

## Slide 30: Cognition is Complex

## Slide 31: Affective Factors
Emotion
Esthetics
Elegance
Attitude
Mood
Motivation
Excitement

## Slide 32: Environmental Factors
Acoustic
Communication
Hearing loss
Thermal
Heat
Humidity
Cold
Air movement
Vibration
Hand / Arm
Whole body
Light and Dark
Vision
Contrast
Color
Chemical and Biological
Gravitational
Space
Pressure
Under Water
Altitude

## Slide 33: Environmental Design - Lighting
Provide natural lighting
Provide sufficient lighting
Avoid glare
Provide special purpose lighting to emphasize task features

## Slide 34: Environmental Design - Noise
Reduce damaging / distracting / interfering noise
  At source
  By barriers
  By PPE
  By exposure reduction (rotation)
Enable task information, communications and alarms distinct from ambient noise
Allow / provide music if it doesn’t interfere with task or colleagues

## Slide 35: Environmental Design - Heat
Maintain air temperature between 220 C – 260 C
  For sedentary work (cooler for physical work)
  Allow some fluctuation
Maintain relative humidity necessary for process
  generally between 30% – 50%
Enable air movement
  Avoid drafts
Address / control radiant heat / cold sources

## Slide 36: Social Context
Managers
Customers
Groups
and
Teams
Hierarchies
Cooperation
Communication`
Competition
Language
and
Jargon
Roles
Jobs
Supervision
Businesses and Companies
Laws
Rules and Regulations
Traditions
Infrastructure
Economics
Politics
Religions
Suppliers
Organizational
Design
Employees

## Slide 37: Time Factors
Job Cycle Time
History
Task Pacing
Remembering
Acceleration
Velocity
Decision Time
Movement Time
Reaction Time
Psychological Refractoriness
Age
Fatigue
Vigilance
Circadian Rhythms
Mental Workload
Duty Cycle
Shift Length
Timing

## Slide 38: Workplace Ergonomics
Space - layout, furniture, postures
Force - materials handling, strength, postures
Time – productivity, fatigue, shiftwork
Information – training, quality
Affect – motivation, behaviors
Context – physical and organizational

## Slide 39: Workplaces

## Slide 40: Postures and Environments

## Slide 41: Physical Workloads

## Slide 42: Standard Times (measured in seconds)

## Slide 43: Awkward Postures

## Slide 44: Overhead Work

## Slide 45: Bicycle Assembly

## Slide 46: Workplaces and Postures

## Slide 47: Assembly Work

## Slide 48: The Office

## Slide 49: The Typing Pool

## Slide 50: The Office

## Slide 51: Call Centers

## Slide 52: Assembly Operations

## Slide 53: Mobile

## Slide 54: The History of Assembly Lines

## Slide 55: I love Lucy, Chocolate wrapping line.
http://www.google.com/url?sa=t&rct=j&q=lucy%20chocolate%20factory&source=web&cd=2&cad=rja&ved=0CCkQtwIwAQ&url=http%3A%2F%2Fwww.youtube.com%2Fwatch%3Fv%3DFGfplQ1FUFs&ei=_eJWULi3IYHNrQf28oCYBw&usg=AFQjCNHkkfIbZobjKqrGwXuspX-A1XPfVQ
http://lloyddeleon.multiply.com/video/item/4/I_Love_Lucy_--_at_chocolate_factory
https://www.youtube.com/watch?v=8NPzLBSBzPI

## Slide 56: Henry Ford – Work Simplification

## Slide 57: Bring the Work to the Worker

## Slide 58: Frederick Winslow Taylor - “Taylorism”
Scientific Management
Managers Manage, Workers Work
Prescriptive work methods

## Slide 59: Lillian and Frank Gilbreth
Time, Motion and Fatigue Studies
Micro motion – “Therbligs”

## Slide 60: Therbligs
Reach
Grasp
Move
Hold
Release
Use
Pre-position
Position
Assemble
Disassemble
Search
Select
Plan
Inspect
Unavoidable Delay
Avoidable delay
Rest

## Slide 61: Hawthorne Studies
Employees motivated by the attention given to them rather than impersonal change in working conditions (lighting)

## Slide 62: Tavistock Institute
Coal Mining
Human Centered Design

## Slide 63: MTM
Methods-Time Measurement is a procedure for improving methods and establishing time standards by recognizing, classifying, and describing the motions used or required to perform a given operation and assigning pre-determined time standards to these motions.
The foundation of modern Work Measurement and Industrial Engineering

## Slide 64: Lots of Components
Lots of savings by removing none value added activities

## Slide 65: Boeing Assembly Line

## Slide 66: Electronics

## Slide 67: Electronics

## Slide 68: Production lines brought enormous improvement in Productivity by the removal of Non Value added work and the improvement of Process consistency / Quality But at what cost?

## Slide 69: Work Measurement
Puropses
  Productivity
  Quality
Micro motion analysis
Remove non value added activities
  Searches, decisions, movements, (checks)
Work simplification
  Reduce the job cycle
    Shortens learning time
    Improves Productivity and Quality?

## Slide 70: Industrial Engineering The Job Cycle
Transport
Grasp
Attach
Inspect
Return
Time

## Slide 71: The Job Cycle (varies between a few seconds, a few minutes and even a few hours)
Check
Position
Cycle Time
Force
*
Posture
Transport
Grasp
Reach
Attach
Return / Rest

## Slide 72: The Industrial Engineering Solution Cut off the peaks of Force and Posture, Reduce Non value Added work and Fill up the Job Cycle
Check
Position
Cycle Time
Force
*
Posture
Transport
Grasp
Reach
Attach
Return / Rest

## Slide 73: Postures

## Slide 74: Tool balancers

## Slide 75: Doors Off

## Slide 76: Skillets – Work height adjustment

## Slide 77: Assembly Lines

## Slide 78: Tilt the Task

## Slide 79: The Results Improved Productivity But increased Static Work
Cycle Time
Force
*
Posture
Transport
Grasp
Attach
Grasp
Attach
Transport
Transport
Grasp
Attach
Line Balance

## Slide 80: The $64,000 Question?
Does (pseudo) Ergonomics cause Illness and Injury?
“Ergonomic / Iatrogenic Disease”
Long durations, low forces, near neutral postures, high repetitions

## Slide 81: The CTD Epidemic Repetitive motion strain Occupational overuse syndrome
Meatpacking
Nursing homes
Automobile manufacturing
Parcel handling
Electronics manufacturing
Textiles
Food processing
Textiles
Checkout counters
etc
Years of Contentious / Combative dialog
among Government (NIOSH / OSHA)
Business (NAM, COT), and Unions (UAW)
providing many opportunities for
Ergonomics Researchers, Professionals, Practitioners and Product developers

## Slide 82: Sedentary Work leads to metabolic disorders – obestity, circulatory disease, diabetes
Ergonomic
X

## Slide 83: Sedentary, Static and Repetitive Work lead to:
Repetitive Strain Injury
  Musculo skeletal disorders
Metabolic disorders
  Obesity, circulatory disorders, diabetes
Cognitive dullness
  Lack of flexibility
Job dissatisfaction
  Absenteeism
  Industrial unrest
Operational deterioration
  Productivity, quality

## Slide 84: Intervention Opportunities
Engineering Interventions
  Robotics
  Mechanical assists to reduce
    Force
    Extreme Postures
Administrative Interventions
  Time
    Job Enlargement
    Job Rotation
    Decoupled assembly lines
    Work Cells
    Vertical Job Enlargement
    Work Teams
    Participation
Time

## Slide 85: The Job Cycle
Check
Position
Cycle Time
Force
*
Posture
Transport
Reach
Attach
Return / Rest
Grasp

## Slide 86: The Rest Pause Question
Are frequent short breaks “better than” less frequent long breaks?
The “Psycho-Social” Answer - No
  People invariably “work ahead” to increase “discretionary time”
The Physiological Answer – Maybe
Rest pauses need managing

## Slide 87: Administrative Interventions Job Design
Job Enlargement
Job Rotation
Decoupled assembly lines
Work Cells
Vertical job enlargement
Team structures
Participation
“Andon Chords”

## Slide 88: Decoupling
Separate cells by buffers so that teams are self rather than line paced
Allows for flexible response to variable conditions
Allows work to continue if there is a problem up or down the line

## Slide 89: Horizontal Enlargement Increase the cycle time, put more (different) functions into the job cycle
Increased Cycle Time
(Load up to 90%)
Varied Force and Posture

## Slide 90: Horizontal Job Enlargement Examples
NUMMI
  Joint Venture between GM – Toyota
  Selected work force
  Team structure
  Participation
  5 minute job cycle
Lansing Craft Center
  Very long cycles
  Non valued added components handling

## Slide 91: Job Rotation
Task
1
Task
2
Task
3
Rotate every ½ , 1, 2 hours or on different days or even weeks

## Slide 92: The Hidden Advantages of Horizontal Job Enlargement and Rotation
Adds more knowledge and skills to the individual worker
Creates greater flexibility in job assignment
Resolves line balance problems due to absenteeism
Creates greater understanding of manufacturing quality issues

## Slide 93: Pay for Knowledge CAMI – Joint GM – Suzuki venture
Add incremental rewards to operators who learn more skills
When a operator learns all the operations in his / her work group he / she
  can be promoted to the role of utility or repair worker
  can fill in for absent operator without line disruption

## Slide 94: “Line Unbalance” Strategy in Mexican components plants due to high employee turnover
With large turnover training problems increase
Assign fewer work elements to new workers
Increase gradually to full “experienced worker standard”
Time
Fixed Job Cycle length
Experienced Worker Standard
New Employee
Operations

## Slide 95: Work Cells
The traditional assembly line can be inefficient, inflexible and uncomfortable
Group tasks in work cells
  5 to 8 operators
Allow personalization of work area
  Team identity, spirit
Reduce between operation transfers by equipment layout
  Non value added time
Use batch transfer between cells
Provide (controlled)buffers
  Allows flexibility

## Slide 96: Kitting
Typically components are presented in separate batches
“Kitting” groups sets of components to support a particular assembly sequence
Reduces non value added part selection and transfer time
Supports work cell and task enlargement arrangements
Requires up front kitting function perhaps at the component plant

## Slide 97: Vertical Job Enlargement
Vertical job enlargement adds managerial responsibilities to an individual’s operational responsibilities
  Quality, Productivity, Health and Safety responsibilities
Both operational and motivational improvements
Removes one layer of supervision
Utility workers fill in
Team members manage different support responsibilities

## Slide 98: Self Directed Work Teams
A natural progression of Administrative Controls such as rotation and enlargement is the creation of self directed work teams.
Self directed work teams can arrange assignments, rotations enlergements etc
They are also collectively responsible for quality, productivity, health, safety and satisfaction
Create “ownership” of total product
They also remove the need for first line supervisors
They will prevent the formation of bottom up informal “complaints” groups

## Slide 99: The Saturn Plant
Created in the 1980s with a greenfield plant, a brand new different product and a collaborative, participating union
Adopted self directed work teams
Used job rotation
Vertical enlargement – all the way up to the shared plant managers office
The process failed in the late 1990s due to poor product performance (design and engineering causes) and infiltration by the national Union with its traditional combative approach.

## Slide 100: Participation
Participation – “Vertical Job Enlargement” works
The people doing the job have the best knowledge of the causes of poor quality, productivity and health and safety.
Install ANDON Chord procedure
  Anyone can stop the line any time
This knowledge should be captured by the company and used to make improvements.

## Slide 101: Quality Management

## Slide 102: The Quality “Control” Myth
Measuring quality is like shutting the barn door after the horse has bolted
Quality is determined by PROCESS
If the PROCESS is managed then Quality will follow.
But it is still important to measure quality to observe trends
Quality charts should be used as described by Deming
  Do not interfere with “Common Causes”
  Only react to “Special Causes”
The Production Team usually has the knowledge to manage the PROCESS
PRODUCT QUALITY = COMPONENT QUALITY + PROCESS QUALITY

## Slide 103: The Toyota Production System W Edwards Deming Outcome measurement Statistical Quality Control The honest worker Prescriptive operations Simple TOOLs

## Slide 104: 5S, 5Whys etc.

## Slide 105: Visual Controls Plot Quality, Productivity, Health and Safety measurements over appropriate time scales Post the charts in the work area
Use Statistical Quality Control Methods

## Slide 106: Use “Loss Functions” rather than “Tolerances”
Tolerances
Target Specification
Loss Function
The principle of Continuous Improvement:
Kaizen Engineering
Target Dimension
“Good Enough”

## Slide 107: Toyota Production System
Principles
Eliminate waste
Visual controls
Standard processes
Quality circles(participation)
Kaizen - Continuous improvement
Simple Tools
5S – Tidy workplaces
Ishikawa Charts (6M)
5 Whys
Statistical process control
Lean
Agile
Participation
Quality Circles
Quality
Productivity

## Slide 108: Socio Technical Systems Macro Ergonomics Big Picture Ergonomics
E
P
B

## Slide 109: Frederick Herzberg Intrinsic motivation and Hygiene (dissatisfiers) factors Job Enrichment
Herzberg, F. 1968, "One more time: how do you motivate employees?", Harvard Business Review, vol. 46, iss. 1, pp. 53–62

## Slide 110: MacroErgonomics Hendrick 1990s Socio Technical Systems revisited Big Picture Ergonomics with micro ergonomics details
E
P
B

## Slide 111: Case Study: Job Redesign in the Bindery
Hong Kong university library
Hard covers on journals and books
10 people
Continuous work flow
  Batches within stages
The problems
  Access to library material, work in progress
  Equipment bottlenecks
  Physical environment
  Social context
  Productivity and job satisfaction

## Slide 112: The Changes
Redesign storage of periodicals waiting to be bound
Introduce cardex system for production control
Introduce small batch system with semi autonomous teams
Introduce job rotation and enlargement
Purchase new equipment, window blinds, task lighting, sound isolation
Rearrange the layout for functional flow
Review salary structure
Use some subcontracting for less skillful work
Protect the boss from the customers

## Slide 113: The Results (2 year follow up)
Better production control and accounting
Increased productivity
Removal of the backlog
Improved physical environment
Much happier customers
  Interface between the team and the customers
Improved job satisfaction
  Hawthorne effect?

## Slide 114: Case Study Organization and Job Design in Medicare Data Processing
200, mostly female clerical workers
High specialization
Open plan, functional zones, cubicles, noisy, untidy
Inefficiencies, backlogs, errors
New computer system
Low morale, threatened with takeover by subcontractor

## Slide 115: The Organizational Problems
Repetitive specialized work, electronic performance monitoring
System breakdowns
Noise, housekeeping – piles of paper
Low productivity, high costs
Low morale, conflict

## Slide 116: Solutions
Discussions of job enlargement with management
Introduction of pilot team”
  Selection of 6 volunteers, with broad background
  Team to take full batch through the whole process, except disbursements
Team responsible for layout of own department and allocation of duties
Carpeted the whole floor and isolated noisy printers
Talked to all the groups

## Slide 117: Results
Acceleration phase
  Physical layout and equipment installation
  Some learning and cross training
Productivity way up, errors down
High team morale
  Envy from the rest of the organization
Everybody liked the new carpet
Organization taken over by subcontractor

## Slide 118: Micro Ergonomics and Design
Workplace Design
  Access, Fit, Reach, Postures
Manual Materials Handling
  Lifting, Holding, Carrying, Pulling, Pushing
Manipulation
  Assembly work
Information Design
  Controls, Displays, Tools
Environment Design
  Light, Heat, Noise
Operations Design
  Tasks, Variety
Job Design
  Control, Breaks, Shifts, Supervision, Teams
Macro
+
Micro

## Slide 119: Workplace Design What can be Changed?
Space
  Reach, fit, postures, support
Force
  Moments and levers
  Pressure points
  Interfaces
  Mechanical assists
Time
  Static – dynamic balance
  Work rest schedules
  Shift work

## Slide 120: You can only change posture by changing the workPlace Layout but even then behaviors will differ

## Slide 121: The Box or the Ball Work (hand) placement for most of the time
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
Sitting
High Sitting
Leaning
Standing

## Slide 122: Visual, Light and Heavy Work
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
+ / - 20 cm

## Slide 123: Storage Rack Guidelines (North America)

## Slide 124: Adjustability and Flexibility
Where possible make workplaces adjustable to individual preference and allow / encourage change

## Slide 125: Manual Materials Handling
Major cause of back injuries
Measurement
  RULA
  NIOSH Lift Equation – Lifting
  Snook Tables – Pushing, Pulling
Change the task?
  Automation
  Mechanical assists
  Change the elements
    Load, Location, Frequency, Duration
Change the method?
  Lifting training

## Slide 126: Manual Materials Handling

## Slide 127: Lifting
Don’t put things on the floor!!
  Put them in the “Box” or “Ball”
Face the object
Move as close as possible to the object CG
Bend hips and knees
Keep back straight
Get a good grip
Don’t twist or jerk, lift smoothly

## Slide 128: MMH Measurement
NIOSH Lift Equation
Liberty Mutual (Snook) Tables

## Slide 129
1991 Version
RWL = LC x HM x VM x DM x AM x FM x DM x CM
A Discounting Equation
Lift Index = LOAD / RWL
Who is responsible for which intervention?

## Slide 130: Snook Tables

## Slide 131: Sources on the Internet
http://www.cdc.gov/niosh/docs/94-110/
http://www.emcins.com/losscontrol/quick_links/employee_safety_health/ergonomicsNIOSH.aspx
http://www.ergoweb.com/news/detail.cfm?id=566
http://www.ccohs.ca/oshanswers/ergonomics/niosh/calculating_rwl.html

## Slide 132: Manipulation / Assembly Tasks
Task requirements
  Visual, cognitive and motor
  Repetition
Outcomes
  Product quality and productivity issues due to
  Hand and arm pathology
  Postural strain – shoulder, neck
  Motion strain – shoulder, elbow, wrist, hand, thumb and fingers
Causes (and opportunities for intervention)
  Force, posture, movement, frequency, duration
Measurement
  Hand Activity Level
  Postural analysis
  Micro motion analysis
Interventions
  Remove, reduce or replace non value added work
  Task / Target Design
  Enlarge or rotate to reduce frequency

## Slide 133: Grasping and Manipulating
Fingers have postures too
How big are your hands?
How big should handles be?
How bent should handles be?
Length, Width, Circumference, Shape
Avoid pressure points

## Slide 134: Tight Targets Take Time

## Slide 135: The assembler had to deal with poorer ACCess and many more components

## Slide 136: Two Automobile Plants
Part Insertion Time
  6.3 secs
  3.9 secs
Target size, orientation ?

## Slide 137: Targets
A
B
Design for Assembly!
Which Targets are Easier?

## Slide 138: Fitts Law(1954)
MT = a + b log2 (2A/W)
where:
MT = Movement Time
a, b = Individual and Situational Constants
A = Amplitude of Movement
W = Width of Target
2A/W = Index of Difficulty (ID)

## Slide 139: Case Study Barbie Dolls
How long does it take to assemble and pack a set of clothes for a Barbie Doll?
How many assemblies per day?
How many workers are needed?
TARGETS!!!

## Slide 140: Target Rules
Increase Target Size Percentage
  Access, Adjustment, Finesse
Consider Effect of Part Weight
Consider Effect of Part Size
Large time and postural stress savings by targeting the targets

## Slide 141: A compromise between user styling requirements and design for manufacturability, even robots have a hard time with TIGHT Targets
“Thin is in” for the customer, but what about the assembler?

## Slide 142: Simplify Choices Choices Take Time and may be Wrong

## Slide 143: Choices Exercise
Hold a pack of playing cards face down
Sort them into 2 piles
Sort them into 4 piles
Sort them into RED and BLACK
Sort them into H, C, D, S
  Hick’s Law MT = a + b log2n
  where: n = number of choices
Measure the Times, Observe the Errors and Hesitations

## Slide 144: Arms, Wrists and Fingers have Postures too
Orient the part
Bend the tool not the wrist
Increase the size of the handle to reduce pressure and force requirements and increase leverage

## Slide 145: Wrists have Postures too

## Slide 146: Sewing Lines

## Slide 147: Small Components Assembly

## Slide 148: Bend the Tool not the Wrist

## Slide 149: Use the right Handle

## Slide 150: Orient the job

## Slide 153: Job and Operations Design The Time factor

## Slide 154: Operations Design
The key to productivity is the removal of non value added work
  Long or frequent transfers
  Search for components or target
  Reorienting the component / product
Use belts / gravity for transfers, components
Place tools / components in the operations sequence
Use belt / gravity for finished goods

## Slide 155: Job Design
Taylorism
  Job simplification
  Managers manage workers work
But workers are able to master many tasks
Workers do have insight into quality, productivity and health and safety issues
Workers do not like to be bored
  Vigilance decrement may be a problem
  Local and general fatigue will be a problem
Therefore design job variety

## Slide 156: Shift Work
Avoid one week rotations
Implement permanent shifts
Implement short cycle shift schedules
  2 – 3 days
  Use forward rotation: Day – Evening – Night – Off
Limit shift durations
  8 is better than 10 and 12 is the limit
  4 crew 3 shift or 3 crew 2 shift arrangements
Provide one long and many short relief breaks for assembly work
  Walking for at least 5 minutes every hour

## Slide 157: Singapore MOM ergo@work app
Postures, stretches, breaks

## Slide 158: Physical Work Stress Index (PWSI) Addressing the TIME Dimension

## Slide 159: PWSI
The Physical Work Stress Index (PWSI) is a simple, robust physical activity measurement system that indicates an optimal level of workload between high static and high dynamic demands.
It uses an activity sampling approach which can be applied to regular (cyclic) work and irregular work over short or long time periods.
The PWSI may be developed as a manual assessment tool or through the use of a spreadsheet

## Slide 160: Physical Stress and Strain People respond well to optimal levels of physical (and cognitive) variety
Strain
Stress

## Slide 161: History
The PWSI was first developed as a student project at the University of Hong Kong in 1976 (Brian Peacock, Janet Liu)
It was further developed at the University of Oklahoma through undergraduate and graduate projects during the early 1980s (Susan Cheatwood, Jacob Chen)
A description of the process was published by Chen, Peacock, and Schlegel in 1989 in the International Journal of Industrial Ergonomics

## Slide 162: Activity Sampling
A random or regular sampling scheme is developed depending on the periodicity of the work activity.
  For regular, machine paced work, a random sample is recommended.
  For irregular work, a regular sampling process is both convenient and valid.
The ordinal mappings from values of each of these major elements are recorded at each sampling instant
Generally it is appropriate to gather data from about 10 samples but greater precision can be achieved by increasing the number of observations

## Slide 163: The Box or the Ball Work (hand) placement for most of the time
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
Sitting
High Sitting
Leaning
Standing

## Slide 164: The Best Posture is the Next Posture

## Slide 165: Walkie-Talkies
Require all employees to walk and talk every hour for 5 minutes
  Walking provides physical relief
  Talking provides social relief
  Walking and talking provide attention relief
  Productivity will not suffer

## Slide 166: Stretching
Systematically and slowly move every joint through its full range
  Move, hold for 3 seconds, relax
Standing (hold on to the back of the chair)
  Move knee up then push leg back
  Move leg across the body, away from the body and in big circles
Sitting
  Bend forward, back, side to side, and twist
  Move shoulders and shoulder girdles in big circles
  Move wrist and hands through full range
  https://itunes.apple.com/sg/app/ergo-work/id556877197?mt=8

## Slide 167: The Usain Bolt fitness test 10 – 100 – 1000 - 10000
Distance (m) | World Record (sec) | Your Time (secs) | Your %
10 | 1 | 5 | 20
100 | 10 | 40 | 25
1000 | 130 | 400 | 43
10000 | 1600 | 4000 | 40
Participants should walk or run 10, 100, 1000, 10000 meters, measure their times and calculate their percentage score against the world record.

## Slide 168: Workability Index
Addresses
  Spatial factors
  Manual materials handling
  Manipulation
  Environmental factors
  Information factors
  Operational factors

## Slide 169: Workability Index
Date |  |  |  |  |  |  |  |  |  |  | Job Description | 
Analyst |  |  |  |  |  |  |  |  |  |  |  | 
Survey Reference / Times |  |  |  |  |  |  |  |  |  |  |  | 
Job Survey Ratings |  |  |  |  |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
 | Place a small "x" in the appropriate rating cell | N/A | Green |  | Yellow |  | Orange |  | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria

## Slide 170
Policy Decisions
Engineering Variable or Composite Index
Common Currency
Outcome Scale
7
6
5
4
3
2
1
Unacceptable
Range
Ideal Range
Region of Interactions and Continuous Improvement
Policy Statements
1
2
3
4
6
5
7

## Slide 171
Design Rules - Consensus
Policy
Science
History
Experience
Evaluation
  Verification
  Validation
  Sensitivity
Predictions
Design
Rule
Rule
Implementation
Data
Consensus:
  HF Experts
  Engineers
  Managers
  Customers
Technical
Memory

## Slide 172: Spatial Factors
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Access |  |  |  |  |  |  |  | Clearances, obstructions, doors, barriers
Fit |  |  |  |  |  |  |  | Head room, Knee / Foot room, Width
Reach |  |  |  |  |  |  |  | Box, 50 cm reach curves
Postures |  |  |  |  |  |  |  | Sitting, Standing, Squatting, Middle, Outer, Inner ranges
Movements |  |  |  |  |  |  |  | Range, speed
Task surface orientation |  |  |  |  |  |  |  | Front, above, below, behind
Ramps |  |  |  |  |  |  |  | Slope, length
Stairs |  |  |  |  |  |  |  | Number, height
Counts |  |  |  |  |  |  |  | Refer to HF Specialist, manufacturing engineer for interventions

## Slide 173: Manual Materials Handling
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Lifting |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Carrying |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Holding |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Pulling |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Pushing |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Twisting, bending |  |  |  |  |  |  |  | Vertical and horizontal task locations
Interfaces, coupling |  |  |  |  |  |  |  | Good, sharp
Counts |  |  |  |  |  |  |  | Refer to NIOSH Lifting Equation and Snook Tables

## Slide 174: Manipulation
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Shoulder, Elbow |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces
Hand, Wrist, Fingers |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces, coupling, interfaces
Targets |  |  |  |  |  |  |  | Target sizes and tolerances
Precision |  |  |  |  |  |  |  | Fine, coarse
Counts |  |  |  |  |  |  |  | Use Hand activity level TLVs

## Slide 175: Environmental Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Heat, Cold |  |  |  |  |  |  |  | Air Temperature, Humidity, Radiant heat, Air movement
Glare |  |  |  |  |  |  |  | Location, intensity, contrast, window and local lighting
Dark |  |  |  |  |  |  |  | Interference with visual demands
Noise Intensity |  |  |  |  |  |  |  | Task, Ambient, Sound Level, Frequency, Variability
Vibration |  |  |  |  |  |  |  | Whole body, hand arm
Accelerations |  |  |  |  |  |  |  | Pounding, jerks
Slip, trip, fall |  |  |  |  |  |  |  | Work context hazards, visibility, barriers
Chemical |  |  |  |  |  |  |  | Refer to OH
Radiation |  |  |  |  |  |  |  | Refer to OH
Counts |  |  |  |  |  |  |  | Refer to OH, Safety or Engineering for intervention

## Slide 176: Information Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Visual |  |  |  |  |  |  |  | Visual acuity, discrimination demands, importance
Acoustic |  |  |  |  |  |  |  | Hearing acuity, discrimination demands, importance
Attentional |  |  |  |  |  |  |  | Sustained and divided attention demands
Memory |  |  |  |  |  |  |  | Operational memory span, interferences
Cognitive |  |  |  |  |  |  |  | Calculations, planning, analyses
Decisions |  |  |  |  |  |  |  | Number of choices, ambiguity, risk
Communication |  |  |  |  |  |  |  | Frequency, variability, importance
Control |  |  |  |  |  |  |  | Precision, feedback, prediction
Situation awareness |  |  |  |  |  |  |  | Importance, distractions
Mental workload |  |  |  |  |  |  |  | Information and time demands, training, stress
Outcomes |  |  |  |  |  |  |  | Consequences of human error
Counts |  |  |  |  |  |  |  | Refer to HF specialist for intervention

## Slide 177: Operational Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
 |  |  |  |  |  |  | Operational factors will usually interact with some or all of the other factors | Intervention through administrative and / or operational controls
Job cycle duration |  |  |  |  |  | Engineering issues |  | Operations per hour, job cycle time
Static posture duration |  |  |  |  |  |  |  | % job cycle, % day
Repetitions, frequencies |  |  |  |  |  |  |  | Frequency per hour of same or similar task
Job pacing |  |  |  |  |  |  |  | Self paced, Piece Rate, Machine paced, Supervisor
Span of responsibility |  |  |  |  |  | Operational Issues |  | Product quality, other colleagues, autonomy
Team structures |  |  |  |  |  |  |  | Job rotations
Participatory processes |  |  |  |  |  |  |  | Do employees participate in work design decisions
Technical support |  |  |  |  |  |  |  | Availability, supervision
Training, Acclimatization |  |  |  |  |  |  |  | Level of experience, adaptation to task
Special Populations |  |  |  |  |  |  |  | Are eldely or disabled persons employed with accommodations?
Counts |  |  |  |  |  |  |  | Refer to HF Specialist / Management for intervention

## Slide 178: Overall Counts
 |  |  | Job Survey Ratings |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
 | Place a small "x" in the appropriate rating cell |  | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Overall Counts 1 |  |  |  |  |  |  |  |  | Notes | Engineering Controls
 |  | 2 |  |  |  |  |  |  | Jobs should be analysed before and after interventions | 
 |  | 3 |  |  |  |  |  |  | The worksheet may also be used repeatedly over a day to analyse the variability of work demands | Administrative Controls
 |  | 4 |  |  |  |  |  |  | Consensus quantitative anchors may be added to the rating scales to improve their consitency | 
 |  | 5 |  |  |  |  |  |  | Basic training (1 day) in the use of this worksheet should be required of all ergonomics monitors (CEM Level 1) | 

## Slide 180: Conclusions – How Ergonomics Works

## Slide 181: Ergonomics Addresses
human, technological, contextual and operational complexity and variability
tradeoffs among many job outcomes
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E
Physical
Cognitive
Social
Affective
Context
Temporal
Sensory
E
P
B
E4S4
Macro
+
Micro