## Slide 1: The Ergonomics of Production Lines Measurement and Interventions from the Factory to the Office
Brian Peacock
SIM University
National University of Singapore

## Slide 2: Some Interesting Articles by Dr Chen
"A Fuzzy Sets Modeling Approach for Ergonomic Workload Stress Analysis", International Journal of Industrial Ergonomics (1994)
"A Computer Assisted System for Physical Ergonomics Analysis", Computers in Industrial Engineering (1991)
"An Observational Technique for Physical Work Stress Analysis", International Journal of Industrial Ergonomics, No.3 (1989)
"A Database Management System for Ergonomics Information Analysis,“ Trends in Ergonomics/Human Factors V, Elsevier (1988)
"Prototype Expert System for Physical Work Stress Analysis“ Trends in Ergonomics/Human Factors IV (1987)
"EVA Suit Glove Design." Space Tech '85 Conference, Anaheim, California (1985)
"An Interactive Biomechanical Lifting Model,“ Mid Central Human Factors/Ergonomics Conference, West Lafayette, Indiana (1985)

## Slide 3: The History of Ergonomics
Tools

## Slide 4: Human Factors Engineering / Ergonomics
Analysis
and
Design
with People in Mind

## Slide 5: An adaptation of the Edwards “SHEL” model
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E
Complexity

## Slide 6: Ergonomics Complexity
serves many PURPOSES
surrounded by VARIABILITY
swamped by CONTEXT
complicated by INTERACTIONS
contends with SPACE, FORCE and TIME
driven by INFORMATION and AFFECT
deals with BENEFITS, RISKS and TRADEOFFS

## Slide 7: Variability
Ergonomics Purpose and Achilles' Heel
Physical
Cognitive
Social
Affective
Context
Temporal
Sensory

## Slide 8: Product Life Cycle
Requirements
Concept
Development
Concept
Selection
Specifications
Tooling
Production
Marketing
Use and
Misuse
Maintenance
Disposal
Feedback, Technical Memory
Many Customers
(including the shareholders)
Design Team
Many Requirements
Feedforward (Anticipation)

## Slide 9: Big Picture Ergonomics
Force
Space
Time
Connections
Gravity
Posture
Reach
Access
Duration
Frequency
Sequence
Fit
E
P
B

## Slide 10: Many Responsibilities
Force
Space
Time
Product Engineer
Packaging Engineer
Manufacturing Engineer
Industrial Engineer
E
P
B

## Slide 11: Infrormation and Affect
Force
Space
Time
E
P
B
Information
Affect

## Slide 12: Big Picture Ergonomics Purposes
Effectiveness Quality
Efficiency Productivity
Ease of Use Comfort and Convenience
Emotional Appeal Pleasant job and context
Safety/Health Acute Injuries and Chronic Illnesses
Security Malicious Third Parties
Satisfaction Of ALL concerned
Sustainability Reliability AND Resilience
If you can’t / don’t measure it you can’t manage it
There will be tradeoffs
E4S4
E
P
B

## Slide 13: Multiple Purposes of Design
Effectiveness
  Meets functional requirements
  “quality”
Efficiency
  Optimal use of resources
  “productivity”
Ease of Use
  Intended users
  Comfort and Convenience
  Prevention of misuse
Elegance
  Esthetic / emotional appeal
  Affective Design
Safety and Health
  Prevention or mitigation of system failures
  For participants and third parties
Security
  Inadvertent or malicious misuse
Satisfaction
  Of ALL customers and stakeholders
There WILL be tradeoffs
Sustainability
  Reliability
    Under intended contexts over the life cycle
  Resilience
    Under unintended, unexpected and harsh conditions
E4S4

## Slide 14: The Purposes of Ergonomics
Contributing to the Multiple Purposes of Design
Helping with the tradeoffs
E4S4
Productivity
Safety

## Slide 15: The 6Us and 2Ms of Usability
Utility
  Is the system useful?
Usage and Misusage
  How and in what context will the system be used?
  What possible extreme contexts may be predicted
Usability
  Is the system easy to use or misuse?
Utilization
  How often and by how many people is the system used?
Users and Misusers
  Who are the users and possible misusers?
User Error
  What kinds of error can be made, when and how will they be made, how frequently and what are the possible consequences?
6U
2M

## Slide 16: Activities of Ergonomists rasdei
Analysis
Design
Usability Testing
Outcome Investigation
Objective Feedback
(Fuzzy) Prediction
Research
External
Forces
Simulation

## Slide 17: The Ergo Cop Problem
Design
Specifications
Ergonomics
Evaluation
The Ergocop
Design
Performance
Review
(waivers by management)
Performance
Requirements
Performance
Review
Precise
Design
Specifications
Ergonomics
Support
Design
Clear
Performance
Requirements
Time to
Market
Calling the designer’s baby ugly!

## Slide 18: Human Factors Applications Need
Domain Knowledge
Measurement and analysis tools
Knowledge of human characteristics, capabilities and limitations

## Slide 19: The Practice of Ergonomics
Breadth– Domain Knowledge
Agriculture, Gas and Oil, Manufacturing, Textiles, Transportation, Consumer Products, Service Industry, Sport and Recreation, Rehabilitation, Aviation, Space Exploration
Process
Depth
Investigation
Evaluation
Design
Simulation
Analysis
Research
Domain
Depth
Get help where it is needed
The
Shaped Profession

## Slide 20: The Broad Scope of Ergonomics
Physical
Sensory
Cognitive
Social and Cultural
Affective
Environmental
Temporal

## Slide 21: Physical Ergonomics
Shape
Size
Strength
Speed
Stamina
Skill

## Slide 22: People vary in Shape and Size

## Slide 23: People vary in their Strength

## Slide 24: People Vary in their Skills

## Slide 25: People vary in their Speed

## Slide 26: People vary in their Stamina

## Slide 27: Sensory Factors
Vision
Touch
Taste
Proprioception
Smell
Hearing

## Slide 28: What happens when you grow old?

## Slide 29: Are you Colorblind?
1. Normal Color Vision: A: 29, B: 45, C: --, D: 26
2. Red-Green Color-Blind: A: 70, B: --, C: 5, D: --
3. Red Color-blind: A: 70, B: --, C: 5, D: 6
4. Green Color-Blind: A: 70, B: --, C: 5, D: 2

## Slide 30: Cognitive Factors
Sensing
Deciding
Learning
Planning
Perceiving
Attending
Communicating
Controlling
Calculating
Understanding
Remembering
Forgetting

## Slide 31: Cognition is complex
Evaluating
Diagnosing
Judging
Deciding
Planning
Investigating
Predicting
Analyzing
Problem Solving
Cognition
Learning
Interpolating and Extrapolating
Goals
Understanding
Synthesizing

## Slide 32: People vary in their Cognitive abilities

## Slide 33: Cognition
Attending
Perceiving
Understanding
Predicting
Deciding
Remembering
Communication
Control
Learning

## Slide 34: Cognition is Complex

## Slide 35: Affective Factors
Emotion
Esthetics
Elegance
Attitude
Mood
Motivation
Excitement

## Slide 36: Environmental Factors
Acoustic
Communication
Hearing loss
Thermal
Heat
Humidity
Cold
Air movement
Vibration
Hand / Arm
Whole body
Light and Dark
Vision
Contrast
Color
Chemical and Biological
Gravitational
Space
Pressure
Under Water
Altitude

## Slide 37: Environmental Design - Lighting
Provide natural lighting
Provide sufficient lighting
Avoid glare
Provide special purpose lighting to emphasize task features

## Slide 38: Environmental Design - Noise
Reduce damaging / distracting / interfering noise
  At source
  By barriers
  By PPE
  By exposure reduction (rotation)
Enable task information, communications and alarms distinct from ambient noise
Allow / provide music if it doesn’t interfere with task or colleagues

## Slide 39: Environmental Design - Heat
Maintain air temperature between 220 C – 260 C
  For sedentary work (cooler for physical work)
  Allow some fluctuation
Maintain relative humidity necessary for process
  generally between 30% – 50%
Enable air movement
  Avoid drafts
Address / control radiant heat / cold sources

## Slide 40: Social and Cultural Factors
Customers
Groups
and
Teams
Hierarchies
Cooperation
Communication
Competition
Language
and
Jargon
Roles
Jobs
Supervision
Businesses and Companies
Laws
Rules and Regulations
Traditions
Infrastructure
Economics
Politics
Religions
Suppliers
Organizational
Design

## Slide 41: Social Factors?

## Slide 42: Time Factors
Job Cycle Time
History
Task Pacing
Remembering
Acceleration
Velocity
Decision Time
Movement Time
Reaction Time
Psychological Refractoriness
Age
Fatigue
Vigilance
Circadian Rhythms
Mental Workload
Duty Cycle
Shift Length
Timing

## Slide 43: The Process of Ergonomics
$
Decisions
Benefits, Costs,
Risks, Tradeoffs
Measurement and Analysis
Screening
In depth Research
Contexts
Spatial, Physical, Mechanical, Chemical, Biological, Geographical, Social, Political, Economic
Design
Tools, Equipment, Workplaces, Tasks, Procedures, Assignments.
The Job
Outcomes
Quality
Productivity
Health, Safety
Ease of Use
Security
Satisfaction
Sustainability

## Slide 44: Workplace Ergonomics

## Slide 46: Workplaces

## Slide 47: Postures and Environments

## Slide 48: Physical Workloads

## Slide 49: Awkward Postures

## Slide 50: Control Room

## Slide 51: Assembly Work

## Slide 52: The Office

## Slide 53: The Modern Office

## Slide 54: The Typing Pool

## Slide 55: Call Centers in the Phillipines

## Slide 56: Assembly Operations

## Slide 57: The Mobile Workplace

## Slide 58: The History of Assembly Lines

## Slide 59: I love Lucy, Chocolate wrapping line.
http://www.google.com/url?sa=t&rct=j&q=lucy%20chocolate%20factory&source=web&cd=2&cad=rja&ved=0CCkQtwIwAQ&url=http%3A%2F%2Fwww.youtube.com%2Fwatch%3Fv%3DFGfplQ1FUFs&ei=_eJWULi3IYHNrQf28oCYBw&usg=AFQjCNHkkfIbZobjKqrGwXuspX-A1XPfVQ
http://lloyddeleon.multiply.com/video/item/4/I_Love_Lucy_--_at_chocolate_factory
https://www.youtube.com/watch?v=8NPzLBSBzPI

## Slide 60: Henry Ford – Work Simplification

## Slide 61: Bring the Work to the Worker

## Slide 62: Frederick Winslow Taylor - “Taylorism”
Scientific Management
Managers Manage, Workers Work
Prescriptive work methods

## Slide 63: Lillian and Frank Gilbreth
Time, Motion and Fatigue Studies
Micro motion – “Therbligs”

## Slide 64: Therbligs
Reach
Grasp
Move
Hold
Release
Use
Pre-position
Position
Assemble
Disassemble
Search
Select
Plan
Inspect
Unavoidable Delay
Avoidable delay
Rest

## Slide 65: Hawthorne Studies
Employees motivated by the attention given to them rather than impersonal change in working conditions (lighting)

## Slide 66: Tavistock Institute
Socio Technical Systems
Coal Mining
The Importance of Human Centered Design

## Slide 67: Frederick Herzberg Intrinsic motivation and Hygiene (dissatisfiers) factors Job Enrichment
Herzberg, F. 1968, "One more time: how do you motivate employees?", Harvard Business Review, vol. 46, iss. 1, pp. 53–62

## Slide 68: MTM
Methods-Time Measurement is a procedure for improving methods and establishing time standards by recognizing, classifying, and describing the motions used or required to perform a given operation and assigning pre-determined time standards to these motions.
The foundation of modern Work Measurement and Industrial Engineering

## Slide 69: Automobile Assembly

## Slide 70: Overhead Work

## Slide 71: Lots of Components
Lots of savings by removing none value added activities

## Slide 72: Sewing Lines

## Slide 73: Meat Packing

## Slide 74: Boeing Assembly Line

## Slide 75: Electronics

## Slide 76: Foxconn

## Slide 77: Production lines brought enormous improvement in Productivity by the removal of Non Value added work and the improvement of Process consistency / Quality But at what cost?

## Slide 78: Measurement Industrial Engineering

## Slide 79: Industrial Engineering The Job Cycle
Transport
Grasp
Attach
Inspect
Return
Time

## Slide 80: Work Measurement
Puropses
  Productivity
  Quality
Micro motion analysis
Remove non value added activities
  Searches, decisions, movements, (checks)
Work simplification
  Reduce the job cycle
  Shortens learning time
  Improves Productivity and Quality?

## Slide 81: Efficiencies

## Slide 82: Vehicle Height

## Slide 83: Skillets – Work height adjustment

## Slide 84: Wiring Harness Assembly Line

## Slide 85: Assembly Lines

## Slide 86: The Job Cycle (varies between a few seconds, a few minutes and even a few hours)
Check
Position
Cycle Time
Force
*
Posture
Transport
Grasp
Reach
Attach
Return / Rest

## Slide 87: The Industrial Engineering Solution Cut off the peaks of Force and Posture, Reduce Non value Added work and Fill up the Job Cycle
Check
Position
Cycle Time
Force
*
Posture
Transport
Grasp
Reach
Attach
Return / Rest

## Slide 88: Task Aids

## Slide 89: Robots

## Slide 90: Robots

## Slide 91: Tool balancers

## Slide 92: Doors Off

## Slide 93: Tilt the Task

## Slide 94: The Results Improved Productivity But increased Static Work
Cycle Time
Force
*
Posture
Transport
Grasp
Attach
Grasp
Attach
Transport
Transport
Grasp
Attach
Line Balance

## Slide 95: The $64,000 Question?
Does (pseudo) Ergonomics cause Illness and Injury?
“Ergonomic / Iatrogenic Disease”
Long durations, low forces, near neutral postures, high repetitions

## Slide 96: The CTD Epidemic Repetitive motion strain Occupational overuse syndrome
Meatpacking
Nursing homes
Automobile manufacturing
Parcel handling
Electronics manufacturing
Textiles
Food processing
Textiles
Checkout counters
etc
Years of Contentious / Combative dialog among Government (NIOSH / OSHA)
Business (NAM, COT), and Unions (UAW)
providing many opportunities for Ergonomics Researchers, Professionals, Practitioners and Product developers

## Slide 97: Upper Limbs and Backs

## Slide 98: Sedentary Work leads to metabolic disorders – obestity, circulatory disease, diabetes
Ergonomic
X

## Slide 99: Sedentary, Static and Repetitive Work lead to:
Repetitive Strain Injury
  Musculo skeletal disorders
Metabolic disorders
  Obesity, circulatory disorders, diabetes
Cognitive dullness
  Lack of flexibility
Job dissatisfaction
  Absenteeism
  Industrial unrest
Operational deterioration
  Productivity, quality

## Slide 100: Administrative Interventions
Time

## Slide 101: Administrative Interventions Job Design
Job Enlargement
Job Rotation
Decoupled assembly lines
Work Cells
Vertical job enlargement
Team structures
Participation
“Andon Chords”

## Slide 102: The Rest Pause Question
Are frequent short breaks “better than” less frequent long breaks?
The “Psycho-Social” Answer - No
  People invariably “work ahead” to increase “discretionary time”
The Physiological Answer – Maybe
Rest pauses need managing

## Slide 103: The Job Cycle
Check
Position
Cycle Time
Force
*
Posture
Transport
Reach
Attach
Return / Rest
Grasp

## Slide 104: Horizontal Enlargement Increase the cycle time, put more (different) functions into the job cycle
Increased Cycle Time
(Load up to 90%)
Varied Force and Posture

## Slide 105: Horizontal Job Enlargement
Increase the duration of the work cycle and the number of job cycle elements
  Is of minimal (physical) value if all the elements are physically similar
    May increase static workload
  Will need greater training effort to achieve acceptable productivity and quality standards
    Will cause staffing problems with large labor turnover
May create greater understanding of the product, subassembly and quality, allows productivity shortcuts by parallel manual / cognitive work element overlap
Will be of significant physical value if the job elements are (physically) dissimilar
  May lead to excessive dynamic work load

## Slide 106: Horizontal Job Enlargement Examples
NUMMI
  Joint Venture between GM – Toyota
  Selected work force
  Team structure
  Participation
  5 minute job cycle
Lansing Craft Center
  Very long cycles
  Non valued added components handling

## Slide 107: Kitting
Typically components are presented in separate batches
“Kitting” groups sets of components to support a particular assembly sequence
Reduces non value added part selection and transfer time
Supports work cell and task enlargement arrangements
Requires up front kitting function perhaps at the component plant

## Slide 108: Job Rotation
Work on one set of task elements then rotate onto another set
  Is of minimal (physical) value if all the elements are physically similar
    May increase static workload
  Will need greater training effort to achieve acceptable productivity and quality standards
    Will cause staffing problems with large labor turnover
May create greater understanding of the product or subassembly
Will be of significant physical value if the job elements are (physically) dissimilar

## Slide 109: The Hidden Advantages of Horizontal Job Enlargement and Rotation
Adds more knowledge and skills to the individual worker
Creates greater flexibility in job assignment
Resolves line balance problems due to absenteeism
Creates greater understanding of manufacturing quality issues

## Slide 110: Pay for Knowledge CAMI – Joint GM – Suzuki venture
Add incremental rewards to operators who learn more skills
When a operator learns all the operations in his / her work group he / she can be promoted to the role of utility worker – can fill in for absent operator without line disruption

## Slide 111: “Line Unbalance” Strategy in Mexican components plants due to high employee turnover
With large turnover training problems increase
Assign fewer work elements to new workers
Increase gradually to full “experienced worker standard”
Time
Fixed Job Cycle length
Experienced Worker Standard
New Employee
Operations

## Slide 112: Job Rotation
Task
1
Task
2
Task
3
Rotate every ½ , 1, 2 hours or on different days or even weeks

## Slide 113: Decoupling
Separate cells by buffers so that teams are self rather than line paced
Allows for flexible response to variable conditions
Allows work to continue if there is a problem up or down the line

## Slide 114: Work Cells
The traditional assembly line can be inefficient, inflexible and uncomfortable
Group tasks in work cells
  5 to 8 operators
Allow personalization of work area
  Team identity, spirit
Reduce between operation transfers by equipment layout
  Non value added time
Use batch transfer between cells
Provide (controlled)buffers
  Allows flexibility

## Slide 115: Vertical Job Enlargement
Vertical job enlargement adds managerial responsibilities to an individual’s operational responsibilities
  Quality, Productivity, Health and Safety responsibilities
Both operational and motivational improvements
Removes one layer of supervision
Utility workers fill in
Team members manage different support responsibilities

## Slide 116: Self Directed Work Teams
A natural progression of Administrative Controls such as rotation and enlargement is the creation of self directed work teams.
Self directed work teams can arrange assignments, rotations enlergements etc
They are also collectively responsible for quality, productivity, health, safety and satisfaction
Create “ownership” of total product
They also remove the need for first line supervisors
They will prevent the formation of bottom up informal “complaints” groups

## Slide 117: The Saturn Plant
Created in the 1980s with a greenfield plant, a brand new different product and a collaborative, participating union
Adopted self directed work teams
Used job rotation
Vertical enlargement – all the way up to the shared plant managers office
The process failed in the late 1990s due to poor product performance (design and engineering causes) and infiltration by the national Union with its traditional combative approach.

## Slide 118: The Politics of Self Directed Work Teams
In the Toyota Production System “Self Directed Work Teams” are created by management
The team members are motivated to improve quality and productivity, with the constraint of health, safety and satisfaction
Without the teams, disgruntled groups form (hierarchical) unions, whose motivations may not gel with those of management

## Slide 119: The “Job Enrichment” Myth
It is possible to intervene with engineering and administrative devices but “enrichment” is an emotional characteristic of the individual employee – some may prefer simple repetitive jobs others may be more ambitious, but if there are incentives associated with the change then administrative interventions may be “enriching”

## Slide 120: Participation
Participation – “Vertical Job Enlargement” works
The people doing the job have the best knowledge of the causes of poor quality, productivity and health and safety.
Install ANDON Chord procedure
  Anyone can stop the line any time
This knowledge should be captured by the company and used to make improvements.

## Slide 121: Quality Management

## Slide 122: The Quality “Control” Myth
Measuring quality is like shutting the barn door after the horse has bolted
Quality is determined by PROCESS
If the PROCESS is managed then Quality will follow.
But it is still important to measure quality to observe trends
Quality charts should be used as described by Deming
  Do not interfere with “Common Causes”
  Only react to “Special Causes”
The Production Team usually has the knowledge to manage the PROCESS
PRODUCT QUALITY = COMPONENT QUALITY + PROCESS QUALITY

## Slide 123: The Toyota Production System W Edwards Deming Outcome measurement Statistical Quality Control The honest worker Prescriptive operations Simple TOOLs

## Slide 124: Toyota Production System
Principles
Eliminate waste
Visual controls
Standard processes
Quality circles(participation)
Kaizen - Continuous improvement
Simple Tools
5S – Tidy workplaces
Ishikawa Charts (6M)
5 Whys
Statistical process control
Lean
Agile
Participation
Quality Circles
Quality
Productivity

## Slide 125: 5S, 5Why etc.

## Slide 126: Special and Common Causes
Do not TAMPER with common causes

## Slide 127: Use “Loss Functions” rather than “Tolerances”
Tolerances
Target Specification
Loss Function
The principle of Continuous Improvement:
Kaizen Engineering
Target Dimension
“Good Enough”

## Slide 128: Socio Technical Systems revisited
E
P
B
MacroErgonomics Hendrick
1990s Big Picture Ergonomics with micro ergonomics details
Understand that there are multiple customers and requirements
E4S4

## Slide 129: Case Study: Job Redesign in the Bindery
Hong Kong university library
Hard covers on journals and books
Continuous work flow
  Batches within stages
The problems
  Access to library material, work in progress
  Equipment bottlenecks
  Physical environment
  Social context
  Productivity and job satisfaction

## Slide 130: The Changes
Redesign storage of periodicals waiting to be bound
Introduce cardex system for production control
Introduce small batch system with semi autonomous teams
Introduce job rotation and enlargement
Purchase new equipment, window blinds, task lighting, sound isolation
Rearrange the layout for functional flow
Review salary structure
Use some subcontracting for less skillful work
Protect the boss from the customers

## Slide 131: The Results (2 year follow up)
Better production control and accounting
Increased productivity
Removal of the backlog
Improved physical environment
Much happier customers
  Interface between the team and the customers
Improved job satisfaction
  Hawthorne effect?

## Slide 132: Case Study Organization and Job Design in Medicare Data Processing
200, mostly female clerical workers
High specialization
Open plan, functional zones, cubicles, noisy, untidy
Inefficiencies, backlogs, errors
New computer system
Low morale, threatened with takeover by subcontractor

## Slide 133: The Separate Functions
Receiving claims
Checking with suppliers and patients
Data input (classroom style)
Checking data
Special investigations
Disbursements

## Slide 134: The Organizational Problems
Repetitive specialized work, electronic performance monitoring
System breakdowns
Noise, housekeeping – piles of paper
Low productivity, high costs
Low morale, conflict

## Slide 135: Solutions
Discussions of job enlargement with management
Introduction of pilot team”
  Selection of 6 volunteers, with broad background
  Team to take full batch through the whole process, except disbursements
Team responsible for layout of own department and allocation of duties
Carpeted the whole floor and isolated noisy printers
Talked to all the groups

## Slide 136: Results
Acceleration phase
  Physical layout and equipment installation
  Some learning and cross training
Productivity way up, errors down
High team morale
  Envy from the rest of the organization
Everybody liked the new carpet
Organization taken over by subcontractor

## Slide 137: Micro Ergonomics and Design
Workplace Design
  Access, Fit, Reach, Postures
Manual Materials Handling
  Lifting, Holding, Carrying, Pulling, Pushing
Manipulation
  Assembly work
Information Design
  Controls, Displays, Tools
Environment Design
  Light, Heat, Noise
Operations Design
  Tasks, Variety
Job Design
  Control, Breaks, Shifts, Supervision, Teams
Macro
+
Micro

## Slide 138: Workplace Design What can be Changed?
Space
  Reach, fit, postures, support
Force
  Moments and levers
  Pressure points
  Interfaces
  Mechanical assists
Time
  Static – dynamic balance
  Work rest schedules
  Shift work

## Slide 139: Workplace Design
Measurement
Design
Anthropometry
Postural analysis
  The Box and the Ball
Movement analysis
  Ranges
  Macro motion analysis
  Micro motion analysis
Adjustability and flexibility
  Seat and task heights
    Lower limb, trunk and neck, arm posture
  Orientations
    Neck, arm and hand postures
  Allow variable postures
    Stand, sit , lean
  Provide support for stability
    Body weight, back, arms, feet

## Slide 140: You can only change posture by changing the workPlace Layout but even then behaviors will differ

## Slide 141: The Box or the Ball Work (hand) placement for most of the time
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
Sitting
High Sitting
Leaning
Standing
+ / - 20 cm

## Slide 142: Adjustability and Flexibility
Where possible make workplaces adjustable to individual preference and allow / encourage change

## Slide 143: Manual Materials Handling

## Slide 144: Manual Materials Handling
Major cause of back injuries
Measurement
  RULA
  NIOSH Lift Equation – Lifting
  Snook Tables – Pushing, Pulling
Change the task?
  Automation
  Mechanical assists
  Change the elements
    Load, Location, Frequency, Duration
Change the method?
  Lifting training

## Slide 145: Low Back Strain
The most common disorder worldwide
  80% population have LBDs at some time
Multiple sites
  Complex anatomy
    Facet joints, intervertebral discs
    Muscles, tendons, ligaments, fascia
      Irritation, inflammation
      Exacerbation of acute strain
    Nerve involvement
      Root compression
      Referred pain
Difficult precise diagnosis

## Slide 146: NIOSH Lift Equation

## Slide 147: Should not be used for:
One handed lifts
More than 8 hours
Seated or kneeling
Restricted work space
Unstable Objects
Carrying, pushing or pulling while lifting
Wheelbarrows or shovels
High speed motion
Unreasonable foot/floor coupling
Unfavorable environment

## Slide 148
Definition of Terms
RWL = Recommended weight limit
LC = Load constant
HM = Horizontal multiplier
VM = Vertical multiplier
DM = Distance multiplier
AM = Asymmetric multiplier
FM = Frequency multiplier
CM = Coupling multiplier

## Slide 149
1991 Version
RWL = LC x HM x VM x DM x AM x FM x CM
A Discounting Equation
Lift Index = LOAD / RWL

## Slide 150: Snook Tables

## Slide 151: Sources on the Internet
http://www.cdc.gov/niosh/docs/94-110/
http://www.emcins.com/losscontrol/quick_links/employee_safety_health/ergonomicsNIOSH.aspx
http://www.ergoweb.com/news/detail.cfm?id=566
http://www.ccohs.ca/oshanswers/ergonomics/niosh/calculating_rwl.html

## Slide 152: Lifting
Don’t put things on the floor!!
  Put them in the “Box” or “Ball”
Face the object
Move as close as possible to the object CG
Bend hips and knees
Keep back straight
Get a good grip
Don’t twist or jerk, lift smoothly

## Slide 153: Storage Rack Guidelines (North America)

## Slide 154: Manipulation

## Slide 155: Manipulation / Assembly Tasks
Task requirements
  Visual, cognitive and motor
  Repetition
Outcomes
  Product quality and productivity issues due to
  Hand and arm pathology
  Postural strain – shoulder, neck
  Motion strain – shoulder, elbow, wrist, hand, thumb and fingers
Causes (and opportunities for intervention)
  Force, posture, movement, frequency, duration
Measurement
  Hand Activity Level
  Postural analysis
  Micro motion analysis
Interventions
  Remove, reduce or replace non value added work
  Task / Target Design
  Enlarge or rotate to reduce frequency

## Slide 156: Grasping and Manipulating
Fingers have postures too
How big are your hands?
How big should handles be?
How bent should handles be?
Length, Width, Circumference, Shape
Avoid pressure points

## Slide 157: Tight Targets Take Time
Tight Targets Take Time

## Slide 158: Two Automobile Plants
Part Insertion Time
  6.3 secs
  3.9 secs
Target size, orientation ?

## Slide 159: If You Don’t Resolve Ergonomics Problems During Product Design
Added Operators
  $75,000 / year x 2 shifts x 6 years product cycle
  $900,000 per added operator
Added Tools
  0.07 min / tool x $0.75 / min x 2 shifts x 75 jph
  x 8 hours per day x 243 days per year x 6 years
  $92,466 per tool

## Slide 160: Lots of Components

## Slide 161: The customer Required a lower Cowl / forward view

## Slide 162: The assembler had to deal with poorer ACCess and many more components

## Slide 163: A compromise between user styling requirements and design for manufacturability, even robots have a hard time with TIGHT Targets
“Thin is in” for the customer, but what about the assembler?

## Slide 164: Targets and Triangles
A
B
Design for Assembly!
Which Targets are Easier?

## Slide 165: Fitts Law(1954)
MT = a + b log2 (2A/W)
where:
MT = Movement Time
a, b = Individual and Situational Constants
A = Amplitude of Movement
W = Width of Target
2A/W = Index of Difficulty (ID)

## Slide 166: Case Study Barbie Dolls
How long does it take to assemble and pack a set of clothes for a Barbie Doll?
How many assemblies per day?
How many workers are needed?
TARGETS!!!

## Slide 167: Target Rules
Increase Target Size Percentage
  Access, Adjustment, Finesse
Consider Effect of Part Weight
Consider Effect of Part Size
Large time and postural stress savings by targeting the targets

## Slide 168: Simplify Choices Choices Take Time and may be Wrong

## Slide 169: Choices Exercise
Hold a pack of playing cards face down
Sort them into 2 piles
Sort them into 4 piles
Sort them into RED and BLACK
Sort them into H, C, D, S
  Hick’s Law MT = a + b log2n
  where: n = number of choices
Measure the Times, Observe the Errors and Hesitations

## Slide 170: Design for Manufacturing Target the Targets Reduce the choices

## Slide 171: Small Components Assembly

## Slide 172: Arms, Wrists and Fingers have Postures too
Orient the part
Bend the tool not the wrist
Increase the size of the handle to reduce pressure and force requirements and increase leverage

## Slide 173: Orient the job

## Slide 174: Use the right Handle

## Slide 178: Operations Design
The key to productivity is the removal of non value added work
  Long or frequent transfers
  Search for components or target
  Reorienting the component / product
Use belts / gravity for transfers, components
Place tools / components in the operations sequence
Use belt / gravity for finished goods

## Slide 179: Job Design
Taylorism
  Job simplification
  Managers manage workers work
But workers are able to master many tasks
Workers do have insight into quality, productivity and health and safety issues
Workers do not like to be bored
  Vigilance decrement may be a problem
  Local and general fatigue will be a problem
Therefore design job variety

## Slide 180: Shift Work
Avoid one week rotations
Implement permanent shifts
Implement short cycle shift schedules
  2 – 3 days
  Use forward rotation: Day – Evening – Night – Off
Limit shift durations
  8 is better than 10 and 12 is the limit
  4 crew 3 shift or 3 crew 2 shift arrangements
Provide one long and many short relief breaks for assembly work
  Walking for at least 5 minutes every hour

## Slide 181: Physical Work Stress Index (PWSI) Addressing the TIME Dimension

## Slide 182: Physical Stress and Strain People respond well to optimal levels of physical (and cognitive) variety
Strain
Static Workload
Dynamic Workload

## Slide 183: History
The PWSI was first developed as a student project at the University of Hong Kong in 1976 (Brian Peacock, Janet Liu)
It was further developed at the University of Oklahoma through undergraduate and graduate projects during the early 1980s (Susan Cheatwood, Jacob Chen)
A description of the process was published by Chen, Peacock, and Schlegel in 1989 in the International Journal of Industrial Ergonomics

## Slide 184: Activity Sampling
A random or regular sampling scheme is developed depending on the periodicity of the work activity.
  For regular, machine paced work, a random sample is recommended.
  For irregular work, a regular sampling process is both convenient and valid.
The ordinal mappings from values of each of these major elements are recorded at each sampling instant
Generally it is appropriate to gather data from about 10 samples but greater precision can be achieved by increasing the number of observations

## Slide 185: Ordinal Values
0 1 2 3
Location Distance from Primary Workplace
< 5 m 5 - 10 m 10 - 50m > 50 m
Postural Base Lying Sitting Leaning Standing
Orientation Forward R/L Side Backward Under
L Hand Position In Box Edge Outside Outside Box of Box Box in Two Planes
R Hand Position In Box Edge Outside Outside Box of Box Box in Two Planes
External Load Light Medium Heavy Very Heavy
0 - 1 lb 1 - 10 lb 10 - 25 lb > 25 lb
Thermal Load Comfortable Warm Hot Very Hot
65 - 75 75 - 85 85 - 95 >95

## Slide 186: Base Posture
The range of base postures considered include lying, sitting, leaning (sit-stand) and standing
Maintaining anyone of these postures all day is undesirable - a high static load.
Constantly changing base posture as in changing from sitting to standing too frequently would indicate a high dynamic workload.

## Slide 187: The Box or the Ball Work (hand) placement for most of the time
Shoulder Height
5th Percentile
Arm Length
5th Percentile
Elbow Height
50th Percentile
Hand Height
95th Percentile
Arm Length
5th Percentile
Elbow Width
95th Percentile
Sitting
High Sitting
Leaning
Standing

## Slide 188: Physical Workload
The absolute physical workload of a task may be estimated by averaging the within element scores and then producing a profile of the task.

## Slide 190: Static and Dynamic Workload Balance
Large differences in the ordinal values of the selected variables between sampling instants reflect a highly dynamic physical workload.
No change between successive time observations reflects a high static physical workload.
Summing (and then averaging) the changes over successive sampling intervals gives an indication of the overall static / dynamic workload balance for each of the elements.

## Slide 192: The Best Posture is the Next Posture

## Slide 193: Walkie-Talkies
Require all employees to walk and talk every hour for 5 minutes
  Walking provides physical relief
  Talking provides social relief
  Walking and talking provide attention relief
  Productivity will not suffer

## Slide 194: Stretching
Systematically and slowly move every joint through its full range
  Move, hold for 3 seconds, relax
Standing (hold on to the back of the chair)
  Move knee up then push leg back
  Move leg across the body, away from the body and in big circles
Sitting
  Bend forward, back, side to side, and twist
  Move shoulders and shoulder girdles in big circles
  Move wrist and hands through full range
  https://itunes.apple.com/sg/app/ergo-work/id556877197?mt=8

## Slide 195: Workability Index

## Slide 196: Workability Index
Date |  |  |  |  |  |  |  |  |  |  | Job Description | 
Analyst |  |  |  |  |  |  |  |  |  |  |  | 
Survey Reference / Times |  |  |  |  |  |  |  |  |  |  |  | 
Job Survey Ratings |  |  |  |  |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
 | Place a small "x" in the appropriate rating cell | N/A | Green |  | Yellow |  | Orange |  | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria

## Slide 197
Policy Decisions
Engineering Variable or Composite Index
Common Currency
Outcome Scale
7
6
5
4
3
2
1
Unacceptable
Range
Ideal Range
Region of Interactions and Continuous Improvement
Policy Statements
1
2
3
4
6
5
7

## Slide 198
Design Rules - Consensus
Policy
Science
History
Experience
Evaluation
  Verification
  Validation
  Sensitivity
Predictions
Design
Rule
Rule
Implementation
Data
Consensus:
  HF Experts
  Engineers
  Managers
  Customers
Technical
Memory

## Slide 199: Workability Index
Addresses
  Spatial factors
  Manual materials handling
  Manipulation
  Environmental factors
  Information factors
  Operational factors

## Slide 200: Spatial Factors
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Access |  |  |  |  |  |  |  | Clearances, obstructions, doors, barriers
Fit |  |  |  |  |  |  |  | Head room, Knee / Foot room, Width
Reach |  |  |  |  |  |  |  | Box, 50 cm reach curves
Postures |  |  |  |  |  |  |  | Sitting, Standing, Squatting, Middle, Outer, Inner ranges
Movements |  |  |  |  |  |  |  | Range, speed
Task surface orientation |  |  |  |  |  |  |  | Front, above, below, behind
Ramps |  |  |  |  |  |  |  | Slope, length
Stairs |  |  |  |  |  |  |  | Number, height
Counts |  |  |  |  |  |  |  | Refer to HF Specialist, manufacturing engineer for interventions

## Slide 201: Manual Materials Handling
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Lifting |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Carrying |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Holding |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Pulling |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Pushing |  |  |  |  |  |  |  | Weights, forces, coupling, sizes
Twisting, bending |  |  |  |  |  |  |  | Vertical and horizontal task locations
Interfaces, coupling |  |  |  |  |  |  |  | Good, sharp
Counts |  |  |  |  |  |  |  | Refer to NIOSH Lifting Equation and Snook Tables

## Slide 202: Manipulation
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Shoulder, Elbow |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces
Hand, Wrist, Fingers |  |  |  |  |  |  |  | Mid, Outer, Inner ranges, forces, coupling, interfaces
Targets |  |  |  |  |  |  |  | Target sizes and tolerances
Precision |  |  |  |  |  |  |  | Fine, coarse
Counts |  |  |  |  |  |  |  | Use Hand activity level TLVs

## Slide 203: Environmental Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Heat, Cold |  |  |  |  |  |  |  | Air Temperature, Humidity, Radiant heat, Air movement
Glare |  |  |  |  |  |  |  | Location, intensity, contrast, window and local lighting
Dark |  |  |  |  |  |  |  | Interference with visual demands
Noise Intensity |  |  |  |  |  |  |  | Task, Ambient, Sound Level, Frequency, Variability
Vibration |  |  |  |  |  |  |  | Whole body, hand arm
Accelerations |  |  |  |  |  |  |  | Pounding, jerks
Slip, trip, fall |  |  |  |  |  |  |  | Work context hazards, visibility, barriers
Chemical |  |  |  |  |  |  |  | Refer to OH
Radiation |  |  |  |  |  |  |  | Refer to OH
Counts |  |  |  |  |  |  |  | Refer to OH, Safety or Engineering for intervention

## Slide 204: Information Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Visual |  |  |  |  |  |  |  | Visual acuity, discrimination demands, importance
Acoustic |  |  |  |  |  |  |  | Hearing acuity, discrimination demands, importance
Attentional |  |  |  |  |  |  |  | Sustained and divided attention demands
Memory |  |  |  |  |  |  |  | Operational memory span, interferences
Cognitive |  |  |  |  |  |  |  | Calculations, planning, analyses
Decisions |  |  |  |  |  |  |  | Number of choices, ambiguity, risk
Communication |  |  |  |  |  |  |  | Frequency, variability, importance
Control |  |  |  |  |  |  |  | Precision, feedback, prediction
Situation awareness |  |  |  |  |  |  |  | Importance, distractions
Mental workload |  |  |  |  |  |  |  | Information and time demands, training, stress
Outcomes |  |  |  |  |  |  |  | Consequences of human error
Counts |  |  |  |  |  |  |  | Refer to HF specialist for intervention

## Slide 205: Operational Factors
 |  |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
Place a small "x" in the appropriate rating cell | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
 |  |  |  |  |  |  | Operational factors will usually interact with some or all of the other factors | Intervention through administrative and / or operational controls
Job cycle duration |  |  |  |  |  | Engineering issues |  | Operations per hour, job cycle time
Static posture duration |  |  |  |  |  |  |  | % job cycle, % day
Repetitions, frequencies |  |  |  |  |  |  |  | Frequency per hour of same or similar task
Job pacing |  |  |  |  |  |  |  | Self paced, Piece Rate, Machine paced, Supervisor
Span of responsibility |  |  |  |  |  | Operational Issues |  | Product quality, other colleagues, autonomy
Team structures |  |  |  |  |  |  |  | Job rotations
Participatory processes |  |  |  |  |  |  |  | Do employees participate in work design decisions
Technical support |  |  |  |  |  |  |  | Availability, supervision
Training, Acclimatization |  |  |  |  |  |  |  | Level of experience, adaptation to task
Special Populations |  |  |  |  |  |  |  | Are eldely or disabled persons employed with accommodations?
Counts |  |  |  |  |  |  |  | Refer to HF Specialist / Management for intervention

## Slide 206: Overall Counts
 |  |  | Job Survey Ratings |  |  |  |  |  | Orange and Red ratings may warrant in depth or specialist investigation regarding importance and feasibility of redesign / intervention | Where feasible all red ratings must be addressed / changed by engineering controls. Orange ratings should be addressed by engineering or administrative controls to reduce exposure
 | Place a small "x" in the appropriate rating cell |  | N/A | Green | Yellow | Orange | Red | Operational Factor Interactions H/M/L | Descriptions / Quantifications / Comments / Justifications | Notes / Guidelines / Criteria
Overall Counts 1 |  |  |  |  |  |  |  |  | Notes | Engineering Controls
 |  | 2 |  |  |  |  |  |  | Jobs should be analysed before and after interventions | 
 |  | 3 |  |  |  |  |  |  | The worksheet may also be used repeatedly over a day to analyse the variability of work demands | Administrative Controls
 |  | 4 |  |  |  |  |  |  | Consensus quantitative anchors may be added to the rating scales to improve their consitency | 
 |  | 5 |  |  |  |  |  |  | Basic training (1 day) in the use of this worksheet should be required of all ergonomics monitors (CEM Level 1) | 

## Slide 207: Singapore MOM ergo@work app
Postures, stretches, breaks

## Slide 209: Conclusions – How Ergonomics Works

## Slide 210: Ergonomics Addresses
human, technological, contextual and operational complexity and variability
tradeoffs among many job outcomes
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E
Physical
Cognitive
Social
Affective
Context
Temporal
Sensory
E
P
B
E4S4
Macro
+
Micro

## Slide 211: The Design Cycle
The Process,
Job, Task,
Transaction
or Simulation
Uncontrollable
Conditions / Context
Specifications
Design
Equipment
Context
Humans
Operations
Guidelines
and
Constraints
Decisions
Policy
Money
Analysis
Requirements
Outcomes
Analysis
Analysis
Tools
Analyses
6U
2M
E4S4
Prediction
Integration
Interfaces
Interactions
Intra actions Interferences
Interdependencies
Rules and Regulations
S
Technology
H
People
L
Context
(Environment)
E